## Slide 1: Multilayer Machine Learning-Assisted Optimization-Based Robust Design and Its Applications to Antennas and Arrays

## Slide 2: Abstract
An efficient multilayer machine learning-assisted optimization (ML-MLAO)-based robust design method is proposed for antenna and array applications. Machine learning methods are introduced into multiple layers of the robust design process, including worst-case analysis (WCA), maximum input tolerance hypervolume (MITH) searching, and robust optimization, considerably accelerating the whole robust design process. First, based on a surrogate model mapping between the design parameters and performance, the WCA is performed using a genetic algorithm to ensure reliability. MITH searching is then carried out using an MLAO-based framework to find the MITH of the given design point.

## Slide 3
Next, based on the training set obtained using MITH searching, correlations between the design parameters and the MITH are learned. The robust design is carried out using surrogate models for both the performance and the MITH, and these models are updated online following the ML-MLAO scheme. Finally, two examples, including an array synthesis problem and an antenna design problem, are used to verify the proposed ML-MLAO method. The numerical results and computation time are discussed to demonstrate the effectiveness of the proposed method.

## Slide 4: Existing System
This review aims to provide an overview of the existing optimization and numerical methods and tools, which can enhance the robust multiobjective optimization procedures, where the emphasis is placed on finding a robust frontier for electrical machine design related problems .
The second part of the paper highlights the role and possibilities of the robust design optimization based tools in the case of some recent technologies, 3D printed and superconductor based machines, and the role of robust design optimization in the development of electric vehicles and digital twin based modeling.

## Slide 5: Disadvantage of Existing System
In contrast to the array synthesis problem discussed above, the solution of the antenna design problem relies on the prediction accuracy of the surrogate models trained with the datasets established by full-wave EM simulations.
For antennas with a large design parameter range, acquiring accurate surrogate models for the entire design space is difficult if time is limited. Therefore, local surrogate models surrounding the possible optimal design points should be established and updated online during the robust design process rather than surrogate models suitable for the entire design space.
The robust antenna design algorithm is divided into two phases: the optimization phase and the robust optimization phase.

## Slide 6: PROPOSED SYSTEM :
They proposed to start the calculation with a relatively small sample size and increase the number of individuals with the number of generations.
Other adaptation methodologies can use a higher sample size for those individuals that have a higher estimated variance or simply calculate the fitness by averaging over the neighborhood of the evaluated individuals.
Another possibility to reduce the noise is implicit averaging because the area of a possible solution is sampled repeatedly, and this information can be used for an implicit averaging

## Slide 7: ADVANTAGE
The predicted optimization results of the MITHs are verified using the proposed DL-MLAO method, and the predicted antenna performance is verified using EM simulations.
The termination criterion, such as the maximum number of iterations iML or the maximum number of unchanged iterations, is then checked.
If one of the termination conditions is met, the process is stopped; otherwise, the database is updated, and Step 4 is repeated.
The ML-MLAO method uses the MITH search strategy as the HF simulation procedure in the MLAO scheme.
The accuracy and robustness of the results are ensured by the accuracy of DL-MLAO MITH searching.

## Slide 8
TITTLE | AUTHOR | DESCRIPTION
Introducing robustness in multi-objective optimization | K. Deb and H. Gupta, | In optimization studies including multi-objective optimization, the main focus is placed on finding the global optimum or global Pareto-optimal solutions, representing the best possible objective values.
Efficient multiobjective antenna optimization with tolerance analysis through the use of surrogate models | J. A. Easum, J. Nagar, P. L. Werner, and D. H. Werner, | To demonstrate the effectiveness of this approach, it will be applied to the optimization of a capacitively loaded monopole and a wideband Vivaldi antenna.

## Slide 9
TITTLE | AUTHOR | DESCRIPTION
Reliability-aware optimization of a wideband antenna | A. Kouassi, N. Nguyen-Trong, T. Kaufmann, S. Lallech ´ ere, P. Bonnet, ` and C. Fumeaux, | A framework for optimization of wideband antennas including statistical reliability considerations is proposed.
Robust optimization with worst case sensitivity analysis applied to array synthesis and antenna designs | B. Zhang and Y. Rahmat-Samii, | This paper incorporates WCSA with optimization to offer a method which not only finds the optimized design, but also ensures 100% feasibility of the optimized design under the certain tolerance criteria

## Slide 10: Block Diagram

## Slide 11: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 12: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 13: CONCLUTION
An ML-MLAO method has been proposed to achieve reliable and efficient robust design for antenna and array applications. By introducing MLAO algorithms to different layers of the robust design process, rapid and trustworthy WCA, MITH searching and robust optimization have been achieved. The heavy computational loads for global searching, EM simulation and tolerance analysis have been greatly reduced by exploiting prior knowledge regarding the correlations between the antenna parameters and responses, WCP and MITH. This increased efficiency has been utilized to make predictions in different design layers, largely accelerating the whole robust design process. Moreover, the surrogate models for the aforementioned design objectives are updated online following the MLMLAO algorithm. Examples including array synthesis and antenna design have been described to verify the efficiency and reliability of the proposed method.

## Slide 14: REFERENCE
[1] K. Deb and H. Gupta, “Introducing robustness in multi-objective optimization,” Evol. Comput., vol. 14, no. 4, pp. 463–494, 2006.
[2] J. A. Easum, J. Nagar, P. L. Werner, and D. H. Werner, “Efficient multiobjective antenna optimization with tolerance analysis through the use of surrogate models,” IEEE Trans. Antennas Propag., vol. 66, no. 12, pp. 6706–6715, 2018.
[3] A. Kouassi, N. Nguyen-Trong, T. Kaufmann, S. Lallech ´ ere, P. Bonnet, ` and C. Fumeaux, “Reliability-aware optimization of a wideband antenna,” IEEE Trans. Antennas Propag., vol. 64, no. 2, pp. 450–460, 2015.
[4] B. Zhang and Y. Rahmat-Samii, “Robust optimization with worst case sensitivity analysis applied to array synthesis and antenna designs,” IEEE Trans. Antennas Propag., vol. 66, no. 1, pp. 160–171, 2018.
[5] C. Hu, S. Zeng, Y. Jiang, J. Sun, Y. Sun, and S. Gao, “A robust technique without additional computational cost in evolutionary antenna optimization,” IEEE Trans. Antennas Propag., vol. 67, no. 4, pp. 2252– 2259, 2019.

## Slide 15
[6] J. Lee, Y. Lee, and H. Kim, “Decision of error tolerance in array element by the monte carlo method,” IEEE Trans. Antennas Propag., vol. 53, no. 4, pp. 1325–1331, 2005.
[7] B. Xia, Z. Ren, and C.-S. Koh, “Utilizing kriging surrogate models for multi-objective robust optimization of electromagnetic devices,” IEEE Trans. Magn., vol. 50, no. 2, pp. 693–696, 2014.
[8] H. Schjaer-Jacobsen and K. Madsen, “Algorithms for worst-case tolerance optimization,” IEEE Trans. Circuits Syst., vol. 26, no. 9, pp. 775–783, 1979.
[9] B. Liu, H. Aliakbarian, Z. Ma, G. A. Vandenbosch, G. Gielen, and P. Excell, “An efficient method for antenna design optimization based on evolutionary computation and machine learning techniques,” IEEE Trans. Antennas Propag., vol. 62, no. 1, pp. 7–18, 2014.
[10] J. P. Jacobs and S. Koziel, “Two-stage framework for efficient gaussian process modeling of antenna input characteristics,” IEEE Trans. Antennas Propag., vol. 62, no. 2, pp. 706–713, 2014.