## Slide 1: An Efficient Eigenvalue Tracking Method for Time-Delayed Power Systems based on Continuation of Invariant Subspaces

## Slide 2: Abstract
Time delays are inevitable in the power systems with wide-area control signals, which may compromise the control performance and thus jeopardize the stability of the power systems. To analyze the impacts of system parameters on critical oscillation modes of a time-delayed power system (TDPS), a new method for eigenvalue trajectory tracking of TDPS is proposed in this paper based on the continuation theory of invariant subspaces. When small changes are imposed on system parameters, such as parameters of wide-area damping controllers (WADCs) and time delays, the invariant subspaces are continuously predicted and corrected, followed by the eigenvalues and eigenvectors.

## Slide 3
In the process, the predictor and corrector are computed by solving linear equations sparsely and in blocks, which is highly scalable and computationally efficient for large-scale power system applications. The 16-generator 68-bus test system and two real-world power grids in China are used to test and demonstrate the proposed method. The results show that the proposed method can accurately and efficiently track eigenvalue trajectories for TDPS, especially for large-scale power grids. In addition, the sensitivities of eigenvalues and eigenvectors with respect to WADCs’ parameters and time delays are obtained as by-products of the approach.

## Slide 4: Existing System
The transcription of the Kronecker sum into the matrix pencil form reduces the problem to the existence of the unit circle of generalized eigenvalues of the corresponding matrix pencil.
The proposed method offered larger delay margin and takes less computation time compared to some existing methods.
Frequency-based DIS methods are generally built on the verification of the non-existence of purely imaginary system poles for arbitrary delay values.
Then, the non-existence of any positive real root of D (ω) - which is a sufficient DIS condition - was proved by the Déscartes rules of signs.

## Slide 5: Disadvantage of Existing System
In continuation methods, the predictor-corrector scheme has been widely applied in power systems, such as continuation power flow.
Its principle is to predict the next solution point and then correct the prediction to get the next point on the curve.
The eigenvalue tracking problem addressed in this paper is not an exception.
This is a challenging problem since the frequencies, damping ratios and their mode shapes may change greatly or jump as WADCs’ parameters change.

## Slide 6: PROPOSED SYSTEM :
The proposed direct method provides the central manifold approximation for lossless propagation model without the use of the central manifold theorem and the structure reconstruction.
It was utilized to investigate the local asymptotic stability of the positive equilibrium for the n-dimensional Lotka-Volterra system and to compute the rightmost characteristic roots (poles), respectively.
The applicability of the method was also improved by the introduction of a new class of TDSs and the corresponding transformation into the proposed common canonical form.

## Slide 7: ADVANTAGE
Previous weakly damped blackouts and increased power system congestion have prompted new techniques to improve the damping of these oscillation modes.
By introducing remote signals with global observability and controllability for interarea oscillation modes, wide-area damping controllers (WADCs) can provide additional damping to effectively improve the weakly damped modes and achieve system-level control.
However, the remote signals can bring inevitable time delays into the widearea closed loop, which may deteriorate WADC performance and even threaten the stability of power systems

## Slide 8
TITTLE | AUTHOR | DESCRIPTION
Design of the Pacific DC intertie wide area damping controller | B. J. Pierre, F. Wilches-Bernal, D. A. Schoenwald, R. T. Elliott, D. J. Trudnowski, R. H. Byrne, and J. C. Neely, | The control system utilizes real-time phasor measurement unit (PMU) feedback to construct a commanded power signal which is added to the scheduled power flow for the PDCI.
Model validation for the August 10, 1996 WSCC system outage | D. N. Kosterev, C. W. Taylor, and W. A. Mittelstadt, | In this paper, the authors describe the simulation of this disturbance using a transient stability program.

## Slide 9
TITTLE | AUTHOR | DESCRIPTION
Optimal PMU placement for power system dynamic state estimation by using empirical observability Gramian | J. Qi, K. Sun, and W. Kang, | The implementation, validation, and the robustness to load fluctuations and contingencies of the proposed method are carefully discussed.
Measurement and modeling of delays in wide-area closed-loop control systems | F. Zhang, Y. Sun, L. Cheng, X. Li, J. H. Chow, and W. Zhao, | This paper aims to study the measurement and modeling methods for delays in wide-area closed-loop control systems (WACS).

## Slide 10: Block Diagram

## Slide 11: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 12: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 13: CONCLUTION
The continuation of invariant subspaces is extended to TDPS and is utilized for accurately tracking eigenvalue trajectories. The proposed method can handle eigenvalues from both forms of DDEs and DDAEs. The method has the following features: 1) When WADCs’ parameters or time delays change, the trajectories of critical eigenvalue can be accurately tracked by the proposed method, which facilitates the follow-up SSSA and WADC design for TDPS. 2) Sensitivities of eigenvalues and eigenvectors to WADCs’ parameters and time delays are obtained as by-products, which can be used to guide tuning of controller parameters and determine the directions of eigenvalue trajectories. 3) By fully utilizing the sparsity of system augmented state matrices, the linear equations are solved by the proposed block and sparse implementation, which highlights the scalability and computation efficiency. 4) In the tested real-world power grids, the efficiency can be improved more than 74% by the proposed method than the existing methods. As system size increases, advantage in computation speed becomes more apparent.

## Slide 14: REFERENCE
[1] B. J. Pierre, F. Wilches-Bernal, D. A. Schoenwald, R. T. Elliott, D. J. Trudnowski, R. H. Byrne, and J. C. Neely, “Design of the Pacific DC intertie wide area damping controller,” IEEE Trans. Power Syst., vol. 34, no. 5, pp. 3594–3604, Sep. 2019.
[2] D. N. Kosterev, C. W. Taylor, and W. A. Mittelstadt, “Model validation for the August 10, 1996 WSCC system outage,” IEEE Trans. Power Syst., vol. 14, no. 3, pp. 967–979, Aug. 1999.
[3] J. Qi, K. Sun, and W. Kang, “Optimal PMU placement for power system dynamic state estimation by using empirical observability Gramian,” IEEE Trans. Power Syst., vol. 30, no. 4, pp. 2041–2054, Jul. 2015.
[4] F. Zhang, Y. Sun, L. Cheng, X. Li, J. H. Chow, and W. Zhao, “Measurement and modeling of delays in wide-area closed-loop control systems,” IEEE Trans. Power Syst., vol. 30, no. 5, pp. 2426–2433, Sep. 2015.
[5] Y. Shen, W. Yao, J. Wen, H. He, and W. Chen, “Adaptive supplementary damping control of VSC-HVDC for interarea oscillation using GrHDP,” IEEE Trans. Power Syst., vol. 33, no. 2, pp. 1777–1789, Mar. 2018

## Slide 15
[6] H. Ye, Q. Mou, and Y. Liu, “Calculation of critical oscillation modes for large delayed cyber-physical power system using pseudo-spectral discretization of solution operator,” IEEE Trans. Power Syst., vol. 32, no. 6, pp. 4464–4476, Nov. 2017.
[7] C. Li, G. Li, C. Wang, and Z. Du, “Eigenvalue sensitivity and eigenvalue tracing of power systems with inclusion of time delays,” IEEE Trans. Power Syst., vol. 33, no. 4, pp. 3711–3719, Jul. 2018.
[8] Q. Mou, H. Ye, and Y. Liu, “Nonsmooth optimization-based WADC tuning in large delayed cyber-physical power system by interarea mode tracking and gradient sampling,” IEEE Trans. Power Syst., vol. 34, no. 1, pp. 668–679, Dec. 2019.
[9] D. Yang and V. Ajjarapu, “Critical eigenvalues tracing for power system analysis via continuation of invariant subspaces and projected Arnoldi method,” IEEE Trans. Power Syst., vol. 22, no. 1, pp. 324–332, Feb. 2007.
[10] J. Rommes and N. Martins, “Computing large-scale system eigenvalues most sensitive to parameter changes, with applications to power system small-signal stability,” IEEE Trans. Power Syst., vol. 23, no. 2, pp. 434– 442, May 2008.