## Slide 1: Fast Power System Event Identification using Enhanced LSTM Network with Renewable Energy Integration

## Slide 2: Abstract
Accurate and fast event identification in power systems is critical for taking timely controls to avoid instability. In this paper, a synchrophasor measurementbased fast and robust event identification method is proposed considering different penetration levels of renewable energy. A difference Teager-Kaiser energy operator (dTKEO)-based algorithm is first proposed to improve multiple-events detection accuracy. Then, feature extractions via the integrated additive angular margin (AAM) loss and the long short-term memory (LSTM) network are developed. This allows us to deal with intraclass similarity and inter-class variance of events when high penetration renewable energy occurs. With the extracted features, a multi-stage weighted summing (MSWS) lossbased criterion is developed for adaptive data window determination and fast event pre-classification. Finally, the re-identification model based on feature similarity is established to identify unknown events, a challenge for existing machine learning algorithms. Simulation results on the IEEE 39-bus, Kundur 2-area, and an actual large-scale power grid system are used to demonstrate the advantages of the proposed method over others.

## Slide 3: Existing System
Although onshore wind turbines have reached maturity due to the sooner evolution and, currently, most of the existing wind farms are onshore, offshore harvesting has drawn attention in the past years as well due to its desirable features.
Forecasting models based on deep learning are able to overcome the barriers and limitations of the existing statistical forecasting models, which are mostly formulated as a linear model in dealing with longer forecasting time horizons.
Among other existing FCs, Proton Exchange Membrane Fuel Cell (PEMFC), Direct Methanol Fuel Cell (DMFC), Alkaline Fuel Cells (AFC), and Solid Oxide Fuel Cells (SOFC) are the most known ones.

## Slide 4: Disadvantage of Existing System
To handle the intra-class similarity caused by DERs integration, the diffusion kernel density estimation (DKDE) and a deep neural network (DNN) are combined .
However, it does not handle the intra-class similarity issue with the increased penetration of DERs.
Furthermore, existing algorithms do not address unknown events.It is worth noting that this paper mainly focuses on the large disturbance events detection and identification, such as faults, generation loss, or load switch-off/on, etc. The remainder of this paper is organized as follows shows the problem formulations.

## Slide 5: PROPOSED SYSTEM :
In , a wind power trading model, including a regulation strategy, is proposed for the day-ahead California electricity market.
Moreover, a state-space dynamic model is proposed in for PV systems with full ancillary services support.
In , a reactive power regulation method is suggested to provide ancillary services by PV inverters using three-phase control strategies.
The authors of proposed a new Repeated Wavelet Transform (WT) based Auto Regressive Integrated Moving Average (ARIMA) (WT-ARIMA) model to predict the wind speed on very short time intervals.

## Slide 6: ADVANTAGE
A residual CNN is proposed in which improves the network training convergence speed and detection accuracy.
In , maximum overlap discrete wavelet transform and stacked sparse denoising autoencoder are combined to improve the anti-noise performance in disturbance detection.
However, the Softmax loss only learns separable features that are not sufficiently discriminative, which may result in poor performance for some cases, such as the events with only slight differences.
The overall accuracy of the test data is 97.99%, which indicates that the proposed method achieves good performances for event identification with renewable energy integrations

## Slide 7
TITTLE | AUTHOR | DESCRIPTION
Distributed formal analysis for power networks with deep integration of distributed energy resources | Y. Li, P. Zhang, M. Althoff and M. Yue, | Therefore, DFA provides an invaluable tool for designing and operating the interconnected power networks of the future, which will feature the deep integration of DERs.
Power system frequency monitoring network (FNET) implementation | Z. Zhong, et al., | This paper summarizes the implementation of the FNET system and shows some preliminary observations and analyses of the data that have been collected from the FNET.

## Slide 8
TITTLE | AUTHOR | DESCRIPTION
A new approach to power system disturbance assessment using wide area post disturbance records | M. K. Jena, B. K. Panigrahi, and S. R. Samantaray, | This paper presents an empirical wavelet transform (EWT) based approach to perform postmortem analysis of wide-area measurement (WAM) based signals.
Real-time identification of dynamic events in power systems using PMU data, and potential applications—models, promises, and challenges | S. Brahma, R. Kavasseri, H. Cao, N. R. Chaudhuri, T. Alexopoulos and Y. Cui, | Potential applications of the task to improve security of power system protection and anomaly detection in the case of a cyberattack are conceptualized.

## Slide 9: Block Diagram

## Slide 10: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 11: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 12: CONCLUTION
This paper presents a fast and robust method for event detection and identification with different levels of renewable energy penetrations. It leverages the PMU data as well as enhanced dTKEO for multiple event detection while developing an enhanced integrated LSTM model for event identification. In particular, the AAM loss is used together with LSTM for better feature extractions, including the intra-class similarity and interclass variance of events when high penetration renewable energy occurs. To enable a fast event identification, the MSWS loss is embedded into the LSTM model and this also provides the adaptive data window. The existing machine learning algorithms could not deal with the unknown events, a challenge that must be solved in today’s more and more complicated grid. With the developed re-identification model based on feature similarity, we can achieve very high identification accuracy under different renewable energy penetrations. Comparisons results with many other machine learning algorithms on the IEEE 39-bus system demonstrate that the proposed method has both high event detection and identification accuracies while being robust to varying renewable integration scenarios. Results on the Kundur 2-area test system and an actual large-scale power system in China demonstrate further generalizability of the proposed method.

## Slide 13: REFERENCE
[1] Y. Li, P. Zhang, M. Althoff and M. Yue, "Distributed formal analysis for power networks with deep integration of distributed energy resources," IEEE Trans. Power Systems, vol. 34, no. 6, pp. 5147-5156, Nov. 2019.
[2] Z. Zhong, et al., ‘‘Power system frequency monitoring network (FNET) implementation,’’ IEEE Trans. Power Systems, vol. 20, no. 4, pp. 1914–1921, Nov. 2005.
[3] M. K. Jena, B. K. Panigrahi, and S. R. Samantaray, “A new approach to power system disturbance assessment using wide area post disturbance records,” IEEE Trans. Industrial Informatics, vol. 14, no. 3, pp. 1253–1261, Mar. 2017.
[4] S. Brahma, R. Kavasseri, H. Cao, N. R. Chaudhuri, T. Alexopoulos and Y. Cui, "Real-time identification of dynamic events in power systems using PMU data, and potential applications—models, promises, and challenges," IEEE Trans. Power Delivery, vol. 32, no. 1, pp. 294-301, Feb. 2017.
[5] R. Yadav, A. K. Pradhan and I. Kamwa, "Real-time multiple event detection and classification in power system using signal energy transformations," IEEE Trans. Industrial Informatics, vol. 15, no. 3, pp. 1521-1531, March 2019

## Slide 14
[6] H. Su and T. Liu, "Enhanced-online-random-forest model for static voltage stability assessment using wide area measurements," IEEE Trans. Power Systems, vol. 33, no. 6, pp. 6696-6704, Nov. 2018.
[7] S. S. Negi, N. Kishor, K. Uhlen and R. Negi, "Event detection and its signal characterization in PMU data stream," IEEE Trans. Industrial Informatics, vol. 13, no. 6, pp. 3108-3118, Dec. 2017.
[8] M. Biswal, S. M. Brahma and H. Cao, "Supervisory protection and automated event diagnosis using PMU data," IEEE Trans. Power Delivery, vol. 31, no. 4, pp. 1855-1863, Aug. 2016.
[9] Y. Song, W. Wang, Z. Zhang, H. Qi and Y. Liu, "Multiple event detection and recognition for large-scale power systems through cluster-based sparse coding," IEEE Trans. Power Systems, vol. 32, no. 6, pp. 4199-4210, Nov. 2017.
[10] R. Yadav, S. Raj, A. K. Pradhan, "Real-time event classification in power system with renewables using kernel density estimation and deep neural network," IEEE Trans. Smart Grid, vol. 10, no. 6, pp. 6849-6859, Nov. 2019.