## Slide 1: On the Impact of Discrete Secondary Controllers on Power System Dynamics

## Slide 2: Abstract
This paper discusses the impact of discrete secondary controllers on the dynamic response of power systems. The idea of the paper originates from the observation that there is a range of values, from few tens of seconds to few minutes, of the execution cycles of conventional automatic generation control (AGC) that leads to a limit cycle. Below and above this range the system is stable. This is certainly not a problem in practice as the AGC updates the power set points of generating units every few seconds. However, this phenomenon has interesting consequences if one considers real-time electricity markets with short dispatch periods (i.e., 5 minutes) as these markets can be modeled as a sort of AGC. The paper first provides a formal analogy between conventional AGC and real-time electricity markets. Then it shows that the discretization-driven instability exists if the system includes a real-time electricity market modeled as secondary frequency controller. Finally, the paper discusses the impact of the combined effect of high wind generation shares and discrete secondary controllers on power system dynamics.

## Slide 3: Existing System
Phasor Measurement Unit is based upon the synchrophasor measurement from the existing power systems. Synchrophasors are the expression of mathematical method by the phasor values of the sinusoidal waveforms in power system. The measurement derived from the synchrophasor is called synchronized measurement.
Small signal stability problems exist in power system for many decades. The system oscillates with undamped or growing phenomenon because of lacking of damping or synchronism.
Electromechanical oscillation in power system is studied in the area of rotor angle stability problem, the oscillation exists because of the behavior that the synchronous generators' power outputs are related to the variation of rotor angles.

## Slide 4: Disadvantage of Existing System
This is certainly not a problem in practice as the AGC updates the power set points of generating units every few seconds.
Moreover, it is shown that the only effective solution to remove this issue is to keep as short as possible the AGC execution cycles.
This is not a major constraint as, in practice, the AGC installed in the control centers of TSOs uses execution cycles that vary in the range of 2 to 6 s, which do not create instability issues.
Moreover, and consider time periods up to a maximum of 14 seconds, which, as shown in this paper, are hardly an issue for secondary controllers.

## Slide 5: PROPOSED SYSTEM :
The generalization is motivated by the multitude of various representations of saturation that have appeared in the literature.
Virtually all methods proposed to date involve the addition of one or more nonlinear terms to the model of (3.148)–(3.159).
The notations and conventions used in this text are as standard as possible given the proliferation of models. It basically follows that of .
Second, it is important to repeat that standard symbols have been defined through the model proposed in this text with a few noted exceptions.

## Slide 6: ADVANTAGE
The scenarios with non-synchronous devices, i.e., the scenarios with inclusion of wind generation, worsen the performance of both AGC/MAGC controllers, and consequently the dynamic performance of the system.
Regarding the differences with respect to the participation of WPPs in real-time electricity markets, the case study shows that this participation does not necessarily mean an improvement in the dynamic performance of the system.
That integrating more wind power generation into power systems worsen the performance of both AGC controllers, and consequently the power system dynamic performance. Simulation results show that power systems that are based on real-time electricity markets should use shorter dispatch periods compared to the case without wind power

## Slide 7
TITTLE | AUTHOR | DESCRIPTION
Foundations ˇ and challenges of low-inertia systems (invited paper) | F. Milano, F. Dorfler, G. Hug, D. J. Hill, and G. Verbi ¨ c, | In this article, we review the challenges of such low-inertia power systems, and survey the solutions that have been put forward thus far.
Automatic generation control and its implementation in real time | D. Apostolopoulou, P. W. Sauer, and A. D. Dom´ınguez-Garcia, | The proposed methodology is illustrated in the WECC system and is compared with other allocation methods.

## Slide 8
TITTLE | AUTHOR | DESCRIPTION
Frequency regulation services: A comparative study of select north american and european reserve markets | V. Pandurangan, H. Zareipour, and O. Malik, | Overview of frequency regulation services and reserve markets in which these regulation services are traded is provided in this paper.
Stability analysis of interconnected power systems coupled with market dynamics | F. L. Alvarado, J. Meng, C. L. DeMarco, and W. S. Mota, | The use of market mechanisms to determine generation dispatch, and the natural tendency to seek improved economic efficiency through rapid market updates, raises a critical issue.

## Slide 9: Block Diagram

## Slide 10: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 11: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 12: CONCLUTION
This paper studies the impact of discrete secondary frequency controllers on power system stability. The paper considers two secondary frequency controllers, namely, AGC and MAGC. The former is a controller installed in most of the control centers of TSOs, while the latter is a model that reproduces the behavior of real-time electricity markets with short dispatch periods. The findings of the paper are summarized below. 1) AGC: The illustrative example on the impact of discrete AGC on power system stability suggests that increasing too much the execution cycles of the AGC leads to a limitcycle or bang-bang phenomena. The example also shows that increasing the execution cycles of the AGC is comparable to increasing its control gain. Moreover, it is shown that the only effective solution to remove this issue is to keep as short as possible the AGC execution cycles. This is not a major constraint as, in practice, the AGC installed in the control centers of TSOs uses execution cycles that vary in the range of 2 to 6 s, which do not create instability issues. Regarding the differences with respect to the participation of WPPs in real-time electricity markets, the case study shows that this participation does not necessarily mean an improvement in the dynamic performance of the system.

## Slide 13: REFERENCE
[1] H. Bevrani, Robust Power System Frequency Control. Springer, 2009.
[2] F. Milano, F. Dorfler, G. Hug, D. J. Hill, and G. Verbi ¨ c, “Foundations ˇ and challenges of low-inertia systems (invited paper),” in Power Systems Computation Conference (PSCC), June 2018, pp. 1–25.
[3] D. Apostolopoulou, P. W. Sauer, and A. D. Dom´ınguez-Garcia, “Automatic generation control and its implementation in real time,” in 47th Hawaii International Conference on System Sciences, 2014, pp. 2444– 2452.
[4] V. Pandurangan, H. Zareipour, and O. Malik, “Frequency regulation services: A comparative study of select north american and european reserve markets,” in North American Power Symposium (NAPS), 2012, pp. 1–8.
[5] AEMO, “Aemo annual report 2018—leading the transformation.” [Online]. Available: https://www.aemo.com.au/-/media/files/about aemo/annual-report/aemo-annual-report-2018.pdf

## Slide 14
[6] F. L. Alvarado, J. Meng, C. L. DeMarco, and W. S. Mota, “Stability analysis of interconnected power systems coupled with market dynamics,” IEEE Transactions on Power Systems, vol. 16, no. 4, pp. 695–701, Nov 2001.
[7] C. Zhang, L. Jiang, Q. H. Wu, Y. He and M. Wu, “Further Results on Delay-Dependent Stability of Multi-Area Load Frequency Control,” IEEE Transactions on Power Systems, vol. 28, no. 4, pp. 4465–4474, 2013.
[8] L. Xu, Q. Guo, Z. Wang and H. Sun, “Modeling of Time-Delayed Distributed Cyber-Physical Power Systems for Small-Signal Stability Analysis,” IEEE Transactions on Smart Grid, in press, pre-print available on ieeexplore.ieee.org.
[9] X. Shangguan et al., “Robust Load Frequency Control for Power System Considering Transmission Delay and Sampling Period,” IEEE Transactions on Industrial Informatics, in press, pre-print available on ieeexplore.ieee.org.
[10] R. Venkateswaran and Y. H. Joo, “Retarded Sampled-Data Control Design for Interconnected Power System With DFIG-Based Wind Farm: LMI Approach,” IEEE Transactions on Cybernetics, in press, pre-print available on ieeexplore.ieee.org.