## Slide 1: A Multi-loop Transient Stability Control via Power Modulation from Energy Storage Device

## Slide 2: Abstract
This paper presents an optimal transient-stability control strategy that modulates the real power injected and absorbed by distributed energy-storage devices. These devices are located at the high-voltage bus of several generators in a synchronous power system. The system is broken into areas based upon groupings of generators. The control strategy consists of two parallel feedback loops. One loop focuses on preserving the synchronism of the generator to its own area. The second loop focuses on preserving the synchronism of a given area to the other areas.

## Slide 3
Each control loop strategy is based upon local and center-of-inertia frequency measurements. The strategy is derived from two perspectives. With the first, the goal is to remove as much kinetic energy gained during a disturbance as quickly as possible before it is converted to potential energy. With the second perspective, an optimal transient control costfunction is minimized. Both perspectives result in the same strategy. The performance of the control strategy is evaluated on a four-machine power system model and on a 34-generator reduced-order model of the western North-American grid. The results show that this control approach significantly improves the transient stability of power systems.

## Slide 4: Existing System
It is worth pointing out that the active and reactive power adjustment methods presented in existing literature usually consider case studies with test systems having a share of renewable power generation up to 50%.
Therefore, this paper focuses on modifying the outer control scheme of the WGs.
Other methods of existing literature attempted to modify the form of performing current limitations on the grid side converter, whereas other methods have proposed to modify the form of active and reactive power injection (e.g., based on signals measured at the connection point of the WGs).

## Slide 5: Disadvantage of Existing System
This is a classical constrained-input, minimum-time optimal control problem and the application of Pontryagin’s minimum principle yields the well-known bang-bang solution.
An optimal control problem can be formulated to determine the best trajectory for Pc(t).
The first constraint limits the maximum power absorption and delivery of the storage device and the second guarantees that the kinetic energy is gone at the end of the active control period.
The state equations are derived from with δ and ˙δ as the states.

## Slide 6: PROPOSED SYSTEM :
In a static synchronous compensator (STATCOM) based method has been proposed to enhance LVRT capability of four parallel-operated fully decoupled WGs fed to a power system by a proportional–integral–derivative (PID) damping controller designed based on the modal control theory.
This paper bridges the research gap on how to mitigate the amplitude of the first swing while enhancing the damping of rotor angle oscillations triggered by major electrical disturbances.
To this aim, a power-angle modulation (PAM) controller is proposed to adjust the post-fault active power response of the WG system

## Slide 7: ADVANTAGE
The performance of the control strategy is evaluated on a four-machine power system model and on a 34-generator reduced-order model of the western North-American grid. The result shows that this control approach significantly improves the transient stability of power systems.
To compare the performance of the multi-loop control strategy with that of the single-loop control, the simulation is repeated; however, in this case, the single-loop control strategy is implemented rather than the proposed multi-loop control strategy.
The performance of the control strategy is demonstrated on this contingency. Using the latched control, the speed of all the generators in the system grouped by their respective areas.

## Slide 8
TITTLE | AUTHOR | DESCRIPTION
Power system stability and control | P. Kundur, N. J. Balu, and M. G. Lauby | The book continues the successful approach of the first edition by progressing from simplicity to complexity.
Definition and classification of power system stability | P. Kundur and V. Ajjarapu, | The problem of defining and classifying power system stability has been addressed by several previous CIGRE and IEEE Task Force reports.

## Slide 9
TITTLE | AUTHOR | DESCRIPTION
Implementation and testing of remedial action schemes for real-time transient stability studies | M. M. Mahmoudi, S. Kincic, H. Zhang, and K. Tomsovic, | Deployment of Remedial Action Schemes (RAS) is a cost-effective alternative when taking pre-contingency actions or building new infrastructure are not desirable.
An eac based braking resistor approach for transient stability improvement | Y. Chen and M. e. El-Hawary, | In this paper, a new braking resistor approach using the equal area criterion (EAC) is presented to improve the transient stability of power systems

## Slide 10: Block Diagram

## Slide 11: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 12: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 13: CONCLUTION
In this paper, we developed and demonstrated an optimal control strategy that modulates the real power absorbed and injected by distributed energy storage devices in a synchronous power system. A single-loop control strategy was derived using a two-machine equivalent power system and then extended to a multi-loop control strategy. The control response was designed to have two parallel feedback loops with one loop focusing on preserving the synchronism of an individual generator to its area, and the other focusing on preserving the synchronism of a given area with other areas. The performance of the multi-loop control strategy is tested on a four-machine power system and a reduced-order model of the wNAPs. The results are compared to that of the derived singleloop control strategy. The results show that both the derived single-loop control strategy and the multi-loop control strategy significantly improve the transient stability of power systems. In cases where areas begin to swing against each other, the multi-loop control strategy outperforms the single-loop control strategy as designed.

## Slide 14: REFERENCE
[1] P. Kundur, N. J. Balu, and M. G. Lauby, Power system stability and control. McGraw-hill New York, 1994, vol. 7.
[2] P. Kundur and V. Ajjarapu, “Definition and classification of power system stability,” IEEE Transaction on Power Systems, vol. 19, pp. 1387–1401, 2004.
[3] M. M. Mahmoudi, S. Kincic, H. Zhang, and K. Tomsovic, “Implementation and testing of remedial action schemes for real-time transient stability studies,” in 2017 IEEE Power & Energy Society General Meeting, 2017, pp. 1–5.
[4] Y. Chen and M. e. El-Hawary, “An eac based braking resistor approach for transient stability improvement,” in 2006 IEEE International Symposium on Industrial Electronics, vol. 3, Conference Proceedings, pp. 1869–1874.
[5] M. H. Ali, T. Murata, and J. Tamura, “Effect of coordination of optimal reclosing and fuzzy controlled braking resistor on transient stability during unsuccessful reclosing,” IEEE Transactions on Power Systems, vol. 21, no. 3, pp. 1321–1330, 2006.

## Slide 15
[6] K. Kawabe and A. Yokoyama, “Improvement of angle and voltage stability by control of batteries using wide-area measurement system in power systems,” in 2012 3rd IEEE PES Innovative Smart Grid Technologies Europe (ISGT Europe), 2012, pp. 1–7.
[7] S. Ojetola, J. Wold, D. Trudnowski, F. Wilches-Bernal, and R. Elliott, “A real power injection control strategy for improving transient stability,” IEEE Power and Energy Society General Meeting, 2020.
[8] R. T. Elliott, “Trajectory tracking wide-area control for power systems,” Ph.D. dissertation, University of Washington, 2020.
[9] P. Sauer and M. Pai, Power system dynamics and stability. Prentice Hall, 1998.
[10] Y. Xue, T. V. Custem, and M. Ribbens-Pavella, “Extended equal area criterion justifications, generalizations, applications,” IEEE Transactions on Power Systems, vol. 4, no. 1, pp. 44–52, 1989.