## Slide 1: Optimal Reactive Power Dispatch with Discrete Controllers Using a Branch-and-Bound Algorithm A Semidefinite Relaxation Approach

## Slide 2: Abstract
Recently, several convex relaxations have been successfully applied to solve the AC optimal power flow (OPF) problem, which has caught the attention of the research community. Among these relaxations, a relaxation based on semidefinite programming (SDP) stands out. Accordingly, in this work a methodology to solve the optimal reactive power dispatch (ORPD) in electric power systems (EPS), considering discrete controllers, is proposed. Discrete controllers, such as the tap position of on-load tap changing (OLTC) transformers and switchable reactive shunt compensation, are optimized by the proposed method.

## Slide 3
A semidefinite relaxation (SDR) of the ORPD problem and a branch-and-bound (B&B) algorithm has been fully deployed. The customized B&B algorithm deals with the discrete nature of the binary control variables. Moreover, in order to enhance the convexification, valid inequalities called lifted non-linear-cuts (NLC) are implemented in the SDR. Additionally, a chordal decomposition technique is used to improve the computational performance. Finally, the B&B algorithm is used to solve the mixed-integer semidefinite programming problem. Several benchmarks have been used to show the accuracy and scalability of the proposed method, and convergence analysis shows that near-global optimal solutions are generated with small relaxation gaps.

## Slide 4: Existing System
If this constraint is satisfied, we stop. Otherwise, we proportionally reallocate the missing generation. However, due to the upper bound P max n , this redistribution may not be sufficient.
In this case, we randomly go through the list of generators and increase those that still have margin until the constraint is satisfied. We propose to test 5 plans of generation for each instance.
We focus on instances with more than 1000 buses. We only present instances for which we are certain that a feasible solution does exist.
This algorithm is very flexible since it is enough to adjust a few parameters to obtain a method adapted to each variant. Our algorithm is able to close the gap or at least improve it on most MATPOWER instances.

## Slide 5: Disadvantage of Existing System
The AC optimal power flow (AC OPF) which is the continuous version of OPF it is well known as a non-linear programming (NLP) problem with non-convex constraints.
It is important to mention that the essential feature that differentiates ORPD and OPF lies in the discrete control variables which represent the tap position of transformers and shunt capacitor banks operation. This additional feature increases the computational burden of the problem due to the "curse in dimensionality“.
As a solution technique, semidefinite programming will be used alongside the Branch and Bound Algorithm, which deals with the integrality nature of the problem.

## Slide 6: PROPOSED SYSTEM :
The proposed formulation provides strong lower bounds. On the other hand, it is not easy for the given model to further strengthen the provided model.
More precisely, we tested different techniques to tighten this SDP relaxation.
We tried to tighten the bounds onVss variables with Optimality-Based Bound Tightening (OBBT) techniques in order to tighten the McCormick envelopes.
We have introduced three new variants of the ROPF problem that tackle RTE issues. We have proposed a SDP-based B&B algorithm to solve them.

## Slide 7: ADVANTAGE
To improve the performance of the relaxations throughout the literature there are several narrowing methods such as bound tightening, the application of valid constraints, or the inclusion of spatial branch and bound algorithms that reinforce the relaxations.
Within the electric power systems, it is common the use of the transformation ratio changers (taps), because they are controllable variables of the system restricted by certain limits.
Classically the transformer tap ratio is included in the formulation of OPF in order to optimize the performance of the power system and improve the final result of the objective function.

## Slide 8
TITTLE | AUTHOR | DESCRIPTION
Power System State Estimation: Theory and Implementation | ABUR, A.; EXPÓSITO, A. | Building the Network Model Maximum Likelihood Estimation Measurement Model and Assumptions WLS State Estimation Algorithm Decoupled Formulation
Power Flow Test Systems Repository | AL-ROOMI, A. R. | A repository that contains most of the standard test systems used in power flow (or load flow) problems

## Slide 9
TITTLE | AUTHOR | DESCRIPTION
Further developments in lp-based optimal power flow | ALSAC, O. et al. | In addition, the approach accommodates a large variety of power system operating limits, including the very important category of contingency constraints.
Semidefinite relaxation and generalised benders decomposition to solve the transmission expansion network and reactive power planning | ALVAREZ, E. F.; PAREDES, M.; RIDER, M. J. | A mixed-integer non-linear programming model for the proposed planning problem is presented and rewritten with semidefinite structures.

## Slide 10: Block Diagram

## Slide 11: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 12: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 13: CONCLUTION
In this work, several SDP formulation for AC-OPF were presented to remark the equivalence between representations. Also, a proposed representation of SDP formulation considering the linear nature of the trace operator was presented to compare the proposed formulation and the non-linear model that later on will be modified to include the operation of discrete controllers i.e., tap position of transformers and reactive shunt compensation. The proposed methodology was developed on Julia Language using the optimization package JuMP (KWON, 2016) and using the commercial solver MOSEK (MOSEK, 2018). This work presented a methodology to solve the optimal reactive power dispatch with discrete controllers, such as the tap position of on-load tap-changing transformers and switchable shunt reactance compensation, via semidefinite relaxation and the branch-andbound algorithm. First, an SDR for the ORPD problem with continuous control variables is presented that considers the new reformulation presented for the OLTC variables, to obtain a connected structure of the SDP matrices.

## Slide 14: REFERENCE
ABUR, A.; EXPÓSITO, A. Power System State Estimation: Theory and Implementation. CRC Press, 2004. (Power Engineering (Willis)). ISBN 9780203913673. Disponível em: . Citado 2 vezes nas páginas 40 and 81.
AL-ROOMI, A. R. Power Flow Test Systems Repository. Halifax, Nova Scotia, Canada: [s.n.], 2015. Disponível em: . Citado na página 81.
ALSAC, O. et al. Further developments in lp-based optimal power flow. IEEE Transactions on Power Systems, v. 5, n. 3, p. 697–711, Aug. 1990. Citado na página 19.
ALVAREZ, E. F.; PAREDES, M.; RIDER, M. J. Semidefinite relaxation and generalised benders decomposition to solve the transmission expansion network and reactive power planning. IET Generation, Transmission Distribution, v. 14, n. 11, p. 2160–2168, 2020. Citado na página 62.
BAI, X. et al. Semidefinite programming for optimal power flow problems. Int. J. of Electrical Power and Energy Systems, v. 30, n. 6-7, p. 383–392, Sep. 2008. Citado 6 vezes nas páginas 20, 38, 40, 43, 45, and 60.

## Slide 15
BARAN, M.; WU, F. F. Optimal sizing of capacitors placed on a radial distribution system. IEEE Transactions on Power Delivery, v. 4, n. 1, p. 735–743, 1989. Citado na página 29.
BEZANSON, J. et al. Julia: A fresh approach to numerical computing. SIAM review, SIAM, v. 59, n. 1, p. 65–98, 2017. Disponível em: . Citado na página 81.
BINGANE, C.; ANJOS, M. F.; DIGABEL, S. L. Tight-and-cheap conic relaxation for the ac optimal power flow problem. IEEE Transactions on Power Systems, v. 33, n. 6, p. 7181–7188, Nov. 2018. Citado na página 21.
BINGANE, C.; ANJOS, M. F.; DIGABEL, S. L. Tight-and-cheap conic relaxation for the optimal reactive power dispatch problem. IEEE Transactions on Power Systems, 2019. Citado 4 vezes nas páginas 49, 61, 62, and 64.
BOSE, S. et al. Equivalent relaxations of optimal power flow. IEEE Transactions on Automatic Control, v. 60, n. 3, p. 729–742, March 2015. Citado 2 vezes nas páginas 47 and 60.