## Slide 1: Adaptive Decoupling Between Receivers of Multi-Receiver Wireless Power Transfer System Using Variable Switched Capacitor

## Slide 2: Abstract
Simultaneously charging multiple devices is a unique advantage of wireless power transfer (WPT). However, it is challenging to analyze and optimize the performance of a multi-receiver (multi-Rx) WPT system due to the intricate coupling among coils. In this paper, a method for adaptive decoupling between Rxs is proposed for electronic device charging, which can achieve independent regulation of each output in a multi-Rx WPT system. A simple feedback control avoids tedious system structure and position parameters measurement and calculation.

## Slide 3
With a fixed driving frequency, the number of Rx is not limited. It is analyzed that the quadrature phenomenon of the Tx and Rx currents can be used as a sign that the cross-coupling is fully compensated. A phase synchronization channel is established that shares power transfer coils. An MCU-free feedback loop is constructed in Rx to control the variable switched capacitor and finally realize adaptive cross-coupling compensation. A two-load experimental prototype was built to verify the theoretical analysis. Compared with the system without adaptive decoupling between Rxs, the measured system efficiency and output power of the proposed system were improved by 69% and 14.3 times, respectively.

## Slide 4: Existing System
It utilizes high-frequency electric fields to transfer electric power, which has three distinguishing advantages: negligible eddy-current loss, relatively low cost and weight, and excellent misalignment performance.
Safety is always an important concern in the WPT technology; it exists in both IPT and CPT systems, and is becoming a major constraint in the practical applications.
Although it has been proven that a CPT system can realize effective power transfer through a considerable distance, this process must be safe enough to be used for the general public.
In CPT system, there are mainly three important safety concerns: high voltage stress on the plates, strong electric fields emissions to the surroundings, and foreign object influence.

## Slide 5: Disadvantage of Existing System
Coupling efficiency peaks at close to 90% at a load resistance of 30 Ω. Although efficiency rolls off to around 36% at 1 kΩ, power delivered to the load resistance is very low and does not present heating problems to the system.
The decrease in power delivery as shown in Figure 5 when load resistance increases is desirable as it helps to regulate the power during trickle charge.
This technology can be applied to rugged electronics to enable the creation of hermetically sealed units, eliminating the problem of charging port contamination and corrosion.

## Slide 6: PROPOSED SYSTEM :
The proposed method is based on the concept of switch-mode gyrator emulating variable lossless inductors oriented to enable self-tunability in WPT receivers.
This paper discusses the mistuning effect of parallel-compensated receivers, and thereof a novel dynamic frequency tuning method and related circuit topology and control is proposed and characterized in the system application.
Therefore, this paper focuses on the discussion of mistuning issues in parallel-compensated WPT receivers in which the proposed dynamic tuning solution is dedicated for the same.

## Slide 7: ADVANTAGE
The gaps between each turn of the transmitting coil are spaced in a manner to achieve uniform field distribution and consistent performance regardless of the placement of the receiving coil.
However, shielding is beyond the scope of this paper and it is assumed that the system is adequately shielded from structures and materials that may significantly affect the system performance.
The purpose of the analysis is to study the performance of the circuit as a generic switch and not as a specific decoupling mechanism.
Transistor and diode models were obtained from the manufacturers to achieve accurate prediction of the performance of the fabricated circuit.

## Slide 8
TITTLE | AUTHOR | DESCRIPTION
Cutting the cord | L. Collins, | This case provides an opportunity to review the conditions for successful implementation of bundling and a-la-carte pricing strategies.
Design and analysis of a loosely coupled planar wireless power transfer system using magnetic induction | Z. N. Low, R. A. Chinga, R. Tseng, and J. Lin, | The overall objective of the inductively coupled power transfer (ICPT) systems is to provide wireless power transfer efficiently

## Slide 9
TITTLE | AUTHOR | DESCRIPTION
A multi-resonant converter for non-contact charging with electromagnetic coupling | R. Laouamer, M. Brunello, J. P. Ferrieux, O. Normand, and N. Bucheit, | This converter allows the transfer of power without oversizing the inverter and a soft-switching mode of the transistors.
A non-contact charger using a resonant converter with parallel capacitor of the secondary coil | H. Abe, H. Sakamoto, and K. Harada, | A method to get the optimum value of the capacitance which would maximize the charging current is described.

## Slide 10: Block Diagram

## Slide 11: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 12: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 13: CONCLUTION
A design approach using the series-parallel impedance transformation network topology is presented. A switch is also presented to achieve the decoupling mechanism based on the technique found in [13–15]. By decoupling a fully charged receiver from the system, power delivery to the other receiver can be improved. Experimental results verified the design. The fabricated system operating at a 12 V supply is capable of delivering nearly 2.5 W power to each receiver for a dual receiver setup under any loading conditions and 5 W to a single receiver alone or when one of the receivers is decoupled by the switch. System efficiency is higher than 55% for power delivery larger than 2 W whereas the efficiency reaches between 67.5% and 77.5% for high-power delivery above 4 W. Higher power system can be implemented by increasing the supply voltage. Increasing the coupling will improve the efficiency of the system. This is achieved by either decreasing the transmitting coil size or increasing the receiving coil size. However, this may decrease the degree of freedom of movement on the planar surface and thus defeat the purpose of a loosely coupled magnetic induction power system.

## Slide 14: REFERENCE
[1] L. Collins, “Cutting the cord,” Engineering and Technology, vol. 2, no. 6, pp. 30–33, 2007.
[2] Z. N. Low, R. A. Chinga, R. Tseng, and J. Lin, “Design and analysis of a loosely coupled planar wireless power transfer system using magnetic induction,” IEEE Transactions on Industrial Electronics, vol. 56, no. 5, pp. 1801–1812, 2009.
[3] R. Laouamer, M. Brunello, J. P. Ferrieux, O. Normand, and N. Bucheit, “A multi-resonant converter for non-contact charging with electromagnetic coupling,” in Proceedings of the 23rd International Conference on Electronics, Control and Instrumentation, vol. 2, pp. 792–797, November 1997.
[4] H. Abe, H. Sakamoto, and K. Harada, “A non-contact charger using a resonant converter with parallel capacitor of the secondary coil,” in Proceedings of the Applied Power Electronics Conference and Exposition, vol. 1, pp. 136–141, February 1998.
[5] G. Wang, W. Liu, M. Sivaprakasam, and G. A. Kendir, “Design and analysis of an adaptive transcutaneous power telemetry for biomedical implants,” IEEE Transactions on Circuits and Systems I, vol. 52, no. 10, pp. 2109–2117, 2005.

## Slide 15
[6] Y. Lu, K. W. E. Cheng, Y. L. Kwok, K. W. Kwok, K. W. Chan, and N. C. Cheung, “Gapped air-cored power converter for intelligent clothing power transfer,” in Proceedings of the 7th International Conference on Power Electronics and Drive Systems, pp. 1578–1584, November 2007.
[7] Y. Jang and M. M. Jovanovic, “A contactless electrical energy transmission system for portable-telephone battery chargers,” IEEE Transactions on Industrial Electronics, vol. 50, no. 3, pp. 520–527, 2003.
[8] C.-S. Wang, G. A. Covic, and O. H. Stielau, “Power transfer capability and bifurcation phenomena of loosely coupled inductive power transfer systems,” IEEE Transactions on Industrial Electronics, vol. 51, no. 1, pp. 148–157, 2004.
[9] C.-S. Wang, G. A. Covic, and O. H. Stielau, “Investigating an LCL load resonant inverter for inductive power transfer applications,” IEEE Transactions on Power Electronics, vol. 19, no. 4, pp. 995–1002, 2004.
[10] C.-S. Wang, O. H. Stielau, and G. A. Covic, “Design considerations for a contactless electric vehicle battery charger,” IEEE Transactions on Industrial Electronics, vol. 52, no. 5, pp. 1308– 1314, 2005.