## Slide 1: Implementation of Embedded Magnetic Encoder for Rotor Position Detection Based on Arbitrary Phase Shift Phase-Lock Loop

## Slide 2: Abstract
Rotor position is essential in control of permanent magnet synchronous motors (PMSMs). In terms of resolution, structural complexity, occupied volume, anti- interference ability, environmental adaptability and cost, embedded magnetic encoder based on linear Halls owns strong competitiveness. When linear Hall sensors are selectively installed at stator slot openings in extremely compact scenario, signal phase-shift asymmetry between two or three Hall sensors is inevitable. Conventionally, pre-filter synchronous reference frame phase locked loops (SRF-PLLs) exhibit excellent phase-lock ability at fixed frequency (50/60Hz),

## Slide 3
but become ill when frequency changes especially at zero frequency. In this paper, a novel transformation matrix is derived to map the asymmetric phase-shift signals onto two-phase stationary coordinate system. Then, an arbitrary phase-shift phase locked loop (APS-PLL) is formed by replacing Clark transformation with the proposed transformation matrix, which can accurately extract rotor position and speed information in a simple and effective way, avoiding the utilization of complex notch filter. Simulations in continuous domain based on MATLAB and experiments in discrete domain based on an 18-slot/20-pole prototyped PMSM both confirm the effectiveness of the proposed method.

## Slide 4: Existing System
Permanent magnet synchronous machines (PMSM) are used to an increasing rate in a wide rage of industrial applications due to their very appealing properties.
Among them are the high efficiency and dynamics, the high torque inertia ratio, the small size and the very low torque ripple.
Efficient operation of synchronous machines implies very low energy losses compensating their higher initial cost.
In a high-performance PMSM operation, advanced control methods are applied, such as field oriented control (FOC), aiming to achieve smooth rotation over the entire speed range, fast response and full torque control.

## Slide 5: Disadvantage of Existing System
However, the use of mechanical position sensor may cause some problems, such as extra cost, increase in system complexity, and reduction in system reliability.
To overcome the above problems, in, the influence of both the flux switching motor poles and winding layers on back-EMF harmonics was analysed and a modified fluxlinkage observer with an adaptive notch filter is proposed to eliminate harmonics to improve the accuracy of estimated rotor position.
To overcome the above problem, the software quadrature PLL can be used since it can synchronise the output signal with the input signal in frequency as well as in phase .
Both the rotor position and speed can be calculated from the estimated equivalent back-EMF with the PLL.

## Slide 6: PROPOSED SYSTEM :
The control strategy is principally based on the adequacy of the proposed modified model and on the appropriateness of the SMO structure to successfully track the rotor flux position with the required stability and accuracy.
Moreover, the proposed PMSM model plays a key role in the proposed sensorless approach.
In this work, a new mathematical model of PMSM is proposed expressed in a modified form for rotor flux equations and referred to the γδ estimated rotating frame.
Among the proposed observer schemes, the sliding mode observers (SMO) are widely studied in the literature and applied on a plethora of industrial applications.

## Slide 7: ADVANTAGE
To achieve high-performance sensorless control of permanent magnet motors with non-sinusoidal back electromotive force (EMF), an improved sliding mode observer (SMO) adopting synchronous rotating low-pass filter (SRLPF) is proposed.
In order to achieve high-performance control of the permanent magnet (PM) motors, both the rotor position and speed are essential.
Compared with other strategies, the SMO is widely used because of its simple algorithm, high robustness, and excellent dynamic performance.
As a new type of PM motor, the stator PM motors have both PMs and armature windings in stator, which exhibit better performance than the traditional interior permanent magnet synchronous motors (IPMSMs).

## Slide 8
TITTLE | AUTHOR | DESCRIPTION
Condition monitoring approach for permanent magnet synchronous motor drives based on the INFORM method | Arellano-Padilla, J., Sumner, M., Gerada, C.: | This paper proposes a monitoring scheme based on saliency tracking to assess the health condition of PMSM drives operating under non stationary conditions.
Carrier signal injection-based sensorless control for permanent magnet synchronous machine drives with tolerance of signal processing delays | Xu, P., Zhu, Z.: | The proposed position error suppression method is very easy and simple to implement, and moreover can significantly improve the sensorless control performance.

## Slide 9
TITTLE | AUTHOR | DESCRIPTION
Full speed region sensorless drive of permanent magnet machine combining saliency-based and back-EMF-based drive | Yang, S.C., Hsu, Y.L.: | At medium speed, electromotive force voltage can be estimated to replace the saliency for the sensorless drive.
Sensorless control of permanent magnet synchronous machine based on second-order sliding-mode observer with online resistance estimation | Liang, D., Li, J., Qu, R.: | A stator current observer is designed based on an STA to estimate the back electromotive force.

## Slide 10: Block Diagram

## Slide 11: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 12: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 13: CONCLUTION
In this paper, a modified rotor position estimator based on SMO with the adoption of SRLPF and quadrature PLL has been presented. The estimated back-EMF harmonics induced by both flux spatial harmonics and inverter non-linearity, which will decrease the estimated accuracy, are considered. The proposed strategy can filter out harmonics and extract the fundamental of estimated back-EMF for calculating the rotor position. Consequently, the performance of sensorless control method can be significantly improved. Additionally, the proposed sensorless control scheme is easy to implement. The effectiveness of the proposed strategy has been validated by experimental results at both steady and dynamic states in the speed range from 60 r/min to the rated speed 750 r/min. Although the developed sensorless control strategy is proposed for the stator PM motor, it can also be applicable to other PMSMs which need to eliminate the influence of non-sinusoidal back-EMF.

## Slide 14: REFERENCE
[1] Kalluf, F.J.H., Isfanuti, A.S., Tutelea, L.N., et al.: ‘1-kw 2000–4500 r/min ferrite PMSM drive: comprehensive characterization and two sensorless control options’, IEEE Trans. Ind. Appl., 2016, 52, (5), pp. 3980–3989
[2] Arellano-Padilla, J., Sumner, M., Gerada, C.: ‘Condition monitoring approach for permanent magnet synchronous motor drives based on the INFORM method’, IET Electr. Power Appl., 2016, 10, (1), pp. 54–62
[3] Xu, P., Zhu, Z.: ‘Carrier signal injection-based sensorless control for permanent magnet synchronous machine drives with tolerance of signal processing delays’, IET Electr. Power Appl., 2017, 11, (6), pp. 1140–1149
[4] Yang, S.C., Hsu, Y.L.: ‘Full speed region sensorless drive of permanent magnet machine combining saliency-based and back-EMF-based drive’, IEEE Trans. Ind. Electron., 2017, 64, (2), pp. 1092–1101
[5] Liang, D., Li, J., Qu, R.: ‘Sensorless control of permanent magnet synchronous machine based on second-order sliding-mode observer with online resistance estimation’, IEEE Trans. Ind. Appl., 2017, 53, (4), pp. 3672– 3682

## Slide 15
[6] Kim, S.I., Im, J.H., Song, E.Y., et al.: ‘A new rotor position estimation method of IPMSM using all-pass filter on high-frequency rotating voltage signal injection’, IEEE Trans. Ind. Electron., 2016, 63, (10), pp. 6499–6509
[7] Hejny, R.W., Lorenz, R.D.: ‘Evaluating the practical low-speed limits for back-EMF tracking-based sensorless speed control using drive stiffness as a key metric’, IEEE Trans. Ind. Appl., 2011, 47, (3), pp. 1337–1343
[8] Lascu, C., Boldea, I., Blaabjerg, F.: ‘A class of speed-sensorless sliding-mode observers for high-performance induction motor drives’, IEEE Trans. Ind. Electron., 2009, 56, (9), pp. 3394–3403
[9] Lu, X., Lin, H., Han, J.: ‘Load disturbance observer-based control method for sensorless PMSM drive’, IET Electr. Power Appl., 2016, 10, (8), pp. 735–743
[10] Park, Y., Sul, S.K.: ‘Sensorless control method for PMSM based on frequency-adaptive disturbance observer’, IEEE J. Emerging Sel. Top. Power Electron., 2014, 2, (2), pp. 143–151