## Slide 1: DORY Automatic End-to-End Deployment of Real-World DNNs on Low-Cost IoT MCUs

## Slide 2: Abstract
The deployment of Deep Neural Networks (DNNs) on end-nodes at the extreme edge of the Internet-of-Things is a critical enabler to support pervasive Deep Learning-enhanced applications. Low-Cost MCU-based end-nodes have limited on-chip memory and often replace caches with scratchpads, to reduce area overheads and increase energy efficiency – requiring explicit DMA-based memory transfers between different levels of the memory hierarchy. Mapping modern DNNs on these systems requires aggressive topology-dependent tiling and double-buffering. In this work, we propose DORY (Deployment Oriented to memoRY) – an automatic tool to deploy DNNs on low cost MCUs with typically less than 1MB of on-chip SRAM memory. DORY abstracts tiling as a Constraint Programming (CP) problem: it maximizes L1 memory utilization under the topological constraints imposed by each DNN layer.

## Slide 3
Then, it generates ANSI C code to orchestrate off- and on-chip transfers and computation phases. Furthermore, to maximize speed, DORY augments the CP formulation with heuristics promoting performance-effective tile sizes. As a case study for DORY, we target GreenWaves Technologies GAP8, one of the most advanced parallel ultra-low power MCU-class devices on the market. On this device, DORY achieves up to 2.5× better MAC/cycle than the GreenWaves proprietary software solution and 18.1× better than the state-of-the-art result on an STM32-H743 MCU on single layers. Using our tool, GAP-8 can perform end-to-end inference of a 1.0-MobileNet-128 network consuming just 63 pJ/MAC on average @ 4.3 fps – 15.4× better than an STM32-H743. We release all our developments – the DORY framework, the optimized backend kernels, and the related heuristics – as open-source software.

## Slide 4: Existing System
Artificial intelligence-powered pocket-sized air robots have the potential to revolutionize the Internet-of-Things ecosystem, acting as autonomous, unobtrusive, and ubiquitous smart sensors.
Nano-sized UAVs, with a sub-ten centimeters form-factor and a few tens of grams in weight, have the potential to enable exciting use cases, out of reach for bulkier aircraft.
We present our dataset augmentation methodology, which maximizes the model’s generalization capability with synthetic pitch, photometric, optical, and geometric enhancements.
Moving into nano-scale UAVs, we focus on those which employ novel deep learning-based algorithms .

## Slide 5: Disadvantage of Existing System
We also investigate the impact of memory dimensions on the network execution time.
The GAP-8 ’cluster’ is composed by eight 4-stage inorder single-issue pipeline RI5CY [38] cores, implementing the RISC-V RV32IMCXpulpV2 Instruction Set Architecture (ISA).
New tools such as TFLite Micro and the Larq Computing Engine (LCE) offer a model-agnostic deployment framework and overcome these problems.
The Solver relies on a 2-step engine, which solves the L3-L2 tiling constrained problem first, and the L2-L1 one afterwards.
Therefore, the load of the internal tiles and the asynchronous I/O DMA load of the following layer’s weights are often impacting performance.

## Slide 6: PROPOSED SYSTEM :
Our work demonstrates that deep learning models for robotic perception, trained and deployed with the proposed methodology, can afford extreme complexity reduction.
In, a model-based reinforcement learning (RL) policy is proposed to control a pocket-size quadcopter.
Parallel ultra-low power (PULP) processing is a recently proposed paradigm that is getting industrial and academic traction to respond to this heightened need of performance and energy efficiency for low-power edge devices.
The proposed neural network is inspired by the original Proximity network, where the same task was addressed with different ResNetbased topology and robotic platform.

## Slide 7: ADVANTAGE
In particular, the scarce availability of memory constitutes a real Deep Learning Memory Wall: a fundamental limitation to the maximum performance of an embedded DNN compute system.
However, to “unlock” such a system’s theoretical performance often requires carefully managed data movement by means of cache locking or explicit DMA transfers.
We evaluate the performance and energy efficiency of the deployed networks produced by DORY on GWT GAP-8, considering both single layers and end-to-end networks.
The GWT AutoTiler directly tackles the data-movement and tile sizing challenge to optimize memory access, reaching state-of-the-art performance on the execution of many networks.

## Slide 8
TITTLE | AUTHOR | DESCRIPTION
Machine learning for internet of things data analysis: a survey | M. S. Mahdavinejad, M. Rezvan, M. Barekatain, P. Adibi, P. Barnaghi, and A. P. Sheth, | The key contribution of this study is presentation of a taxonomy of machine learning algorithms explaining how different techniques are applied to the data in order to extract higher level information.
UAV-based IoT platform: A crowd surveillance use case | N. H. Motlagh, M. Bagaa, and T. Taleb, | A high-level view of a UAV-based integrative IoT platform for the delivery of IoT services from large height, along with the overall system orchestrator, is presented in this article.

## Slide 9
TITTLE | AUTHOR | DESCRIPTION
An overview of Internet of Things (IoT) and data analytics in agriculture: Benefits and challenges | O. Elijah, T. A. Rahman, I. Orikumhi, C. Y. Leow, and M. N. Hindia, | We present the IoT ecosystem and how the combination of IoT and DA is enabling smart agriculture.
A 64mW DNN-based Visual Navigation Engine for Autonomous Nano-Drones | D. Palossi, A. Loquercio, F. Conti, E. Flamand, D. Scaramuzza, and L. Benini, | To achieve this goal we developed a complete methodology for parallel execution of complex DNNs directly on board resource-constrained milliwatt-scale nodes.

## Slide 10: Block Diagram

## Slide 11: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 12: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 13: CONCLUTION
In this work, we introduced a novel framework for DNN deployment, DORY, which unburdens the programmer from the manual optimizations of neural networks on end-nodes. As a case study, we targeted a DNN-oriented MCU, GWT GAP-8, showing that it achieves 12.6× higher energy efficiency and 7.1× higher performance compared to the industry-standard STM32H743, and up to 26.6% end-to-end inference improvement compared to the proprietary tool from GWT. Our developments are released as open-source at https://github.com/pulp-platform/dory. Future work will focus on adding support for stronger quantization, hardware-accelerated primitives, and emerging memory technologies to support more high-accuracy networks directly on sub 10 mW extreme edge platforms.

## Slide 14: REFERENCE
[1] M. S. Mahdavinejad, M. Rezvan, M. Barekatain, P. Adibi, P. Barnaghi, and A. P. Sheth, “Machine learning for internet of things data analysis: a survey,” Digital Communications and Networks, vol. 4, no. 3, pp. 161 – 175, 2018.
[2] N. H. Motlagh, M. Bagaa, and T. Taleb, “UAV-based IoT platform: A crowd surveillance use case,” IEEE Communications Magazine, vol. 55, no. 2, pp. 128–134, 2017.
[3] M. Zanghieri, S. Benatti, A. Burrello, V. Kartsch, F. Conti, and L. Benini, “Robust Real-Time Embedded EMG Recognition Framework Using Temporal Convolutional Networks on a Multicore IoT Processor,” IEEE Transactions on Biomedical Circuits and Systems, 2019.
[4] O. Elijah, T. A. Rahman, I. Orikumhi, C. Y. Leow, and M. N. Hindia, “An overview of Internet of Things (IoT) and data analytics in agriculture: Benefits and challenges,” IEEE Internet of Things Journal, vol. 5, no. 5, pp. 3758–3773, 2018.
[5] D. Palossi, A. Loquercio, F. Conti, E. Flamand, D. Scaramuzza, and L. Benini, “A 64mW DNN-based Visual Navigation Engine for Autonomous Nano-Drones,” IEEE Internet of Things Journal, 2019.

## Slide 15
[6] F. Conti, R. Schilling, P. D. Schiavone, A. Pullini, D. Rossi, F. K. Gurkaynak, M. Muehlberghuber, M. Gautschi, I. Loi, G. Haugou ¨ et al., “An IoT Endpoint System-on-Chip for Secure and EnergyEfficient Near-Sensor Analytics,” IEEE Transactions on Circuits and Systems I: Regular Papers, vol. 64, no. 9, pp. 2481–2494, 2017.
[7] F. Conti, M. Rusci, and L. Benini, “The Memory Challenge in UltraLow Power Deep Learning,” in NANO-CHIPS 2030. Springer, 2020, pp. 323–349.
[8] H. Gao, W. Tao, D. Wen, T.-W. Chen, K. Osa, and M. Kato, “Ifqnet: Integrated fixed-point quantization networks for embedded vision,” in Proceedings of the IEEE Conference on Computer Vision and Pattern Recognition Workshops, 2018, pp. 607–615.
[9] Y. Chen, J. Emer, and V. Sze, “Eyeriss: A Spatial Architecture for Energy-Efficient Dataflow for Convolutional Neural Networks,” in 2016 ACM/IEEE 43rd Annual International Symposium on Computer Architecture (ISCA), 2016, pp. 367–379.
[10] F. Conti and L. Benini, “A Ultra-Low-Energy Convolution Engine for Fast Brain-Inspired Vision in Multicore Clusters,” in 2015 Design, Automation Test in Europe Conference Exhibition (DATE), 2015, pp. 683–688.