## Slide 1: A Novel Wireless Multifunctional Electronic Current Transformer based on ZigBee-based Communication

## Slide 2: Abstract
Overhead and underground power line monitoring is an essential infrastructure for advanced operation in the smart grid. Wireless sensor networks (WSN) are attractive to remote power line monitoring, due to their rare geography restrictions, simple engineering design, and flexible equipment expansion. Considering the ZigBee’s characteristic of low transmission rate, almost commercial sensors adopt the high-speed communication, such as Cellular and WiFi, to implement the real-time wireless monitoring. However, among all wireless technologies, ZigBee, characterizing high security, ultra-low power consumption, reliable network, low cost, and ease of design, is widely used in many industries.

## Slide 3
This paper proposes a new ZigBee-based communication for multifunctional electronic current transformers (ECTs), which are used in overhead and underground line monitoring. To tackle ZigBee’s low transmission rate, the proposed method involving a transmission strategy can make the ZigBee-based communication satisfy both measurable and protective purposes of multifunctional ECTs. Finally, the new ZigBee-based wireless communication is implemented and integrated with an ECT, which is based on the coreless Hall-effect current transformer (HCT), and the proposed ZigBee-based wireless multifunctional HCT is called ZiHCT. The measurement results show that the ZiHCT can achieve accuracy not only to Class 0.5 for measuring CTs, but also to Class 5P20 for protective CTs according to IEC standard 60044-8.

## Slide 4: Existing System
We are monitoring current and voltage through ADC and displayed on the LCD.
The monitoring of power grid has become an important part of maintaining the security and stability of power grid.
Smart grid collects the working information of power grid using sensors and judges the working state of power grid in the server of the monitoring center.
The emergence of wireless communication technology makes sensor constitute wireless sensor network, and the transmission of data does not need to rely on data lines such as optical fiber, saving more costs.

## Slide 5: Disadvantage of Existing System
The problem of core saturation still exists, and the sizes of the sensors are also almost the same as those of traditional CTs.
Moreover, the problem of different DC voltage levels existing in three amplified Hall voltages is also solved, and then the Hall voltages are sent to a low-pass filter to filter noise.
ZigBee characterizes the low transmission rate, the traditional ZigBee-based wireless communication used in real-time current waveform measurement will result in problems of signal packet error and serious delay.
The reconstructed waveform is similar to the actual current waveform, resolving the problem that ZigBee cannot be used for waveform transmission.

## Slide 6: PROPOSED SYSTEM :
It is the wireless device for transmitting and receiving purpose or simply it called as Transceiver.
In the transmitter section three sensors are interfaced to the LPC2148 controller and this controller is responsible for entire manipulations and the updated condition is displayed on the LCD and the same status is transmitted to the receiver section by using zigbee communication and is displayed on the pc which is on the receiver section.
A GSM modem is also interfaced to the controller to send the status to the pre-stored mobile number.
This project uses two power supplies, one is regulated 5V for modules and other one is 3.3V for microcontroller. 7805 three terminal voltage regulator is used for voltage regulation.

## Slide 7: ADVANTAGE
The ZiHCT has price and size advantages to potentially replace traditional CTs and other ECTs.
Traditional current transformers (CTs), mainly used to measure currents in power systems, are wound on closed cores of silicon steel sheets; thus, they are easily influenced by magnetic saturation and hysteresis.
The magnification design of the small and medium current ranges, the minified Hall voltages are transmitted to the positive inputs of an amplification circuit with two built-in instrumentation amplifiers, and then a DC offset adjustment circuit is used to produce two different voltage offsets to the negative inputs of amplification circuit.
An autotransformer T1 is used to control the special transformer T2, which has only one turn in its secondary winding.

## Slide 8
TITTLE | AUTHOR | DESCRIPTION
Real-time monitoring and dynamic thermal rating of power transmission circuits | D. A. Douglass and A. Edris, | These methods have been given various names including dynamic thermal rating, on-line rating, and dynamic ratings to describe the process of adjusting thermal ratings of power equipment for actual weather conditions and actual electrical load patterns.
A review of condition monitoring of underground power cables | A. A. Khan, N. Malik, A. Al-Arainy, and S. Alghuwainem, | Power distribution system relies heavily on a vast network of medium voltage (MV) underground cables for power delivery.

## Slide 9
TITTLE | AUTHOR | DESCRIPTION
Synchronized phasor measurement applications in power systems | J. D. L. Ree, V. Centeno, J. S. Thorp, and A. G. Phadke, | With the occurrence of major blackouts in many power systems around the world, the value of data provided by PMUs has been recognized, and installation of PMUs on power transmission networks of most major power systems has become an important current activity.
PMU-based monitoring of rotor angle dynamics | J. Yan, C. C. Liu, and U. Vaidya, | This paper proposes a PMU-based application for online monitoring of rotor angle stability.

## Slide 10: Block Diagram

## Slide 11: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 12: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 13: CONCLUTION
A multifunctional ECT for measurement and protection with ZigBee-based wireless communication is designed and implemented in this research. In the proposed method of ZigBee-based communication, when the measured current is detected as being in the small or medium current range, the RMS value per current cycle is transmitted to a back-end monitoring system to accomplish real-time monitoring. Furthermore, a reconstructed waveform based on timedelayed sampling technology is also delivered to the monitoring system. However, when the measured current is detected in the large current range, an alarm is immediately sent to the monitoring system, and 10 cycles of the actual current will be sent later for event analysis. The research tested the accuracy class of the proposed ZiHCT in accordance with IEC Standard 60044-8. The proposed ZiHCT (rated current: 600 A) can meet accuracy Class 0.5 for measuring CTs and 5P20 for protective CTs.

## Slide 14: REFERENCE
[1] D. A. Douglass and A. Edris, “Real-time monitoring and dynamic thermal rating of power transmission circuits,” IEEE Trans. Power Delivery, vol. 11, no. 3, pp. 1407–1418, Jul. 1996.
[2] A. A. Khan, N. Malik, A. Al-Arainy, and S. Alghuwainem, “A review of condition monitoring of underground power cables,” in Proc. 2012 Condition Monitoring and Diagnosis, Bali, Indonesia, pp. 909–912, Sept. 23–27, 2012.
[3] F. P. Mohamed, W. H. Siew, J. J. Soraghan, S. M. Strachan, and J. Mcwilliam, “The use of power frequency current transformers as partial discharge sensors for underground cables,” IEEE Trans. Dielectrics and Electrical Insulation, vol. 20, no. 3, pp. 814–824, Jun. 2013.
[4] J. D. L. Ree, V. Centeno, J. S. Thorp, and A. G. Phadke, “Synchronized phasor measurement applications in power systems,” IEEE Trans. Smart Grid, vol. 1, no. 1, pp. 20–27, Jun. 2010.
[5] J. Yan, C. C. Liu, and U. Vaidya, “PMU-based monitoring of rotor angle dynamics,” IEEE Trans. Power Systems, vol. 26, no. 4, pp. 2125–2133, Nov. 2011.

## Slide 15
[6] D. Cai, P. Regulski, M. Osborne, and V. Terzija, “Wide area inter-area oscillation monitoring using fast nonlinear estimation algorithm,” IEEE Trans. Smart Grid, vol. 4, no. 3, pp. 1721–1731, Sept. 2013.
[7] N. Kondrath, M. K. azimierczuk, “Bandwidth of current transformers,” IEEE Trans. Instrumentation and Measurement, vol. 58, no. 6, pp. 2008–2016, Jun. 2009.
[8] F. B. Ajaei, M. Sanaye-Pasand, M. Davarpanah, A. Rezaei-Zare, and R. Iravani, “Compensation of the current-transformer saturation effects for digital relays,” IEEE Trans. on Power Delivery, vol. 26, no. 4, pp. 2531–2540, Oct. 2011.
[9] H. Kirkham, “Current measurement methods for the smart grid,” in Proc. 2009 IEEE Power & Energy Society General Meeting, Calgary, Canada, Jul. 26–30, 2009.
[10] F. Li, W. Qiao, H. Sun, H. Wan, J. Wang, Y. Xia, Z. Xu, and P. Zhang, “Smart transmission grid: vision and framework,” IEEE Trans. Smart Grid, vol. 1, no. 2, pp. 168–177, Sept. 2010.