## Slide 1: Low-power wearable ECG monitoring system for multiple-patient remote monitoring

## Slide 2: Abstract
Many devices and solutions for remote ECG monitoring have been proposed in the literature. These solutions typically have a large marginal cost per added sensor and are not seamlessly integrated with other smart home solutions. Here we propose an ECG remote monitoring system that is dedicated to non-technical users in need of long-term health monitoring in residential environments and is integrated in a broader Internetof-Things (IoT) infrastructure. Our prototype consists of a complete vertical solution with a series of advantages with respect to the state of the art, considering both prototypes with integrated front end and prototypes realized with off-the-shelf components: i) ECG prototype sensors with record-low energy per effective number of quantized levels, ii) an architecture providing low marginal cost per added sensor/user, iii) the possibility of seamless integration with other smart home systems through a single internet-of-things infrastructure.

## Slide 3: Existing System
We introduce the relative investigation of all with past existing methodology.
Strength of matured individuals should be checked all the more often, which represents a more noteworthy challenge to existing clinical framework.
An electrocardiogram gadget screens the cardiovascular status of a patient by recording the heart's electrical potential versus time.
Such gadgets assume a vital part to save the existence of patients who endure a respiratory failure or experience the ill effects of these patients.
The gadget requires a few links associated with a patient of which influences the existence nature of a tolerant.

## Slide 4: Disadvantage of Existing System
The disadvantage of this system is it increases cost per patient.
However, power consumption mostly in such sensors is mainly due to the radio link and therefore the optimization obtained by the use of the dedicated front-end has a limited impact on the power performance of the complete sensor.
Most non-industrial nations have very helpless data about these medical services issues.
One such clinical issue which is normal and requires standard checking is pulse.
The current of the analog circuit results in low slew rate and problems of large signal performance of the system.

## Slide 5: PROPOSED SYSTEM :
In this paper we proposed an efficient system which is able to check ECG and send data to the webserver. Our proposed approach is do the proper justice with Cost, Size, power & Efficiency parameters.
The proposed ultra-low power ECG monitoring system provides a convenient everyday monitoring both for the patients and their physicians.
This robust system enables the users to track their hearts'signals even during intensive physical activities by removing the motion artifacts and filtering the external noises.
Some of the proposed ECG sensor nodes are based on a dedicated integrated front end, that sometimes includes a DSP, and require a second off-the-shelf chip to implement the radio link.

## Slide 6: ADVANTAGE
Our system instead, is based on a general-purpose, high performance, high resolution, low power ADC (Texas Instruments ADS1246)that also includes a digital filter.
Recent advances in microelectronics and in communication protocols enable cost reduction and performance improvement in these systems, both at the level of individual sensors, and at the level of the infrastructure.
When compared with fully integrated solutions, our circuit performance are better in terms of CMRR, input noise and ENOB.
We would like to stress the fact that a dedicated front-end chip is not enough to achieve an advantage in terms of overall sensor performance.

## Slide 7
TITTLE | AUTHOR | DESCRIPTION
Bayesian probabilistic population projections for all countries | A.E. Raftery, N. Li, H. Ševčíková, P. Gerland, G.K. Heilig, | They are mostly done deterministically, but there is a widespread need for probabilistic projections.
Vital Signs via Broadband: Remote Monitoring Technologies Transmit Savings | L. Robert, | An increasing reliance on health care information technology (IT) could mitigate some of the projected growth in health care spending, and thus help address mounting affordability concerns.

## Slide 8
TITTLE | AUTHOR | DESCRIPTION
Wireless sensor networks for monitoring physiological signals of multiple patients | R. S. Dilmaghani, H. Bobarshad, M. Ghavami, S. Choobkar, C. Wolfe, | The proposed remote monitoring system is a wireless sensor network with the nodes of the network installed in the patients' homes.
A long-term wearable electrocardiogram measurement system | M. K. Delano and C. G. Sodini, | A low-power, wearable electrocardiogram (ECG) monitor was developed for long-term data acquisition and analysis.

## Slide 9: Block Diagram

## Slide 10: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 11: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 12: CONCLUTION
We have proposed a wireless wearable ECG monitoring system embedded in an IoT platform that integrates heterogeneous nodes and applications, has a long battery life, and provides a high-quality ECG signal. The system allows monitoring multiple patients on a relatively large indoor area (home, building, nursing home, etc.). Our ECG sensor exhibits the record-low EEQNL figure of merit (energy per effective number of quantized levels) of all solutions with both discrete and integrated frontends available in the literature. As we have shown, this result is obtained through a careful set of choices at the level of components, circuit solutions, and algorithms. We would like to stress the fact that a dedicated front-end chip is not enough to achieve an advantage in terms of overall sensor performance. The latter depends on the optimization of the whole sensor, that is more practically done using off-the shelf components. Indeed, our proposed ECG sensor, based on a high performance ADC and a microprocessor-radio combo chip, provides much better performance, in terms of power consumption and noise, than many proposed systems based on a purposely designed front end chip. Another remarkable feature of our system is a very low marginal cost per added sensor, since our architecture enables a single low-cost gateway to manage multiple sensors.

## Slide 13: REFERENCE
[1] A.E. Raftery, N. Li, H. Ševčíková, P. Gerland, G.K. Heilig, “Bayesian probabilistic population projections for all countries,” in Proc. 2012 National Academy of Sciences, vol. 109 p. 13915-139121.
[2] G. Vincent, V. Velkoff, “The Next Four Decades: The Older Population in the United States 2010 to 2050”, Washington, DC: US Census Bureau, US Government Printing Office, 2010.
[3] European Commission, “The 2012 Ageing Report: Economic and budgetary projections for the 27 EU Member States (2010-2060),” 2012.
[4] L. Robert, “Vital Signs via Broadband: Remote Monitoring Technologies Transmit Savings,” Better Health Care Together Coalition, p. 1, Oct. 2008.
[5] IBM Institute for Business Value, “The future of connected health devices”, Executive Report, 2011.

## Slide 14
[6] R. S. Dilmaghani, H. Bobarshad, M. Ghavami, S. Choobkar, C. Wolfe, “Wireless sensor networks for monitoring physiological signals of multiple patients.,” IEEE transactions on biomedical circuits and systems, vol. 5, no. 4, pp. 347–56, Aug. 2011.
[7] M. K. Delano and C. G. Sodini, “A long-term wearable electrocardiogram measurement system,” in 2013 IEEE International Conference on Body Sensor Networks, 2013, pp. 1–6.
[8] E. S. Winokur, M. K. Delano, and C. G. Sodini, “A wearable cardiac monitor for long-term data acquisition and analysis,” IEEE Trans. Biomed. Eng., vol. 60, no. 1, pp. 189–92, Jan. 2013.
[9] N.J. Kim, J.H. Hong, T.S. Lee, “A Study on Power Consumption and Transmission Rate in ECG Signal Processing in Mobile Environment,” IFMBE Proceedings, Vol. 14, 2007, pp.4107-4110.
[10] I.-J. Wang, L.-D. Liao, Y.-T. Wang, C.-Y. Chen, B.-S. Lin, S.-W. Lu, C.-T. Lin, “A Wearable Mobile Electrocardiogram Measurement Device with Novel Dry Polymer-based Electrodes,” in Proc. 2010 IEEE Region 10 Conference, Fukuoka, Japan, 21–24 Nov. 2010, pp. 379–384.