## Slide 1: Exoskeleton robots for upper-limb rehabilitation

## Slide 2: Abstract
In this paper, the design of a new upper limb rehabilitation system is presented. The developed system is an exoskeleton with two degrees of freedom that can be used for diagnosis, physical therapy, and outcome evaluation. The system is dedicated to the patients with paraplegia of their upper extremities due to stroke or any disorders of the central or peripheral nervous system. The designed robot-aided therapy actuates both movements: flexion/extension for the elbow and pronation/supination for the forearm. The robotic system used Kinects skeletal tracking for an upper limb rehabilitation. Position control is communicated via a wireless network. Indeed a ZigBee protocol using xbee communication modules has been installed to ensure remote control of rehabilitation exercise. A kinematic model has been developed based on Denavit-Hartenberg approach to make first tests. A sliding mode robust law control has been implemented. The Lyapunov-based approach has been used to establish the system asymptotic stability. Experimental results are provided to demonstrate performances of the developed robot of upper limb remote rehabilitation.

## Slide 3: Existing System
In particular, the all-round comparisons of existing rehabilitation robots are based on the published available data, to make researchers fully aware of the limitations and advantages of diverse mechanical designs and control schemes.
The existing problems of upper limb rehabilitation robots are presented in this paper.
The end-effector-based upper limb rehabilitation robots (such as MIT-Manus, MIME) have the advantages of simple structure, easy carrying, simple control method, easy trajectory planning, etc., applying force to the patient's hand to pull upper limbs.
However, the exoskeleton style requires that the mechanical joint axis and the human body joint axis must coincide.

## Slide 4: Disadvantage of Existing System
The BONES occupies five actuators to provide a wide range of motion for the upper limb and further measurements for safety issues.
The disadvantage is that it is limited to two-dimensional space and it can not provide more training assistance to the upper limbs.
This paper analyzes some the upper limb rehabilitation robots and summarizes the problems in the structural design of these rehabilitation robots.
Many of these innovations were technology-driven, limiting their clinical application and impact.
A positive impact on outcome of function, rehabilitation approaches should be based on neurophysiological and clinical insights, keeping in mind that recovery of function is limited.

## Slide 5: PROPOSED SYSTEM :
The proposed exoskeleton robot depends on the extracted EMG signal to perform the limb’s motions.
The proposed exoskeleton rehabilitates the impaired limb by providing different angular velocities in addition to variations in impedance.
The proposed system, however, has its own limitations, such as its size and weight, in addition to its poor attachment.
The movement of the upper limb of the patient is assisted by the robot to achieve the purpose of rehabilitation training.
The training of cooperative hand movements (e.g. opening a bottle) has been proposed using a dedicated device, and can also be achieved by virtually coupling two unimanual devices through control.

## Slide 6: ADVANTAGE
The performance was judged based on timing and smoothness. While the training session consisted of goal direct reaching movement performed by the subject.
The performance and the recovery of the patients would suffer if the patient is not motivated and/or satisfied with the robotic rehabilitation.
Clinical studies have used different devices, training protocols and evaluation criteria to judge the performance of robotic device on impairment reduction.
The advantage of the end-effector-base robot is that the structure is simple and portable, the control method is simple and the trajectory planning is easy.

## Slide 7
TITTLE | AUTHOR | DESCRIPTION
Hand robotics rehabilitation: feasibility and preliminary results of a robotic treatment in patients with hemiparesis | P Sale, V Lombardi and M Franceschini, | This preliminary observer study was aimed at evaluating the efficacy of intensive robot-assisted therapy in hand function recovery, in the early phase after a stroke onset.
Supinator Extender (SUE): a pneumatically actuated robot for fore-arm/wrist rehabilitation after stroke | J Allington, SJ Spencer, J Klein, M Buell, DJ Reinkensmeyer and J Bobrow, | The flexion-extension motion is actuated by a cantilevered pneumatic cylinder, which allows the palm of the hand to remain open.

## Slide 8: Block Diagram

## Slide 9: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 10: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 11: CONCLUTION
In past two decades, many robotic devices for upper limb rehabilitation have been developed and tested. This paper has a systematic review on exoskeleton robotic-based upper limb robotic system, including their mechanism design, control strategies and clinical trial performance. These exoskeletons have been used in various clinical studies that measured their effectiveness using various clinical and non-clinical tests. A clinical trial of exoskeleton robots for upper limb revealed positive outcome as this form of therapy can easily match and in many cases produce a better result than conventional therapy. Results also indicated if the patient is active during the therapy session than the reduction in impairment was higher. Therefore exoskeleton with patient-driven control strategy produced significantly better results. Impact of robot-assisted therapy was not just restricted to clinical results. It was found that patient preferred this form of therapy, found it less boring and more effective.

## Slide 12: REFERENCE
1. F Vanoglio, A Luisa and F Garofali, "Mora C: Evaluation of the effectiveness of Gloreha (Hand Rehabilitation Glove) on hemiplegic patients", Pilot study. In XIII Congress of Italian Society of Neurorehabilitation, pp. 18-20, 2013.
2. I Parrinello, S Faletti and G Santus, "Use of a continuous passive motion device for hand rehabilitation: clinical trial on neurological patients", 41 National Congress of Italian Society of Medicine and Physical Rehabilitation, pp. 14-16, 2013.
3.V Varalta, N Smania, C Geroin, C Fonte, M Gandolfi, A Picelli, et al., "Effects of passive rehabilitation of the upper limb with robotic device Gloreha on visual-spatial and attentive exploration capacities of patients with stroke issues", XIII Congress of Italian Society of Neurorehabilitation, pp. 18-20, 2013.
4.C Casellato, A Pedrocchi, G Zorzi, L Vernisse, G Ferrigno and N Nardocci, "EMG-based visual-haptic biofeedback: a tool to improve motor control in children with primary dystonia", IEEE Trans Neural Syst Rehabil Eng, vol. 21, no. 3, pp. 474480, 2013.
5.P Sale, V Lombardi and M Franceschini, "Hand robotics rehabilitation: feasibility and preliminary results of a robotic treatment in patients with hemiparesis", Stroke Res Treat 2012, pp. 820931, 2012.

## Slide 13
6.L Pignolo, G Dolce, G Basta, LF Lucca, S Serra and WG Sannita, "Upper limb rehabilitation after stroke: ARAMIS a robo-mechatronic innovative approach and prototype", 4th IEEE RAS and EMBS Int. Conf. Biomedical Robotics and Biomechatronics (BioRob), pp. 14101414, 2012.
7.SE Palsbo and P Hood-Szivek, "Effect of robotic-assisted three-dimensional repetitive motion to improve hand motor function and control in children with handwriting deficits: a nonrandomized phase 2 device trial", Am J Occup Ther, vol. 66, no. 6, pp. 682690, 2012.
8.NSK Ho, KY Tong, XL Hu, KL Fung, XJ Wei, W Rong, et al., "An EMG-driven exoskeleton hand robotic training device on chronic stroke subjects: task training system for stroke rehabilitation", IEEE Int Conf Rehabil Robot, pp. 5975340, 2011.
9.S Masiero, M Armani and G Rosati, "Upper-limb robot-assisted therapy in rehabilitation of acute stroke patients: focused review and results of new randomized controlled trial", J Rehabil Res Dev, vol. 48, no. 4, pp. 355366, 2011.
10. J Allington, SJ Spencer, J Klein, M Buell, DJ Reinkensmeyer and J Bobrow, "Supinator Extender (SUE): a pneumatically actuated robot for fore-arm/wrist rehabilitation after stroke", Conf Proc IEEE Eng Med Biol Soc 2011, pp. 15791582, 2011.