## Slide 1: Identify the Deterioration in Pipe by Using Wheel Operated Robot

## Slide 2: Abstract
Nowadays, Robots are used in many industries for various purposes. Inspection is the one of the field in which robot used as the inspector. One application is monitoring the inside of the pipe, Recognizing and solving problem through interiorof the pipe. So, Inspection of pipe can be achieved by using wheel operated robot. Various problems related to pipe line such as corrosion, erosion and cracks. They can effectively reduce strength and wall thickness of pipe. Pipe inspection is necessary to locate defects due to corrosion and wear to avoid failure. In this work, Pipe inspection robot with ability to move inside horizontal and vertical pipes has been designed and fabricated. The robot consists of motor for driving and camera for monitoring.

## Slide 3: Existing System
Many very different designs exist for mechanisms moving inside pipes.
For inspection of large sewer pipes a large number of wheeled vehicles exist which provide traction with the pipe-wall simply trough their weight.
However, none of the existing projects targets both the small diameter, large spreading factor and capabilities of taking mitered bends at the same time.
Different wheel designs exist, the main difference lying in their roll-off shape.
A typical mecanum wheel can have a continuous motion on a flat floor providing traction perpendicular to the roller wheel orientation.

## Slide 4: Disadvantage of Existing System
A possible solution for this problem is explored in this paper, using omni-wheels or mecanum wheels.
The same problem has been solved on a different (conceptual) level by the RoboScan design where wheels have been employed which can rotate round a vertical axis.
With the progress of robotics technology, various types of mobile robots and mechanisms are designed to cope with this issue.
Encountering these issues gave us the inspiration to improve the previous design for better performance during operation.

## Slide 5: PROPOSED SYSTEM :
With most of the peristaltic or crawler-type robots no attention is paid to the orientation (or rotation) of the system inside the pipe.
The solution explored and proposed here makes use of the properties of an omniwheel to provide friction necessary for traction in the driving direction while allowing free motion in a direction tangential to the wheel.
To design a robot that fulfills the requirements proposed by the CNPC, some literature is investigated.
More sensors (e.g., IR sensors and tactile sensors) will be added into the inspection robotic system to satisfy multifunctional purposes in the oil pipeline inspection.

## Slide 6: ADVANTAGE
Using flat plate has the advantage that the design can be manufactured quickly using a laser cutter, allowing for short development cycles.
These wheels have been used in many robot platforms mainly aimed at a flat floor.
A PID controller has been used to control the robot’s orientation. Since damping in the system due to friction is very high and the first-order behavior is dominant, the D action can be omitted.
These might be contributed to the uneven surface of the wheels caused by the individual rollers.
The deviation between the encoder data (purple) and the accelerometer data (green) is caused by the slip of the roller wheels.

## Slide 7
TITTLE | AUTHOR | DESCRIPTION
Kinematic Analysis and Locomotion Strategy of A Pipe Inspection Robot Concept For Operation In Active Pipelines | Amr Bekhit, Abbas Dehghani, Robert Richardson | This paper outlines the requirements for such a robot and considers the advantages and disadvantages of existing systems.
Investigations Of Design Issues Related To In-pipe Inspection robots | Ankit Nayak, S. K. Pradhan | Several designs of in-pipe inspection robots have been proposed in the literature to solve the problems related with inspection of these complicated internal geometries.

## Slide 8
TITTLE | AUTHOR | DESCRIPTION
Defect Identification In Pipe Lines Using Pipe Inspection Robot | E Navin Prasad, M Kannan, A Azarudeen And N Karuppasamy | This robot can withstand many tough condition in pipeline and satisfy various requirements.
Development Of An Inspection Robot For Small Diameter Gas Distribution Mains | Edwin Dertien, Stefano Stramigioli, Kees Pulles. | The requirement to negotiate bends, T-joints and steep inclinations pose another set of strict design constraints.

## Slide 9: Block Diagram

## Slide 10: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 11: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 12: CONCLUTION
A very important goal of the robotic systems is the adaptability to the inner diameter of the pipes. Robot reduces human efforts making work simple and efficient. There are many fields where they are employed that include pipelines inspect and maintenance too. So, we had proposed a new design in inspecting pipelines. The major advantages are that it could be used in case of pipe diameter variation with the simple mechanism. We developed a pipe inspection robot that can be applied 20-30cm diameter pipeline. Robot is designed for vertical and horizontal purpose. So, Pipe inspecting robot is used in many industry for inspection of pipe.

## Slide 13: REFERENCE
[1] Amr Bekhit, Abbas Dehghani, Robert Richardson “Kinematic Analysis and Locomotion Strategy of A Pipe Ipnsection Robot Concept For Operation In Active Pipelines”, IJMEM, Vol.1, Issue 1, 2012, pp. 15-27.
[2] Ankit Nayak1, S. K. Pradhan2 “Investigations Of Design Issues Related To In-pipe Inspection robots”, IJETAE, vol. 4, Issue 3, March 2014,pp. 819-824.
[3] Atul Gargade1, Dhanraj Tambuskar2, Gajanan Thokal3 “120 Modelling and Analysis of Pipe Inspection Robot”, IJETAE, Vol. 3, Issue 5, May 2013, pp.120-126.
[4] E Navin Prasad1, M Kannan1, A Azarudeen1 And N Karuppasamy1 “Defect Identification In Pipe Lines Using Pipe Inspection Robot”, IJMERS vol.1, No.2, July 2012, pp. 21-31.
[5] Edwin Dertien, Stefano Stramigioli, Kees Pulles. “Development Of An Inspection Robot For Small Diameter Gas Distribution Mains,’’IEEE International Conference On Robotics And Automation, May 2011, pp. 5044-5049.

## Slide 14
[6]E Navin Prasad1, M Kannan1, A Azarudeen1 And N Karuppasamy1 “Defect Identification In Pipe Lines Using Pipe Inspection Robot”, IJMERS vol.1, No.2, July 2012, pp. 21-31.
[7]Harish P, V.Venkateswarlu “Design and Motion Planning of Indoor Pipeline Inspection Robot”, IJITEE, Vol.-3, Issue-7, December 2013, pp. 41-47.
[8]Mihaita Horodinca, Ioan Doroftei, Emmanuel Mignon, André Preumont “A Simple Architecture for In-pipe Inspection Robots” Universite Libre De Bruxelles, pp. 1-4.
[9]Nur Afiqah Binti Haji Yahya, Negin Ashrafi, Ali Hussein Humod, “Development And Adaptability Of In-pipe Inspection Robots” Vol. 11, Issue 4, jul-Aug.2014, pp. 1-8.
[10]Puneet Singh and G. K. Ananthasuresh “A Compact and Compliant External Pipe-Crawling Robot”, IEEE,Vol. 29, No. 1, February 2013, pp. 251-260.