## Slide 1: Low MOSFET Count Isolated DC-AC Converter

## Slide 2: Abstract
This letter proposes a novel soft-switched single-stage-isolated dc-ac converter topology from the industry point of view. The proposed converter requires a lesser number of MOSFETs compared to a widely studied cycloconverter-type (CCT)-isolated dc-ac converter topology. This converter provides lower duty cycle loss, better efficiency, and electromagnetic interference performance compared to a CCT dc-ac converter. Also, it is thermally more stable, thus requires a smaller heat sink. The converter operation is demonstrated in a 1-kW prototype developed with SiC MOSFETs.

## Slide 3: Existing System
It should be noted here that, although the choice of carrier between triangular waveform and sawtooth waveform does not make much difference in normal three-phase Sine-PWM (SPWM) converters, it makes a significant difference in terms of switching loss for the case of the nine-switch converter.
As can be found in almost all the existing literatures, owing to the XOR operation, the middle switches operate at twice the switching frequency (2fs), because a triangular carrier has been used everywhere.

## Slide 4: Disadvantage of Existing System
The previous connection had the disadvantage of not getting the whole Vdc at each of the primary sides.
One way to avoid the problem can be to choose a gating signal in such a way that the loads do not operate at the same time.
In that way one of the loads will have the whole input voltage at the primary side and the other will have zero.
The problem of not having Vdc as primary side voltage like the previous design will still remain. Also depending on the load condition, the voltage level will fluctuate and hence will be difficult to control.

## Slide 5: PROPOSED SYSTEM :
In order to avoid the bulky mains transformer and/or to increase power density and efficiency, alternatively, topologies with high-frequency isolation based on a dc–dc system feeding the dc link of a full-bridge dc–ac converter connected directly to the mains are proposed.
However, here, the low losses of the high-frequency isolation transformer have to be seen considering the additional losses of the rectifier stage and, especially, the line-side inverter.
According to the required dc-link voltage level (e.g., 400 V), this power stage, in general, has to be equipped with insulated gate bipolar transistors (IGBTs), which show a nonoptimum efficiency for operating in the partial load area.

## Slide 6: ADVANTAGE
Though these converters provide desired performance, they have two major concerns from a product perspective.
A bulky electrolytic capacitor bank is necessary to integrate the dc-dc stage and dc-ac inverter which reduces the power density. Typically, the standard electrolytic capacitors are rated for 105◦C. Thus, a lot of design efforts go into thermal management to achieve a longer product life.
The control complexity is high. It requires an additional dc voltage sensor to regulate the output of the dc-dc stage.

## Slide 7
TITLE | AUTHOR | DESCRIPTION
Novel DC–AC inverter based on phase-shift shoot-through controlled dual-active-bridge and high-frequency pulse DC link | Z. Song and W. Chen, | Based on the commonly used two-stage isolated inverter, this study proposed a novel DC–AC inverter that combines dual-active-bridge (DAB) converter, switched capacitor and full-bridge inverter.
High-Frequency Isolated AC–DC–AC Interleaved Converter for Power Quality Applications | O. Filho, B. Almeida, D. Oliveira J´unior and T. Neto, | The proposed converter is suitable for power quality applications, such as dynamic voltage restorers, uninterruptable power supplies, and voltage regulators.

## Slide 8
TITLE | AUTHOR | DESCRIPTION
A Unified State-Space Modeling Method for a Phase-Shift Controlled Bidirectional Dual-Active Half- Bridge Converter | H. Shi, K. Sun, H. Wu and Y. Li, | The existing state-space modeling methods are only suitable for modeling such a converter in two PSs directions separately, which results in a positive-PS model and a negative-PS model.
A Comparative Study Between AI-HM and SPD-HM for Railway Auxiliary Inverter With Pulsating DC Link | L. Diao, H. Du, Z. Shu, Y. Xue, M. Li and S. M. Sharkh, | Then a piecewise compensation of modulation wave and a carrier phase-shift strategy are proposed to improve the output voltage quality of AI-HM under zero portion effect.

## Slide 9: Block Diagram

## Slide 10: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 11: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 12: CONCLUSION
This letter proposes a single-stage isolated dc-ac converter with a target of industrial implantation. It addresses the shortcomings of conventional single-stage CCT converters. The converter performance is evaluated in a 1kW prototype. Compared to conventional CCT, the MOSFET count is reduced by two. The duty cycle loss is reduced by 40%. The average device case temperature is reduced by 10◦C. It also provides a better CE response with a noise reduction of 12 dBµV. The peak efficiency of the proposed converter is 97.2%. These advancements can help in developing a low-cost and reliable product for UPS applications.

## Slide 13: REFERENCE
[1] Z. Song and W. Chen, “Novel DC–AC inverter based on phase-shift shoot-through controlled dual-active-bridge and high-frequency pulse DC link,” IET Power Electronics, vol. 12, no. 14, pp. 3842-3851, 27- 11-2019.
[2] O. Filho, B. Almeida, D. Oliveira Junior and T. Neto, “High-Frequency ´ Isolated AC–DC–AC Interleaved Converter for Power Quality Applications,” IEEE Trans. on Ind. Appl., vol. 54, no. 5, pp. 4594-4602, Sept./Oct. 2018.
[3] H. Shi, K. Sun, H. Wu and Y. Li, “A Unified State-Space Modeling Method for a Phase-Shift Controlled Bidirectional Dual-Active HalfBridge Converter,” IEEE Trans. on Power Electron., vol. 35, no. 3, pp. 3254-3265, March 2020.
[4] L. Diao, H. Du, Z. Shu, Y. Xue, M. Li and S. M. Sharkh, “A Comparative Study Between AI-HM and SPD-HM for Railway Auxiliary Inverter With Pulsating DC Link,” IEEE Trans. on Ind. Electron., vol. 65, no. 7, pp. 5816-5825, July 2018.
[5] C. Abbate, G. Busatto, F. Iannuzzo, D. Marciano and D. Tedesco, “Isolated DC/AC Converter with ZVT based on Pulsating DC Link,” in IEEE Appl. Power Electron. Conf. and Expo., 2020, pp. 1162-1167.

## Slide 14
[6] M. Wang, S. Guo, Q. Huang, W. Yu and A. Q. Huang, “An Isolated Bidirectional Single-Stage DC–AC Converter Using Wide-Band-Gap Devices With a Novel Carrier-Based Unipolar Modulation Technique Under Synchronous Rectification,” IEEE Trans. on Power Electron., vol. 32, no. 3, pp. 1832-1843, March 2017.
[7] M. Wang, Q. Huang, S. Guo, X. Yu, W. Yu and A. Q. Huang, “SoftSwitched Modulation Techniques for an Isolated Bidirectional DC–AC,” IEEE Trans. on Power Electron., vol. 33, no. 1, pp. 137-150, Jan. 2018.
[8] P. Nayak, K. Rajashekara and S. K. Pramanick, “Soft-Switched Modulation Technique for a Single-Stage Matrix-Type Isolated DC–AC Converter,” IEEE Trans. on Ind. Appl., vol. 55, no. 6, pp. 7642-7656, Nov./Dec. 2019.
[9] S. Tiwari, S. Basu, T. M. Undeland and O. Midtgard, “Efficiency and ˚ Conducted EMI Evaluation of a Single-Phase Power Factor Correction Boost Converter Using State-of-the-Art SiC Mosfet and SiC Diode,” IEEE Trans. on Ind. Appl., vol. 55, no. 6, pp. 7745-7756, Nov./Dec. 2019.
[10] W. Zhu, K. Zhou and M. Cheng, “A Bidirectional High-Frequency-Link Single-phase Inverter: Modulation, Modeling, and Control,” IEEE Trans. on Power Electron., vol. 29, no. 8, pp. 4049-4057, Aug. 2014.