## Slide 1: Feed forward-Cutset-Free Pipelined Multiply-Accumulate Unit for the Machine Learning Accelerator

## Slide 2: Abstract
Multiply–accumulate (MAC) computations account for a large part of machine learning accelerator operations. The pipelined structure is usually adopted to improve the performance by reducing the length of critical paths. An increase in the number of flip-flops due to pipelining, however, generally results in significant area and power increase. A large number of flip-flops are often required to meet the feedforward-cutset rule. Based on the observation that this rule can be relaxed in machine learning applications, we propose a pipelining method that eliminates some of the flip-flops selectively. The simulation results show that the proposed MAC unit achieved a 20% energy saving and a 20% area reduction compared with the conventional pipelined MAC.

## Slide 3: Existing System
The proposed design method reduces the area and the power consumption by decreasing the number of inserted flipflops for the pipelining when compared to the existing pipelined architecture for MAC computation.
The deep neural network (DNN) emerged as a powerful tool for various applications including image classification and speech recognition.
In a machine learning accelerator, a large number of multiply– accumulate (MAC) units are included for parallel computations, and timing-critical paths of the system are often found in the unit.
It is well known that pipelining is one of the most effective ways to reduce the critical path delay, thereby increasing the clock frequency.

## Slide 4: Disadvantage of Existing System
Number of inserted flip flops increases the pipeline stages.
Consumes larger area and high critical path delay.
Power consumption is high.

## Slide 5: PROPOSED SYSTEM :
The proposed plan technique lessens the zone and the power utilization by diminishing the quantity of embedded flipflops for the pipelining.
In this area, the proposed pipelining strategy is applied to the MAC engineering by utilizing the one of a kind normal for Dadda multiplier.
The proposed MAC design the FCF (MAC with the proposed FCF pipelining) for the segment expansion and the MFCF-PA for the collection.
We accept that the proposed thought to use the one of a kind normal for machine learning calculation for progressively effective MAC configuration can be received in numerous neural system.

## Slide 6: ADVANTAGE
An accumulator consists of the carry-propagation adder. Long critical paths through these stages lead to the performance degradation of the overall system.
Based on the previously explained idea, this paper proposes a feed forward-cut set-free (FCF) pipelined MAC architecture that is specialized for a high-performance machine learning accelerator.
Although pipelining is an efficient way to reduce the critical path delays, it results in an increase in the area and the power consumption due to the insertion of many flip-flops.
While the conventional pipelining method is advantageous because it effectively reduces the critical path delays, it leads mostly to an increase in the area and the power consumption due to the insertion of a large number of flip-flops.

## Slide 7
TITTLE | AUTHOR | DESCRIPTION
ImageNet classification with deep convolutional neural networks | A. Krizhevsky, I. Sutskever, and G. E. Hinton, | ImageNet consists of variable-resolution images, while our system requires a constant input dimensionality.
Very deep convolutional networks for large-scale image recognition | K. Simonyan and A. Zisserman. (2014). | In this work we investigate the effect of the convolutional network depth on its accuracy in the large-scale image recognition setting.

## Slide 8
TITTLE | AUTHOR | DESCRIPTION
Going deeper with convolutions | C. Szegedy et al., | We propose a deep convolutional neural network architecture codenamed Inception that achieves the new state of the art for classification and detection in the ImageNet Large-Scale Visual Recognition Challenge 2014 (ILSVRC14).
Speech recognition with deep recurrent neural networks | A. Graves, A.-R. Mohamed, and G. Hinton, | They have gained attention in recent years with the dramatic improvements in acoustic modelling yielded by deep feedforward networks.

## Slide 9: Block Diagram

## Slide 10: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 11: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 12: CONCLUSION
We introduced the FCF pipelining method in this paper. In the proposed scheme, the number of flip-flops in a pipeline can be reduced by relaxing the feedforward-cutset constraint, thanks to the unique characteristic of the machine learning algorithm. We applied the FCF pipelining method to the accumulator (FCF-PA) design, and then optimized the power dissipation of FCF-PA by reducing the chance of undesired data transitions (MFCF-PA). The proposed scheme was also expanded, and applied to the MAC unit (FCF-MAC). For the evaluation, the conventional and proposed MAC architectures were synthesized in a 65-nm CMOS technology. The proposed accumulator showed the reduction of area and the power consumption by 17% and 19%, respectively, compared with the accumulator with the conventional CLA adder-based design. In the case of the MAC architecture, the proposed scheme reduced both the area and power by 20%. We believe that the proposed idea to utilize the unique characteristic of machine learning computation for more efficient MAC design can be adopted in many neural network hardware accelerator designs in the future.

## Slide 13: REFERENCE
[1] A. Krizhevsky, I. Sutskever, and G. E. Hinton, “ImageNet classification with deep convolutional neural networks,” in Proc. Adv. Neural Inf. Process. Syst., 2012, pp. 1097–1105.
[2] K. Simonyan and A. Zisserman. (2014). “Very deep convolutional networks for large-scale image recognition.” [Online]. Available: https://arxiv.org/abs/1409.1556
[3] C. Szegedy et al., “Going deeper with convolutions,” in Proc. IEEE Conf. Comput. Vis. Pattern Recognit., Jun. 2015, pp. 1–9.
[4] A. Graves, A.-R. Mohamed, and G. Hinton, “Speech recognition with deep recurrent neural networks,” in Proc. IEEE Int. Conf. Acoust., Speech Signal Process. (ICASSP), May 2013, pp. 6645–6649.
[5] J. K. Chorowski, D. Bahdanau, D. Serdyuk, K. Cho, and Y. Bengio, “Attention-based models for speech recognition,” in Proc. Adv. Neural Inf. Process. Syst., 2015, pp. 577–585.

## Slide 14
[6] Y. H. Chen, T. Krishna, J. S. Emer, and V. Sze, “Eyeriss: An energy-efficient reconfigurable accelerator for deep convolutional neural networks,” IEEE J. Solid-State Circuits, vol. 52, no. 1, pp. 127–138, Jan. 2017.
[7] B. Moons, R. Uytterhoeven, W. Dehaene, and M. Verhelst, “Envision: A 0.26-to-10tops/w subword-parallel dynamic-voltage-accuracyfrequency-scalable convolutional neural network processor in 28nm FDSOI,” in Proc. IEEE Int. Solid-State Circuits Conf. (ISSCC), Feb. 2017, pp. 246–247.
[8] C. S. Wallace, “A suggestion for a fast multiplier,” IEEE Trans. Electron. Comput., vol. EC-13, no. 1, pp. 14–17, Feb. 1964.
[9] L. Dadda, “Some schemes for parallel multipliers,” Alta Frequenza, vol. 34, no. 5, pp. 349–356, Mar. 1965.
[10] P. F. Stelling and V. G. Oklobdzija, “Implementing multiply-accumulate operation in multiplication time,” in Proc. 13th IEEE Symp. Comput. Arithmetic, Jul. 1997, pp. 99–106.