## Slide 1: Multiloop control for Fast Transient DC-DC Converter

## Slide 2: Abstract
A novel ac coupled feedback (ACCF) is proposed to alternatively realize fast transient response while inherently controlling the start-up in-rush current of a dc–dc switching converter. The proposed ACCF is modified from a conventional capacitor multiplier and connected between the outputs of the converter and the transconductance. With this supplemental feedback, the transient response has been significantly improved due to the gain-boosting effect around the compensator’s midband. Moreover, the ACCF circuit assists to manage the ramping speed of the output voltage during power-up, thereby eliminating the bulky soft-start circuit.

## Slide 3
The new controller is very simple to implement and occupies a tiny footprint on-chip. A buck converter with the proposed scheme has been fabricated using the 0.18-µm standard CMOS process with an active silicon area of 0.573 mm2. Measurement results show that the output voltage rises linearly for a soft-start period of 1.05 ms according to the designed slope. Excellent load transient responses are achieved under different load current steps; the output voltage overshoot/undershoot of 60 mV settles down within 10 µs for a load variation from 50 µA to 1 A in 1 µs. Moreover, the proposed converter maintains both excellent load and line regulations of 0.018 mV/mA and 0.0056 mV/mV, respectively.

## Slide 4: Existing System
There is a massive load current change when the system switches from an idle mode to an active mode. Ideally, the regulator should maintain a voltage level that is almost constant, which means that there should be a negligible output voltage overshoot /undershoot and rapid response time.
To accomplish these stringent requirements, various research works on fast transient dc–dc converters have been proposed.
The pole and zero are moved back immediately after the transient event to stabilize the system.
However, a careful design targeting system stability during the whole process needs to be taken into consideration once the bandwidth is tentatively changed.

## Slide 5: Disadvantage of Existing System
Difficult to achieve fast load transient performance.
Current boosting modules in existing system require more power, which degrades the overall efficiency.
High electromagnetic interface (EMI) noise.

## Slide 6: PROPOSED SYSTEM :
This paper utilizes a current-mode controller to improve the response speed aspect by increasing the system bandwidth in order to enhance the load transient response.
A novel ACCF is paralleled around the compensator to boost the response strength at the mid-band.
With the help of the ACCF circuit, in this case, the fast-rising voltage appearing at Vout caused by the inrush start-up current is coupled through the ACCF and induces the ac current from Vc into the ACCF itself.
This particular inherent function of the proposed ACCF eliminates the need for a dedicated soft-start circuit in the conventional designs.

## Slide 7: ADVANTAGE
The demand for fast load transient performance has grown significantly, affecting the power supplies of modern high-speed processors especially processors targeting to achieve a fast transition from the low-power idle mode to the high-speed active mode.
The load transient performance is improved on account of the gain boosting effect around the compensator’s mid-band.
A variable resistor was connected at the output of the converter in series with a switch to measure the load transient performance.
Moreover, current-boosting modules introduce more power consumption, which degrades the overall efficiency.

## Slide 8
TITTLE | AUTHOR | DESCRIPTION
Fast transient response DC–DC converter with start-up in-rush current control | M. Zhou, Z. Sun, Q. Low, and L. Siek, | A new alternative to achieve fast transient response while inherently managing the in-rush current during DC/DC switching converter start-up is proposed.
Adaptive pole-zero position (APZP) technique of regulated power supply for improving SNR | C.-Y. Hsieh and K.-H. Chen, | This paper proposes an adaptive pole-zero position (APZP) technique to achieve excellent transient response of dc--dc converters.

## Slide 9
TITTLE | AUTHOR | DESCRIPTION
A monolithic current-mode CMOS DC-DC converter with on-chip current-sensing technique | C. F. Lee and P. K. T. Mok, | A monolithic current-mode CMOS DC-DC converter with integrated power switches and a novel on-chip current sensor for feedback control is presented in this paper.
An integrated CMOS current-sensing circuit for low-voltage current-mode buck regulator | C. Y. Leung, P. K. T. Mok, K. N. Leung, and M. Chan, | An integrated current-sensing circuit for low-voltage buck regulator is presented.

## Slide 10: Block Diagram

## Slide 11: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 12: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 13: CONCLUTION
A compact fast transient response current-mode buck converter with inherent soft-start is presented in this paper. Experimental results show that the designed converter can achieve a fast load transient response under different load current steps (500 mA and 1 A) with different output voltages (1.2 and 1.8 V). The soft-start period of more than 1 ms is also inherently realized. The controller is simple to implement, and yet demonstrates great performance in both load and line regulations. The proposed converter is appropriate for applications which necessitate the fast transient response over a large load range, especially for use in conjunction with microprocessors.

## Slide 14: REFERENCE
[1] M. Zhou, Z. Sun, Q. Low, and L. Siek, “Fast transient response DC–DC converter with start-up in-rush current control,” Electron. Lett., vol. 52, no. 22, pp. 1883–1885, Oct. 2016.
[2] C.-Y. Hsieh and K.-H. Chen, “Adaptive pole-zero position (APZP) technique of regulated power supply for improving SNR,” IEEE Trans. Power Electron., vol. 23, no. 6, pp. 2949–2963, Nov. 2008.
[3] Y.-H. Lee, S.-C. Huang, S.-W. Wang, and K.-H. Chen, “Fast transient (FT) technique with adaptive phase margin (APM) for current mode DC-DC buck converters,” IEEE Trans. Very Large Scale Integr. (VLSI) Syst., vol. 20, no. 10, pp. 1781–1793, Oct. 2012.
[4] C. F. Lee and P. K. T. Mok, “A monolithic current-mode CMOS DC-DC converter with on-chip current-sensing technique,” IEEE J. Solid-State Circuits, vol. 39, no. 1, pp. 3–14, Jan. 2004.
[5] C. Y. Leung, P. K. T. Mok, K. N. Leung, and M. Chan, “An integrated CMOS current-sensing circuit for low-voltage current-mode buck regulator,” IEEE Trans. Circuits Syst. II, Exp. Briefs, vol. 52, no. 7, pp. 394–397, Jul. 2005.

## Slide 15
[6] K.-I. Wu, B.-T. Hwang, and C. C.-P. Chen, “Synchronous doublepumping technique for integrated current-mode PWM DC–DC converters demand on fast-transient response,” IEEE Trans. Power Electron., vol. 32, no. 1, pp. 849–865, Jan. 2017.
[7] Y.-H. Lee, K.-Y. Chu, C.-J. Shih, and K.-H. Chen, “Proportional compensated buck converter with a differential-in differential-out (DIDO) error amplifier and load regulation enhancement (LRE) mechanism,” IEEE Trans. Power Electron., vol. 27, no. 5, pp. 2426–2436, May 2012.
[8] P.-J. Liu, T.-H. Chen, and S.-R. Hsu, “Area-efficient error amplifier with current-boosting module for fast-transient buck converters,” IET Power Electron., vol. 9, no. 10, pp. 2147–2153, Aug. 2016.
[9] J. Roh, “High-performance error amplifier for fast transient DC-DC converters,” IEEE Trans. Circuits Syst. II, Exp. Briefs, vol. 52, no. 9, pp. 591–595, Sep. 2005.
[10] H. Lee, P. K. T. Mok, and K. N. Leung, “Design of low-power analog drivers based on slew-rate enhancement circuits for CMOS low-dropout regulators,” IEEE Trans. Circuits Syst. II, Exp. Briefs, vol. 52, no. 9, pp. 563–567, Sep. 2005.