## Slide 1: CMOS First-Order All-Pass Filter With 2-Hz Pole Frequency

## Slide 2: Abstract
A CMOS fully integrated all-pass filter with an extremely low pole frequency of 2 Hz is introduced in this paper. It has 0.08-dB passband ripple and 0.029-mm2Si area. It has 0.38-mW power consumption in strong inversion with ±0.6-V power supplies. In subthreshold, it has 0.64-µW quiescent power and operates with ±200-mV dc supplies. Miller multiplication is used to obtain a large equivalent capacitor without excessive Si area. By varying the gain of the Miller amplifier, the pole frequency can be varied from 2 to 48 Hz. Experimental and simulation results of a test chip prototype in 130-nm CMOS technology validate the proposed circuit.

## Slide 3: Existing System
This paper has presented a new voltage-mode first order all-pass filter employing one FDCCII, one grounded capacitor and resistor.
The salient features of the proposed circuit is use of grounded capacitor, suitable for IC implementation, providing inverting and non inverting voltage-mode all-pass responses simultaneously from the circuit and also providing one of the voltage output at low impedance thus making them suitable for voltage-mode cascading.
This element is a versatile building block whose applications exist in the literature.
Some voltage-mode circuits benefit from minimum component feature and hence require no matching constraints.

## Slide 4: Disadvantage of Existing System
Temperature dependence and manufacturing tolerances are common problems in all continuous time integrated filters.
A voltage-mode all-pass filter with minimum component is expected to use two passive components and one active element.
Two component based circuits are free from matching problems as both pole and zero frequency depend on the same two components such circuits would benefit from easy control over the pole frequency, as only a single element need to be controlled unlike the circuits require three components.
This feature not collectively exhibited in any of the reported work in the literature, including the most recent and useful circuit.

## Slide 5: PROPOSED SYSTEM :
The proposed circuit demonstrates a high linearity and consumes merely 16 mW power from a 1.8-V supply.
A new first-order voltage-mode filter employing minimum active and passive components is proposed.
The proposed configuration employs one differential voltage current conveyor (DVCC), one grounded capacitor and one resistor.
In this paper, the authors proposed a simple first-order filter employ minimum active and passive components.
The proposed circuit can realize first-order lowpass, highpass and allpass filter responses in the same configuration and still enjoys all of the above features.

## Slide 6: ADVANTAGE
In these circuits the current rather than the voltage is used as the active variable either throughout the whole circuit or only in certain critical areas.
The use of current-mode active devices has many other advantages such as larger dynamic, higher bandwidth, greater linearity, simple circuitry and low power consumption compared to that of voltage-mode counterparts for example operational amplifiers.
Due to a simple structure and appropriate performance of the proposed all-pass filter, this filter achieves a flat group delay of over 60 ps with a pole/zero pair located at 4.5 GHz.
If the useful frequency range of the proposed filter is limited in, the influences of parasitic elements to the coefficient n will be diminished.

## Slide 7
TITLE | AUTHOR | DESCRIPTION
Design and application of allpass filters with equiripple group delay errors | X. Lai and Z. Lin, | In this paper, an iterative linear programming (LP) algorithm is first presented to solve the minimax phase error design of allpass filters.
A new second-order all-pass filter in 130-nm CMOS | P. Ahmadi, B. Maundy, A. S. Elwakil, L. Belostotski, and A. Madanayake, | The core of the circuit consists of only one transistor, two resistors, and two energy storage elements.

## Slide 8
TITLE | AUTHOR | DESCRIPTION
Differential-input buffered and transconductance amplifier-based all-pass filter and its application in quadrature oscillator | J. Vavra, J. Bajer, and D. Biolek, | The paper deals with a novel all-pass filter circuit employing Differential-input Buffered and Transconductance Amplifier (DBTA), two grounded resistors and two grounded capacitors.
Frequency limitations of first-order gm –RC all-pass delay circuits | S. K. Garakoui, E. A. M. Klumperink, B. Nauta, and F. E. vanVliet, | All-pass filter circuits can implement a time delay but, in practice, show delay and gain variations versus frequency, limiting their useful frequency range.

## Slide 9: Block Diagram

## Slide 10: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 11: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 12: CONCLUSION
A first-order APF with extremely low f0 frequency (Hz) was introduced and verified experimentally with a test chip prototype in 130-nm CMOS technology. To the authors’ knowledge, no other APF with such low f0 frequency has been reported in the literature. The proposed circuit is based on a linear OTA and provides very low passband ripple. It achieves extremely large time constants (∼seconds) with low silicon area requirements due to the utilization of quasi-floating gate transistors and Miller capacitors. By varying the gain of the Miller amplifier, variable f0 can be achieved. Experimental results substantiate that the proposed APF provides phase quadrature at 2 Hz and a constant gain from dc to 100 kHz. It was verified with simulations that the proposed circuit can also work in the subthreshold region with essentially reduced supply voltages and power dissipation.

## Slide 13: REFERENCE
[1] X. Lai and Z. Lin, “Design and application of allpass filters with equiripple group delay errors,” in Proc. IEEE Int. Symp. Circuits Syst. (ISCAS), May 2013, pp. 2924–2927.
[2] P. Ahmadi, B. Maundy, A. S. Elwakil, L. Belostotski, and A. Madanayake, “A new second-order all-pass filter in 130-nm CMOS,” IEEE Trans. Circuits Syst. II, Exp. Briefs, vol. 63, no. 3, pp. 249–253, Mar. 2016.
[3] J. Vavra, J. Bajer, and D. Biolek, “Differential-input buffered and transconductance amplifier-based all-pass filter and its application in quadrature oscillator,” in Proc. 35th Int. Conf. Telecommun. Signal Process. (TSP), Jul. 2012, pp. 411–415.
[4] S. K. Garakoui, E. A. M. Klumperink, B. Nauta, and F. E. vanVliet, “Frequency limitations of first-order gm –RC all-pass delay circuits,” IEEE Trans. Circuits Syst. II, Exp. Briefs, vol. 60, no. 9, pp. 572–576, Sep. 2013.
[5] P. Ahmadi, M. H. Taghavi, L. Belostotski, and A. Madanayake, “10-GHz current-mode 1st- and 2nd-order allpass filters on 130 nm CMOS,” in Proc. IEEE 56th Int. Midwest Symp. Circuits Syst. (MWSCAS), Aug. 2013, pp. 1–4.

## Slide 14
[6] D. Biolek and V. Biolkova, “Allpass filter employing one grounded capacitor and one active element,” Electron. Lett., vol. 45, no. 16, pp. 807–808, Jul. 2009.
[7] C. Cakir, U. Cam, and O. Cicekoglu, “Novel allpass filter configuration employing single OTRA,” IEEE Trans. Circuits Syst. II, Exp. Briefs, vol. 52, no. 3, pp. 122–125, Mar. 2005.
[8] S. M. Al-Shahrani, “A novel CMOS wideband auto-tuning phase shifter circuit,” in Proc. 14th IEEE Int. Conf. Electron., Circuits Syst., Dec. 2007, pp. 649–652.
[9] A. Toker and S. Ozoguz, “Tunable allpass filter for low voltage operation,” Electron. Lett., vol. 39, no. 2, pp. 175–176, Jan. 2003.
[10] C. Sawigun and P. Pawarangkoon, “A 1.5-V, 300-nW, continuous-time allpass filter With 67 dB dynamic range,” in Proc. 11th Int. Conf. Electr. Eng./Electron., Comput., Telecommun. Inf. Technol. (ECTI-CON), May 2014, pp. 1–4.