## Slide 1: Radiation Hardened 14T SRAM Bitcell With Speed and Power Optimized for Space Applications

## Slide 2: Abstract
In this paper, a novel radiation-hardened 14-transistor SRAM bitcell with speed and power optimized [radiation-hardened with speed and power optimized (RSP)-14T] for space application is proposed. By circuit- and layout-level optimization design in a 65-nm CMOS technology, the 3-D TCAD mixed-mode simulation results show that the novel structure is provided with increased resilience to single-event upset as well as single-event–multiple-node upsets due to the charge sharing among OFF-transistors. Moreover, the HSPICE simulation results show that the write speed and power consumption of the proposed RSP-14T are improved by ∼65% and ∼50%, respectively, compared with those of the radiation hardened design (RHD)-12T memory cell.

## Slide 3: Existing System
In the radiation environment, when the heavy ion is incident on the semiconductor material, the particles will be ionized. These excess charges will be collected by the sensitive nodes of the device.
The charge sharing results in single-event–multiple-node upsets (SEMNUs), which is becoming the main effect of energetic particle strikes in emerging nanometer CMOS technology.
The soft error rate (SER) in SRAM is increased with the technology scaled in the nanometer regime. In order to reduce the SER, numerous alternatives have been proposed to the standard 6T SRAM cell.
The main reinforcement method is through constructing special topology of transistor connections inside cells to achieve circuit-level protection.

## Slide 4: Disadvantage of Existing System
During the write operation, the feedback mechanism will be interrupted easily.
The charge sharing between transistors will be neglected.
To reduce the impact of charge sharing on N2 and N0 when P2 is hit by a particle, they are also moved away from P2.
Low-Power and High-Performance have become a burning issue in VLSI industries these days.

## Slide 5: PROPOSED SYSTEM :
In this paper, we propose the first radiation-hardened static random access memory (SRAM) bitcell targeted at low-voltage functionality, while maintaining high soft-error robustness.
The proposed radiation-hardened bitcell is a pioneer solution for embedded memories in low-power space applications.
Various bitcell designs and architectural techniques have been proposed to enable operation deep into the subthreshold region.
The proposed bitcell is specifically designed to enable robust, low-voltage, ULP operation in space applications and other high-radiation environments.
The proposed 13T bitcell features single-ended readout through the read access transistor (N8).

## Slide 6: ADVANTAGE
During the write operation, the feedback mechanism will not be interrupted easily.
Requires low area.
Due to their static power consumption, scaling the supply voltage of the SRAM macros is an efficient method to reduce total chip power.
The SET is obtained by heavy ions striking on drain of OFF-transistors, and the efficiency of the charge sharing among the OFF-transistors is evaluated by the angle of the hit.
The most efficient way to achieve ULP operation in integrated circuits is to aggressively reduce the supply voltage (VDD) and operate all components of the chip in the near-threshold or subthreshold region, thereby significantly reducing both static and dynamic power consumption.

## Slide 7
TITLE | AUTHOR | DESCRIPTION
Basic mechanisms and modeling of single-event upset in digital microelectronics | P. E. Dodd and L. W. Massengill, | Physical mechanisms responsible for nondestructive single-event effects in digital microelectronics are reviewed, concentrating on silicon MOS devices and integrated circuits.
Physics of multiple-node charge collection and impacts on single-event characterization and soft error rate prediction | J. D. Black, P. E. Dodd, and K. M. Warren, | The impact of multiple-node charge collection on soft error rate prediction is also presented and shows that full circuit prediction is not yet well understood.

## Slide 8
TITLE | AUTHOR | DESCRIPTION
Soft error rate estimation of digital circuits in the presence of multiple event transients (METs) | M. Fazeli, S. N. Ahmadian, S. G. Miremadi, H. Asadi, and M. B. Tahoori, | In this paper, we present a very fast and accurate technique to estimate the soft error rate of digital circuits in the presence of Multiple Event Transients (METs).
Analysis and design of nanoscale CMOS storage elements for single-event hardening with multiple-node upset | S. Lin, Y.-B. Kim, and F. Lombardi, | The occurrence of a single event with a multiple-node upset is likely to increase significantly in nanoscale CMOS due to reduced device size and power supply voltage scaling.

## Slide 9: Block Diagram

## Slide 10: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 11: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 12: CONCLUSION
In this paper, the radiation-hardened 14T SRAM bitcell with speed and power optimized (RSP-14T) based on the source isolation technique is presented. Through the circuit- and layout-level optimization, the mixed-mode simulation results show that it can not only tolerate an SEU on any of its inner single node, but also have partial SEMNUs immune even at the LET value equal to 60 MeV-cm2/mg, which is larger than that reported for RHD-12T. Meanwhile, compared with RHD12T, its write speed and power consumption are significantly improved. Thus, the excepting area increased slightly, and the proposed RSP-14T cell is more suitable for the space application.

## Slide 13: REFERENCE
[1] P. E. Dodd and L. W. Massengill, “Basic mechanisms and modeling of single-event upset in digital microelectronics,” IEEE Trans. Nucl. Sci., vol. 50, no. 3, pp. 583–602, Jun. 2003.
[2] J. D. Black, P. E. Dodd, and K. M. Warren, “Physics of multiple-node charge collection and impacts on single-event characterization and soft error rate prediction,” IEEE Trans. Nucl. Sci., vol. 60, no. 3, pp. 1836–1851, Jun. 2013.
[3] M. Fazeli, S. N. Ahmadian, S. G. Miremadi, H. Asadi, and M. B. Tahoori, “Soft error rate estimation of digital circuits in the presence of multiple event transients (METs) ,” in Proc. IEEE Int. Conf. Design, Automat. Test Eur., Mar. 2011, pp. 70–75.
[4] S. Lin, Y.-B. Kim, and F. Lombardi, “Analysis and design of nanoscale CMOS storage elements for single-event hardening with multiple-node upset,” IEEE Trans. Device Mater. Rel., vol. 12, no. 1, pp. 68–77, Mar. 2012.
[5] E. Ibe, H. Taniguchi, Y. Yahagi, K. Shimbo, and T. Toba, “Impact of scaling on neutron-induced soft error in SRAMs from a 250 nm to a 22 nm design rule,” IEEE Trans. Electron Devices, vol. 57, no. 7, pp. 1527–1538, Jul. 2010.

## Slide 14
[6] R. C. Baumann, “Soft errors in advanced semiconductor devices-part I: The three radiation sources,” IEEE Trans. Device Mater. Rel., vol. 1, no. 1, pp. 17–22, Mar. 2001.
[7] S. M. Jahinuzzaman, D. J. Rennie, and M. Sachdev, “A soft error tolerant 10T SRAM bit-cell with differential read capability,” IEEE Trans. Nucl. Sci., vol. 56, no. 6, pp. 3768–3773, Dec. 2009.
[8] T. Calin, M. Nicolaidis, and R. Velazco, “Upset hardened memory design for submicron CMOS technology,” IEEE Trans. Nucl. Sci., vol. 43, no. 6, pp. 2874–2878, Dec. 1996.
[9] R. Rajaei, B. Asgari, M. Tabandeh, and M. Fazeli, “Design of robust SRAM cells against single-event multiple effects for nanometer technologies,” IEEE Trans. Device Mater. Rel., vol. 15, no. 3, pp. 429–436, Sep. 2015.
[10] J. Guo, L. Xiao, and Z. Mao, “Novel low-power and highly reliable radiation hardened memory cell for 65 nm CMOS technology,” IEEE Trans. Circuits Syst. I, Reg. Papers, vol. 61, no. 7, pp. 1994–2001, Jul. 2014.