## Slide 1: A Nanopower Biopotential Lowpass Filter Using Sub threshold Current-Reuse Biquads With Bulk Effect Self-Neutralization

## Slide 2: Abstract
A nanopower CMOS 4 th -order lowpass filter suitable for biomedical applications is presented. The filter is formed by cascading two types of subthreshold current-reuse biquadratic cell. Each proposed cell is capable of neutralizing the bulk effect that induces the passband attenuation. The nearly 0 dB passband gain can thus be maintained while the entire filter circuit remains compact and power-efficient. Designed for electrocardiogram detection as an example of application, the filter prototype has been fabricated in a 0.35 µm CMOS process occupying 269 µm × 383 µm chip area. Measurements verify that the filter can operate from a 1.5 V single supply and consumes 5.25 nW while providing a cutoff frequency of 100 Hz and input-referred noise of 39.38 μVrms. The intermodulation-free dynamic range of 51.48 dB is obtained from a two-tone test of 50 and 60 Hz input frequencies. Compared with state-of-the-art nanopower lowpass filters using the most relevant and reasonable figure of merit, the proposed filter ranks the best.

## Slide 3: Existing System
The existence of a transmission window, flanking a polariton minimum, extends well into the stable regime.
In this regime, the system demonstrates a stark duality in signal transport, marked by the possibility of achieving both transparency and opacity, for the same set of system parameters.
The greater signal sensitivity and control incorporated by the an harmonicity could be harnessed for the design of photonic devices with optical switching properties.
However, there exists no single allen compassing quantum system capable of holding up to all the requirements and vital performance metrics of a modern day signal-processing network.

## Slide 4: Disadvantage of Existing System
This paper tackles the aforementioned problem by introducing two current-reuse CMOS biquads so that their problems of bulk effect can be neutralized.
We tried to mitigate the mismatch problem by combining common centroid and inter-digitation layout techniques to all current mirror circuits.
The impact of transistor mismatch could be further lowered, applying larger transistor channel sizes, at the cost of silicon area of the filter.
Switched capacitor (SC) filters are not suitable for lowfrequency applications as they suffer from clock feed-through and leakage problems in advanced processes.

## Slide 5: PROPOSED SYSTEM :
The CMOS structure of the proposed filter utilize the bulkdriven technique and operates in subthreshold region to achieve extremely low-voltage supply (0.3V) and nanopower consumption (0.676 nW) for cut-off frequency of 100 Hz.
In this paper we propose a new solution for an ULV ECG filter based on the BD approach.
The filter is a cascade connection of two newly-proposed second-order (biquad) filters, developed from a compact current re-use CMOS buffers.
This idea has been next adopted to signal filtering purposes, in a similar way as described.

## Slide 6: ADVANTAGE
The slope factors of pMOS (np) and nMOS (nn) are slightly different and this can also be another non-ideality affecting the filter performance apart from the bulk effect.
This is in line with the fundamental trade-off in analog design that to achieve low noise performance for a certain fC, we need to sacrifice capacitive area and current consumption.
This represents the standard form of a second-order transfer function with a unity passband gain that can be used for cascade design of a higher-order LPF.
In this design, the bias currents are in the range of a few nanoamperes or below, and all transistors used are largely sized, the flicker noise can be neglected and the shot noise becomes dominant.

## Slide 7
TITLE | AUTHOR | DESCRIPTION
Microelectrodes, microelectronics, and implantable neural microsystems | K. Wise, A. Sodagar, Y. Yao, M. Gulari, G. Perlin, and K. Najafi, | Lithographically defined microelectrode arrays now permit high-density recording and stimulation in the brain and are facilitating new insights into the organization and function of the central nervous system.
The design of integrated circuits to observe brain activity | R. R. Harrison, | The ability to monitor the simultaneous electrical activity of multiple neurons in the brain enables a wide range of scientific and clinical endeavors.

## Slide 8
TITLE | AUTHOR | DESCRIPTION
A 1 V 450 nW fully integrated programmable biomedical sensor interface chip | X. D. Zou, X. Y. Xu, L. B. Yao, and Y. Lian, | This paper presents a fully integrated programmable biomedical sensor interface chip dedicated to the processing of various types of biomedical signals.
On the design and characterization of femtoampere current-mode circuits | B. Linares-Barranco and T. Serrano-Gotarredona, | The technique involves specific-current extractors and logarithmic current splitters for obtaining on-chip subpicoampere currents.

## Slide 9: Block Diagram

## Slide 10: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 11: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 12: CONCLUSION
Theory and design considerations of two compact power-efficient CMOS biquads, and their application to a 4 th -order biopotential LPF filter have been described. The LPF, fabricated in a 0.35 µm CMOS process, provides a near 0 dB passband gain by self-neutralizing the bulk effect without the need for any additional compensation circuit. Compared with other state-of-the-art nanopower LPFs, the proposed filter attains the best FoM1. It can thus be useful for ultra-low-power biomedical signal acquisition.

## Slide 13: REFERENCE
[1] K. Wise, A. Sodagar, Y. Yao, M. Gulari, G. Perlin, and K. Najafi, “Microelectrodes, microelectronics, and implantable neural microsystems,” Proceedings of the IEEE, vol. 96, pp. 1184–1202, Jul. 2008.
[2] R. R. Harrison, “The design of integrated circuits to observe brain activity,” Proceedings of the IEEE, vol. 96, no. 7, pp. 1203-1216, Jul. 2008.
[3] X. D. Zou, X. Y. Xu, L. B. Yao, and Y. Lian, “A 1 V 450 nW fully integrated programmable biomedical sensor interface chip,” IEEE J. Solid-State Circuits, vol. 44, no. 4, pp. 1067-1077, Apr. 2009.
[4] J. G. Webster, Medical Instrumentations: Application and Design, New York: Wiley, 1995.
[5] B. Linares-Barranco and T. Serrano-Gotarredona, “On the design and characterization of femtoampere current-mode circuits,” IEEE Journal of Solid-State Circuits, vol. 38, no. 8, pp. 1353-1363, Aug. 2003.

## Slide 14
[6] C. Sawigun, W. Ngamkham and W. A. Serdijn, “A 0.5-V, 2-nW, 55-dB DR, fourth-order bandpass filter using single branch biquads: An efficient design for FoM enhancement,” Microelectronics Journal, vol. 35, no. 15, pp. 367-374, April 2014.
[7] T.-T. Zhang, P.-I. Mak, M.-I, Vai, P.-U. Mak, M.-K. Law, S.-H. Pun, F. Wan and R. Martins, “15-nW biopotential LPFs in 0.35-µm CMOS using subthreshold-source-follower biquads with and without gain compensation,” IEEE Transactions on Biomedical Circuits and Systems, vol. 7, no. 5, pp. 690-702, Mar. 2013.
[8] S. D’Amico, M. Conta and A. Baschirotto, “A 4.1-mW, 10-MHz, fourth-order source-follower-based continuous-time filter with 79-dB DR,” IEEE J. Solid-State Circuits, pp. 2713-2719, Dec. 2006.
[9] Y. Chen, P. Mak, and Y. Zhou, “Source-follower-based bi-quad cell for continuous-time zero-pole type filters,” in Proc. IEEE International Symposium on Circuits and Systems, Paris, 2010, pp. 3629-3632.
[10] Y. Chen, P. Mak, L. Zhang and Y. Wang, “0.07 mm2 , 2 mW, 75 MHz-IF, fourth-order BPF using source-follower-based resonator in 90 nm CMOS,” IET Electronics Letters, vol. 48, no. 10, pp. 552-554, 10 May 2012.