## Slide 1: Analysis, Comparison, and Experimental Validation of a Class AB Voltage Follower With Enhanced Bandwidth and Slew Rate

## Slide 2: Abstract
This paper describes a bandwidth (BW)- and slew rate (SR)-enhanced class AB voltage follower (VF). A thorough small signal analysis of the proposed and a state-of-the-art AB-enhanced VF is presented to compare their performance. The proposed circuit has 50-MHz BW, 19.5-V/µs SR, and a BW figure of merit of 41.6 (MHz × pF/µW) for CL = 50 pF. It provides 13 times higher current efficiency and 15 times higher BW than the conventional VF with equal 60-µW static power dissipation. The experimental and simulation results of a fabricated test chip in the 130-nm CMOS technology validate the proposed circuit.

## Slide 3: Existing System
Due to the inclusion of cascoding transistor in the feedback path, the proposed FVF cell has an additional advantage of very small variations at node ‘X’ with respect to other existing FVF configurations.
It is evident that the proposed FVF cell offers higher slew rate, wider bandwidth, lesser noise, lower THD than the existing FVF cell.
This trend has been mainly driven by the need to reduce power consumption of the digital circuitry in mixed-mode very large-scale integration (VLSI) systems and to prevent oxide breakdown with decreasing gate-oxide thickness.
In addition, low power consumption and low supply voltages are requirements of the portable electronic equipment market.

## Slide 4: Disadvantage of Existing System
The abilities of the FVF to solve the problems which appear when operating analog and mixed-signal systems with a low voltage supply.
A drawback of this circuit is that current through transistor depends on the output current, so that is not constant and, hence, for resistive loads, the voltage gain is less than unity. A similar problem occurs with capacitive loads at high frequencies.
A possible solution to overcome these problems is to include a dc level shifter between node and the gate of transistor , like in at the cost of increased power consumption, and reduced bandwidth.

## Slide 5: PROPOSED SYSTEM :
The paper proposes a class-AB flipped voltage follower (FVF) cell, in which the bulk-driven transistor is used as an input transistor with a replica-biased scheme to eliminate the DC level shift while a cascoding transistor is used to reduce the output resistance.
The proposed FVF cell has several advantages such as low output resistance, approximately unity voltage gain, high symmetrical slew rate, high current sourcing capability, high current sinking capability and wide bandwidth.
In the proposed FVF cell, the bulk-driven transistor is used to feed the input voltage and the cascoding transistor is used to reduce the output resistance.

## Slide 6: ADVANTAGE
This is related to the SR improvement and the large signal performance of the circuit.
The implementation technology and supply voltage can have a significant effect on the performance of a circuit.
In this paper, the PRP-AB-VF is intended to be used as a buffer for amplifiers.
The advantageous performance parameters of proposed FVF cell such as free from DC level shift, low output resistance, approximately unity voltage gain, high symmetrical slew rate, high current sourcing capability, high current sinking capability and wide bandwidth, make it a suitable building block for low-power and high-speed analog integrated circuits.

## Slide 7
TITLE | AUTHOR | DESCRIPTION
The flipped voltage follower: A useful cell for low-voltage low-power circuit design | R. G. Carvajal et al., | It is evidenced how different versions of this cell, coined as "flipped voltage follower (FVF)" have been used in the past for many applications.
Power-efficient class AB CMOS buffer | A. J. Lopez-Martin, J. Ramirez-Angulo, R. G. Carvajal, and L. Acosta, | It is based on the use of quasi-floating gate (QFG) techniques in a super source follower topology.

## Slide 8
TITLE | AUTHOR | DESCRIPTION
Very low-voltage analog signal processing based on quasi-floating gate transistors | J. Ramirez-Angulo, A. J. Lopez-Martin, R. G. Carvajal, and F. M. Chavero, | A novel design principle for very low-voltage analog signal processing in CMOS technologies is presented. It is based on the use of quasi-floating gate (QFG) MOS transistors.
Design of two-stage class AB CMOS buffers: A systematic approach | A. L. Martin, J. M. A. Miguel, L. Acosta, J. Ramirez-Angulo, and R. G. Carvajal, | A systematic approach for the design of two-stage class AB CMOS unity-gain buffers is proposed.

## Slide 9: Block Diagram

## Slide 10: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 11: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 12: CONCLUSION
A simple modification to a CNV-AB-VF has been shown to significantly improve the positive and negative SRs and the BW, with the same power dissipation and a small additional silicon area with respect to the CNV-VF and the CNV-AB-VF. This has been demonstrated by performing an analytical and experimental comparison of the proposed circuit to the abovementioned VFs. It has been shown that the proposed circuit has the highest global figure of merit of all the VFs reported in the literature. It has 13 times higher current efficiency and 14.8 times higher FOMBW than the CNV-VF with the same power dissipation.

## Slide 13: REFERENCE
[1] R. G. Carvajal et al., “The flipped voltage follower: A useful cell for low-voltage low-power circuit design,” IEEE Trans. Circuits Syst. I, Reg. Papers, vol. 52, no. 7, pp. 1276–1291, Jul. 2005.
[2] A. J. Lopez-Martin, J. Ramirez-Angulo, R. G. Carvajal, and L. Acosta, “Power-efficient class AB CMOS buffer,” Electron. Lett., vol. 45, pp. 89–90, Jan. 2009.
[3] J. Ramirez-Angulo, A. J. Lopez-Martin, R. G. Carvajal, and F. M. Chavero, “Very low-voltage analog signal processing based on quasi-floating gate transistors,” IEEE J. Solid-State Circuits, vol. 39, no. 3, pp. 434–442, Mar. 2004.
[4] A. L. Martin, J. M. A. Miguel, L. Acosta, J. Ramirez-Angulo, and R. G. Carvajal, “Design of two-stage class AB CMOS buffers: A systematic approach,” Etri J., vol. 33, pp. 393–400, Jun. 2011.
[5] M. P. Garde, A. J. Lopez-Martin, and J. Ramirez-Angulo, “Powerefficient class-AB telescopic cascode opamp,” Electron. Lett., vol. 54, no. 10, pp. 620–622, 2018.

## Slide 14
[6] J. Ramirez-Angulo, S. Gupta, R. G. Carvajal, and A. J. Lopez-Martin, “New improved CMOS class AB buffers based on differential flipped voltage followers,” in Proc. IEEE Int. Symp. Circuits Syst., May 2006, pp. 3917-1–3917-4.
[7] C. Sawigun, A. Demosthenous, X. Liu, and W. A. Serdijn, “A compact rail-to-rail class-AB CMOS buffer with slew-rate enhancement,” IEEE Trans. Circuits Syst. II, Exp. Briefs, vol. 59, no. 8, pp. 486–490, Aug. 2012.
[8] G. Xing, S. H. Lewis, and T. R. Viswanathan, “Self-biased unity-gain buffers with low gain error,” IEEE Trans. Circuits Syst. II, Exp. Briefs, vol. 56, no. 1, pp. 36–40, Jan. 2009.
[9] A. J. Lopez-Martin, E. Osés, J. Ramírez-Angulo, and R. G. Carvajal, “Micropower class AB voltage followers with simple quiescent current control,” in Proc. IEEE 55th Int. Midwest Symp. Circuits Syst. (MWSCAS), Aug. 2012, pp. 218–221.
[10] T. C. Carusone, D. Johns, and K. Martin, Analog Integrated Circuit Design, 2nd ed. Hoboken, NJ, USA: Wiley, 2012.