## Slide 1: Design of Area-Efficient and Highly Reliable RHBD 10T Memory Cell for Aerospace Applications

## Slide 2: Abstract
In this brief, based on upset physical mechanism together with reasonable transistor size, a robust 10T memory cell is first proposed to enhance the reliability level in aerospace radiation environment, while keeping the main advantages of small area, low power, and high stability. Using Taiwan Semiconductor Manufacturing Company 65-nm CMOS commercial standard process, simulations performed in Cadence Spectre demonstrate the ability of the proposed radiation-hardened-by-design 10T cell to tolerate both 0 → 1 and 1 → 0 single node upsets, with the increased read/write access time.

## Slide 3: Existing System
The proposed Cell completely hardens DNU whereas the existing cell systems partially hardens DNU. The proposed cell has higher compilation time than the existing cell system.
It can be relieved by cold booting(restarting).In the combinational rationale circuit, when a molecule strikes a delicate node in a rationale door, the gathered charges may cause a transient heartbeat, i.e., a single event transient (SET), at the yield of the struck rationale entryway.
In this manner, the SET heartbeat may spread through the downstream rationale entryways landing at a capacity component, and the beat might be caught, along these lines prompting invalid worth maintenance.

## Slide 4: Disadvantage of Existing System
The most vital issues faced by memories are due to single event upsets (SEUs) which are induced by radiation particles.
Another critical problem is that the speed and stability of SRAM decrease with voltage scaling which has been widely used in ultra-low power (ULP) applications such as implantable medical devices, wireless sensor networks and smart grids.
In the radiation condition, for example, space and atomic blasts, the radiation impact has been one of the fundamental unwavering quality issues of electronic frameworks.
The SRAMs, which are usually used in high speed cache, must cope with the voltage scaling trends to be compatible with the logic.

## Slide 5: PROPOSED SYSTEM :
To overcome multiple event upsets 12T memory cell was proposed and are effectively work in high radiation environments but consumes more power.
The Proposed cell achieves complete SEU and DNU tolerance through feedback and buffering mechanisms among its internal nodes.
The proposed BQCCM10T cell has high robustness and high Read Access time and Write Access Time.
Due to the possibility of SRAM being affected by SEU at ground level and the three limitations mentioned above of applying the near/subthreshold voltage, there is a trend to propose soft error tolerant SRAM cells for highly reliable terrestrial low-voltage applications.

## Slide 6: ADVANTAGE
When the charged particle hits a sensitive node of an integrated circuit, the induced charge along its path can be efficiently collected and accumulated through drift processes.
Soft error robustness with radiation-hardenedby-design (RHBD) techniques is an increasingly important prerequisite in aerospace applications due to the above reasons and more complex cosmic radiation environment, and proposing a novel area-efficient and high-reliability RHBD memory cell is needed.
All of the above RHBD cells are not suitable for aerospace applications in which RHBD memory cells with both area-efficient and highreliability properties are required in order to offer appropriate designfor-reliability systems.

## Slide 7
TITLE | AUTHOR | DESCRIPTION
Impact of scaling on neutron-induced soft error in SRAMs from a 250 nm to a 22 nm design rule | E. Ibe, H. Taniguchi, Y. Yahagi, K.-I. Shimbo, and T. Toba, | The area affected by one nuclear reaction spreads over 1 M bits and bit multiplicity of multi-cell upset become as high as 100 bits and more.
ICARE on-board SAC-C: More than 8 years of SEU and MCU, analysis and prediction | C. Boatella, G. Hubert, R. Ecoffet, and S. Duzellier, | The correlation between SEU rate and the space environment is shown along with the evolution of the geomagnetic cutoff, the geographical dependence of the MBU multiplicity inside the SAA.

## Slide 8
TITLE | AUTHOR | DESCRIPTION
Combined SEU and SEFI protection for memories using orthogonal Latin square codes | A. Sánchez-Macián, P. Reviriego, and J. A. Maestro, | Radiation effects cause several types of errors on memories including single event upsets (SEUs) or single event functional interrupts (SEFIs).
Double node-upset-resilient latch design for nanoscale CMOS technology | A. Yan, Z. Huang, M. Yi, X. Xu, Y. Ouyang, and H. Liang, | The latch comprises three interlocked single-node-upset-resilient cells and each of the cells mainly consists of three mutually feeding back Muller C-elements.

## Slide 9: Block Diagram

## Slide 10: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 11: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 12: CONCLUSION
A novel RHBD 10T cell in TSMC 65-nm CMOS process is proposed in this brief. Compared with previous hardened 10T memory cell, the proposed cell can recover an error in any one sensitive node. The simulation results present that the penalty introduced for the proposed 10T cell is the increased write/read access time that may affect its applications with high-speed requirements. However, when considering the constraints of the target applications, compared with other hardened memory cells, the proposed RHBD 10T cell can be regarded as a good choice for aerospace applications as it provides a good balance among performance, area, power, and reliability for memories working at radiation environment.

## Slide 13: REFERENCE
[1] E. Ibe, H. Taniguchi, Y. Yahagi, K.-I. Shimbo, and T. Toba, “Impact of scaling on neutron-induced soft error in SRAMs from a 250 nm to a 22 nm design rule,” IEEE Trans. Electron Devices, vol. 57, no. 7, pp. 1527–1538, Jul. 2010.
[2] C. Boatella, G. Hubert, R. Ecoffet, and S. Duzellier, “ICARE on-board SAC-C: More than 8 years of SEU and MCU, analysis and prediction,” IEEE Trans. Nucl. Sci., vol. 57, no. 4, pp. 2000–2009, Aug. 2003.
[3] A. Sánchez-Macián, P. Reviriego, and J. A. Maestro, “Combined SEU and SEFI protection for memories using orthogonal Latin square codes,” IEEE Trans. Circuits Syst. I, Reg. Papers, vol. 63, no. 11, pp. 1933–1943, Nov. 2016.
[4] A. Yan, Z. Huang, M. Yi, X. Xu, Y. Ouyang, and H. Liang, “Doublenode-upset-resilient latch design for nanoscale CMOS technology,” IEEE Trans. Very Large Scale Integr. (VLSI) Syst., vol. 25, no. 6, pp. 1978–1982, Jun. 2017.
[5] R. Giterman, L. Atias, and A. Teman, “Area and energy-efficient complementary dual-modular redundancy dynamic memory for space applications,” IEEE Trans. Very Large Scale Integr. (VLSI) Syst., vol. 25, no. 2, pp. 502–509, Feb. 2017.

## Slide 14
[6] R. Bishnoi, F. Oboril, and M. B. Tahoori, “Design of defect and faulttolerant nonvolatile spintronic flip-flops,” IEEE Trans. Very Large Scale Integr. (VLSI) Syst., vol. 25, no. 4, pp. 1421–1432, Feb. 2017.
[7] I.-S. Jung, Y.-B. Kim, and F. Lombardi, “A novel sort error hardened 10T SRAM cells for low voltage operation,” in Proc. IEEE 55th Int. MWSCAS, Aug. 2012, pp. 714–717.
[8] S. M. Jahinuzzaman, D. J. Rennie, and M. Sachdev, “A soft error tolerant 10T SRAM bit-cell with differential read capability,” IEEE Trans. Nucl. Sci., vol. 56, no. 6, pp. 3768–3773, Dec. 2009.
[9] S. Lin, Y.-B. Kim, and F. Lombardi, “A 11-transistor nanoscale CMOS memory cell for hardening to soft errors,” IEEE Trans. Very Large Scale Integr. (VLSI) Syst., vol. 19, no. 5, pp. 900–904, May 2012.
[10] T. Calin, M. Nicolaidis, and R. Velazco, “Upset hardened memory design for submicron CMOS technology,” IEEE Trans. Nucl. Sci., vol. 43, no. 6, pp. 2874–2878, Dec. 1996