## Slide 1: VLSI Design of SVM-Based Seizure Detection System With On-Chip Learning Capability

## Slide 2: Abstract
Portable automatic seizure detection system is very convenient for epilepsy patients to carry. In order to make the system on-chip trainable with high efficiency and attain high detection accuracy, this paper presents a very large scale integration (VLSI) design based on the nonlinear support vector machine (SVM). The proposed design mainly consists of a feature extraction (FE) module and an SVM module. The FE module performs the threelevel Daubechies discrete wavelet transform to fit the physiological bands of the electroencephalogram (EEG) signal and extracts the time–frequency domain features reflecting the nonstationary signal properties. The SVM module integrates the modified sequential minimal optimization algorithm with the table-driven-based Gaussian kernel to enable efficient on-chip learning. The presented design is verified on an Altera Cyclone II field-programmable gate array and tested using the two publicly available EEG datasets. Experiment results show that the designed VLSI system improves the detection accuracy and training efficiency.

## Slide 3: Existing System
The conventional implementation of most classification algorithms is resource intensive such that devices in existence today sacrifice the classification accuracy and latency to meet the power and size constraints.
However, the existing closed-loop neuromodulation devices are too simplistic and lack sufficient on-chip processing and intelligence.
The existing closed-loop devices mainly rely on simple comparison of a pre-selected biomarker (typically from 1 out of 4 channels) against a fixed threshold.
Next-generation closed-loop neuromodulation systems will require significant improvements in the existing devices.

## Slide 4: Disadvantage of Existing System
The impact of multiplication can be substantially less than in typical voltage-based circuits.
However, training classical SVM is solving a quadratic programming (QP) problem which is computationally complex and energy-consuming, so integrating an efficient SVM training algorithm is very important.
Multiplication substantially increases the dynamic range required, which has a severe impact on voltage-based analog circuits.
Moreover, recent studies report the impact of using temporal patterns delivered via multiple contacts in enhancing plasticity and symptom relief , highlighting the benefits of high-channel-count stimulation.

## Slide 5: PROPOSED SYSTEM :
To facilitate a fair comparison and guide design choices among various on-chip classifiers, we propose a new energy-area (E-A) efficiency figure of merit that evaluates hardware efficiency and multi-channel scalability.
The design proposed is an 8-channel closed loop neuromodulation system for DBS, that was verified using stereo-EEG (sEEG) electrodes.
In this work, we propose the Depth-Variant Tree Ensemble (DVTE), a novel low-latency variation of conventional ensemble methods.
We implemented the DVTE classifier in hardware to demonstrate the efficacy of the proposed cost-aware learning approach.

## Slide 6: ADVANTAGE
This paper proposes a VLSI design of nonlinear SVM-based seizure detection system, which integrates the MSMO algorithm and the db4 DWT for achieving efficient on-chip training capability and high detection accuracy.
The proposed detection system has better performance on Specific Dataset than Randomized Dataset in both training efficiency and detection accuracy.
The boundaries are also used to check the optimality of the samples, which avoids the optimality-satisfaction assumption in the SMO algorithm and consequently requires fewer iterations and performs more efficiently on all the benchmark datasets.

## Slide 7
TITLE | AUTHOR | DESCRIPTION
Epileptic seizure prediction and control | L. D. Iasemidis, | This invited paper presents an overview of the application of signal processing methodologies based upon the theory of nonlinear dynamics to the problem of seizure prediction.
Discrete harmony search based expert model for epileptic seizure detection in electroencephalography | T. K. Gandhi, P. Chakraborty, G. G. Roy, and B. K. Panigrahi, | In order to demonstrate the efficacy of the proposed algorithm for classification purpose using PNN, we have implemented 10-fold cross validation.

## Slide 8
TITLE | AUTHOR | DESCRIPTION
Estimation of direction of attention using EEG and out-of-head sound localization | M. Ebisawa, M. Kogure, S.-H. Yano, S. Matsuzaki, and Y. Wada, | Brain-Machine Interfaces (BMIs) are being researched controlling external devices such as robots and computers by measuring the cranial nerve activity of the operator.
Classification of EEG signals by using support vector machines | K. S. Bayram, M. A. Kızrak, and B. Bolat, | In this work, EEG signals were classified by support vector machines to detect whether a subject's planning to perform a task or not.

## Slide 9: Block Diagram

## Slide 10: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 11: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 12: CONCLUSION
A VLSI design for the automatic seizure detection is implemented to enable efficient on-chip learning and improve the detection rate. The architecture of the designed system comprises of a feature extraction module and an SVM module. The feature extraction module decomposes the EEG signal to fit the clinical bands using the three-level Daubechies DWT and yields the mean absolute value and variance of the four DWT coefficients as the time-frequency domain feature vector. The modified sequential minimal optimization algorithm is integrated into the SVM module with the table-driven-based Gaussian kernel to achieve the efficient on-chip training. This system is verified on Altera Cyclone II FPGA using the public EEG datasets, and the experiment results show that the designed VLSI system improves the detection rate and training efficiency.

## Slide 13: REFERENCE
[1] L. D. Iasemidis, “Epileptic seizure prediction and control,” IEEE Trans. Biomed. Eng., vol. 50, no. 5, pp. 549–558, May 2003.
[2] T. K. Gandhi, P. Chakraborty, G. G. Roy, and B. K. Panigrahi, “Discrete harmony search based expert model for epileptic seizure detection in electroencephalography,” Expert Syst. Appl., vol. 39, no. 4, pp. 4055–4062, Mar. 2012.
[3] E. Niedermeyer and F. H. Lopes da Silva, Electroencephalography. Baltimore, MD, USA: Williams & Wilkins, 1993.
[4] M. Ebisawa, M. Kogure, S.-H. Yano, S. Matsuzaki, and Y. Wada, “Estimation of direction of attention using EEG and out-of-head sound localization,” in Proc. 33rd Annu. Int. Conf. IEEE Eng. Med. Biol. Soc., Boston, MA, USA, Aug. 30, 2011, pp. 7417–7421.
[5] K. S. Bayram, M. A. Kızrak, and B. Bolat, “Classification of EEG signals by using support vector machines,” in Proc. IEEE Int. Symp. Innov. Intell. Syst. Appl., 2013, pp. 1–3.

## Slide 14
[6] J. Yoo, L. Yan, D. El-Damak, M. A. Altaf, A. Shoeb, and A. P. Chandrakasan, “An 8-channel scalable EEG acquisition SoC with patientspecific seizure classification and recording processor,” IEEE J. SolidState Circuits, vol. 48, no. 1, pp. 214–228, Jan. 2013.
[7] Y. Song and P. Lio, “A new approach for epileptic seizure detection: ` Sample entropy based feature extraction and extreme learning machine,” J. Biomed. Sci. Eng., vol. 3, no. 4, pp. 556–567, Jun. 2010.
[8] A. Sharmila and P. Geethanjali, “DWT based detection of epileptic seizure from EEG signals using naive Bayes and k-NN classifiers,” IEEE Access, vol. 4, pp. 7716–7727, 2016.
[9] L. Guo, D. Rivero, and A. Pazos, “Epileptic seizure detection using multiwavelet transform based approximate entropy and artificial neural networks,” J. Neurosci. Methods, vol. 193, no. 1, pp. 156–163, Oct. 2010.
[10] M. Li, W. Chen, and T. Zhang, “Classification of epilepsy EEG signals using DWT-based envelope analysis and neural network ensemble,” Biomed. Signal Process. Control, vol. 31, pp. 357–365, Jan. 2017.