## Slide 1: A Real Time FHD Learning Based Super Resolution System Without a Frame Buffer

## Slide 2: Abstract
This brief presents a real-time learning-based superresolution (SR) system without a frame buffer. The system running on an Altera Stratix IV field programmable gate array can achieve output resolution of 1920 × 1080 (FHD) at 60 fps. The proposed architecture performs an anchored neighborhood regression algorithm that generates a high-resolution image from a low-resolution image input using only numbers of line buffers. This real-time system without a frame buffer makes it possible to integrate SR operation into image sensors or display drivers carrying out computational photography and display.

## Slide 3: Existing System
In order to upgrade existing videos without extra storage costs, we propose an FPGA-based super-resolution system that enables real-time Ultra-HD upscaling in high quality.
Our super-resolution system generates a higher resolution video than reported in existing literature, namely 3940×2160 UHD videos from 1920×1080 FHD sources at a frame rate of approximately 30fps on an embedded FPGA board.
The existing super-resolution works and techniques, we proposed a real-time UHD super-resolution solution based on FPGA accelerator.
Many accelerators focus on improving the computational efficiency.

## Slide 4: Disadvantage of Existing System
It is a well-known, ill-posed problem since a single HR image could generate more than one LR image, and it requires enough prior knowledge to reconstruct the highquality HR images.
This problem, learning-based single-image SR methods have achieved outstanding performance and gained state-of-the-art results, by learning from millions of external image patches.
This problem, the proposed SR architecture doubles the operation period in the second stage, and the system is then designed with multiple clock domains.
This fundamentally important problem in image processing and computer vision has become particularly attractive as highdefinition displays dominate the market.

## Slide 5: PROPOSED SYSTEM :
The huge storage expense of UHD content and inspired by the aforementioned state-of-the-art super-resolution techniques, we propose a super-resolution generation solution in real-time with FPGA in this work.
We propose a quantitative model for analysis and optimization to balance the utilization of limited hardware resources, the attainable frame rate, and the visual performance.
Fixed-point precision is used, and a highly pipelined architecture is proposed for the real-time purpose.
Though uniform memory partition strategies are explored in recent publications, e.g.,we adopt the micro-architecture proposed by to decouple the stencil access pattern from the computation.

## Slide 6: ADVANTAGE
The first is a low-frequency interpolation stage, where bicubic interpolation is used for reconstructing the low-frequency parts of HR images.
While one line buffer is used for memory write by the input low resolution image, the other four line buffers are used for memory read to the bicubic kernel.
However, most of these CPU-based methods are far from reaching ideal performance as well as energy efficiency.
FPGA-based accelerators for neural networks are gaining popularity because of its higher energy-efficiency comparing to GPUs and shorter development cycles comparing to ASICs.

## Slide 7
TITLE | AUTHOR | DESCRIPTION
A+: Adjusted anchored neighborhood regression for fast super-resolution | R. Timofte, V. De Smet, and L. Van Gool, | We propose A+, an improved variant of ANR, which combines the best qualities of ANR and SF.
Super-resolution through neighbor embedding | H. Chang, D.-Y. Yeung, and Y. Xiong, | While this formulation resembles other learning-based methods for super-resolution, our method has been inspired by recent manifold teaming methods, particularly locally linear embedding (LLE).

## Slide 8
TITLE | AUTHOR | DESCRIPTION
Nonlinear dimensionality reduction by locally linear embedding | S. T. Roweis and L. K. Saul, | We introduce locally linear embedding (LLE), an unsupervised learning algorithm that computes low-dimensional, neighborhood-preserving embeddings of high-dimensional inputs.
Image super-resolution via sparse representation | J. Yang, J. Wright, T. S. Huang, and Y. Ma, | The effectiveness of such a sparsity prior is demonstrated for both general image super-resolution (SR) and the special case of face hallucination.

## Slide 9: Block Diagram

## Slide 10: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 11: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 12: CONCLUSION
We implement a real-time learning-based regression super resolution system using 128 pre-trained regression functions, which is the first hardware design for such system in the literature, to the best of our knowledge. Most SR algorithms are complicated and often used only on image processing for post-production. This real-time system without a frame buffer makes it possible to integrate SR operation into image sensors or display drivers carrying out computational photography and display. Moreover, this system is applicable to all general regression SR methods by replacing the pre-trained regression functions with those obtained by other algorithms.

## Slide 13: REFERENCE
[1] R. Timofte, V. De Smet, and L. Van Gool, “A+: Adjusted anchored neighborhood regression for fast super-resolution,” in Proc. Asian Conf. Comput. Vis., Singapore, 2014, pp. 111–126.
[2] W. T. Freeman, T. R. Jones, and E. C. Pasztor, “Example-based superresolution,” IEEE Comput. Graph. Appl., vol. 22, no. 2, pp. 56–65, Mar./Apr. 2002.
[3] H. Chang, D.-Y. Yeung, and Y. Xiong, “Super-resolution through neighbor embedding,” in Proc. IEEE Conf. Comput. Vis. Pattern Recognit. (CVPR), Washington, DC, USA, 2004, p. 1.
[4] S. T. Roweis and L. K. Saul, “Nonlinear dimensionality reduction by locally linear embedding,” Science, vol. 290, no. 5500, pp. 2323–2326, 2000.
[5] J. Yang, J. Wright, T. S. Huang, and Y. Ma, “Image super-resolution via sparse representation,” IEEE Trans. Image Process., vol. 19, no. 11, pp. 2861–2873, Nov. 2010.

## Slide 14
[6] R. Zeyde, M. Elad, and M. Protter, “On single image scale-up using sparse-representations,” in Proc. Int. Conf. Curves Surfaces, Avignon, France, 2010, pp. 711–730.
[7] A. Michal, M. Elad, and A. Bruckstein, “The K-SVD: An algorithm for designing overcomplete dictionaries for sparse representation,” IEEE Trans. Signal Process., vol. 54, no. 11, pp. 4311–4322, Nov. 2006.
[8] R. Timofte, V. De Smet, and L. Van Gool, “Anchored neighborhood regression for fast example-based super-resolution,” in Proc. IEEE Int. Conf. Comput. Vis. (ICCV), Sydney, NSW, Australia, 2013, pp. 1920–1927.
[9] S. Schulter, C. Leistner, and H. Bischof, “Fast and accurate image upscaling with super-resolution forests,” in Proc. IEEE Conf. Comput. Vis. Pattern Recognit. (CVPR), Boston, MA, USA, 2015, pp. 3791–3799.
[10] J. Salvador and E. Pérez-Pellitero, “Naive Bayes super-resolution forest,” in Proc. IEEE Int. Conf. Comput. Vis. (ICCV), Santiago, Chile, 2015, pp. 325–333.