## Slide 1: A Single-Ended With Dynamic Feedback Control 8T Sub-threshold SRAM Cell

## Slide 2: Abstract
A novel 8-transistor (8T) static random access memory cell with improved data stability in subthreshold operation is designed. The proposed single-ended with dynamic feedback control 8T static RAM (SRAM) cell enhances the static noise margin (SNM) for ultralow power supply. It achieves write SNM of 1.4× and 1.28× as that of isoarea 6T and read-decoupled 8T (RD-8T), respectively, at 300 mV. The standard deviation of write SNM for 8T cell is reduced to 0.4× and 0.56× as that for 6T and RD-8T, respectively. It also possesses another striking feature of high read SNM ∼2.33×, 1.23×, and 0.89× as that of 5T, 6T, and RD-8T, respectively. The cell has hold SNM of 1.43×, 1.23×, and 1.05× as that of 5T, 6T, and RD-8T, respectively. The write time is 71% lesser than that of single-ended asymmetrical 8T cell. The proposed 8T consumes less write power 0.72×, 0.6×, and 0.85× as that of 5T, 6T, and isoarea RD-8T, respectively. The read power is 0.49× of 5T, 0.48× of 6T, and 0.64× of RD-8T. The power/energy consumption of 1-kb 8T SRAM array during read and write operations is 0.43× and 0.34×, respectively, of 1-kb 6T array. These features enable ultralow power applications of 8T.

## Slide 3: Existing System
The power consumption can be minimized by using nonconventional device structures, new circuit topologies and optimizing the various architectures.
The portable microprocessor controlled devices contain embedded memory which represents an extensive part of the system on chip (SoC).
Ultra-low power on chip memory is now mandatory to achieve higher reliability and longer battery life for handheld devices.
The SEDFC enables writing through single nMOS in 8T and it also separates the read and write path.

## Slide 4: Disadvantage of Existing System
The data stability of SRAM cell is a severe problem and worsens with the scaling of MOSFET to sub nanometer technology.
The basic and an effective way to eliminate this problem is the decoupling of true storing node from the bit lines during the read operation.
Another problem is to obtain optimized noise margin against process variations at all operations.
Although, voltage scaling has led to circuit operation in subthreshold regime with minimum power consumption, but there is a disadvantage of exponential reduction in performance.

## Slide 5: PROPOSED SYSTEM :
The proposed single finished with dynamic criticism control 8T static RAM (SRAM) cell improves the static commotion edge (SNM) for ultralow control supply.
Due to the design constraints and contact area between M2, M3, M4, and M8 for proposed 8T, there is 2× area overhead as compared with 6T cell.
The proposed 8T cell has high stability and can be operated at ULV of 200–300 mV power supplies.
The advantage of reduced power consumption of the proposed 8T cell enables it to be employed for battery operated SoC design.

## Slide 6: ADVANTAGE
The single-ended design is used to reduce the differential switching power during read–write operation.
A separate read bit line (RBL) is used to transfer the data from cell to the output when read word line (RWL) is activated. Input data and column address signals are used to generate these control signals.
A common circuit is used for a single column, therefore, there would be a small area overhead at array level.
An 8T-SRAM cell using Adoptive Voltage Level Ground (AVLG) technique with better performance, low power consumption and less leakage power has been implemented.

## Slide 7
TITLE | AUTHOR | DESCRIPTION
Low-Power CMOS VLSI Circuit Design | K. Roy and S. Prasad, | Low-power VLSI circuit design is a dynamic research area driven bythe growing reliance on battery-powered portable computing andwireless communications products.
Ultra-low power sub-threshold SRAM cell design to improve read static noise margin | C. Kushwah and S. K. Vishvakarma, | In this paper, we give a deep insight of sub-threshold SRAM cell design issues and discuss several important circuit techniques.

## Slide 8
TITLE | AUTHOR | DESCRIPTION
A 256-kb 65-nm sub-threshold SRAM design for ultra-low-voltage operation | B. H. Calhoun and A. P. Chandrakasan, | Low-voltage operation for memories is attractive because of lower leakage power and active energy, but the challenges of SRAM design tend to increase at lower voltage.
A 160 mV robust Schmitt trigger based subthreshold SRAM | J. P. Kulkarni, K. Kim, and K. Roy, | It utilizes differential operation and hence does not require any architectural changes from the present 6T architecture.

## Slide 9: Block Diagram

## Slide 10: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 11: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 12: CONCLUSION
An 8T SRAM cell with high data stability (high μ and low σ ) that operates in ULV supplies is presented. We attained enhanced SNM in subthreshold regime using SE-DFC and read decoupling schemes. The proposed cell’s area is twice as that of 6T. Still, it’s better built-in process tolerance and dynamic voltage applicability enables it to be employed similar to cells (8T, 9T, and 10T) along with 1.8 × −2× area overhead. The proposed 8T cell has high stability and can be operated at ULV of 200–300 mV power supplies. The advantage of reduced power consumption of the proposed 8T cell enables it to be employed for battery operated SoC design. Future and applications of the proposed 8T cell can potentially be in low/ULV and medium frequency operation like neural signal processor, subthreshold processor, wide-operating-range IA-32 processor, fast Fourier transform core, and low voltage cache operation.

## Slide 13: REFERENCE
[1] K. Roy and S. Prasad, Low-Power CMOS VLSI Circuit Design, 1st ed. New York, NY, USA: Wiley, 2000.
[2] N. Verma and A. P. Chandrakasan, “A 256 kb 65 nm 8T subthreshold SRAM employing sense-amplifier redundancy,” IEEE J. Solid-State Circuits, vol. 43, no. 1, pp. 141–149, Jan. 2008.
[3] C. Kushwah and S. K. Vishvakarma, “Ultra-low power sub-threshold SRAM cell design to improve read static noise margin,” in Progress in VLSI Design and Test (Lecture Notes in Computer Science), vol. 7373. Berlin, Germany: Springer-Verlag, 2012, pp. 139–146.
[4] B. H. Calhoun and A. P. Chandrakasan, “A 256-kb 65-nm sub-threshold SRAM design for ultra-low-voltage operation,” IEEE J. Solid-State Circuits, vol. 42, no. 3, pp. 680–688, Mar. 2007.
[5] C. B. Kushwah, D. Dwivedi, and N. Sathisha, “8T based SRAM cell and related method,” U.S. Patent IN920 130 218 US1, May 30, 2013.

## Slide 14
[6] J. P. Kulkarni, K. Kim, and K. Roy, “A 160 mV robust Schmitt trigger based subthreshold SRAM,” IEEE J. Solid-State Circuits, vol. 42, no. 10, pp. 2303–2313, Oct. 2007.
[7] C.-H. Lo and S.-Y. Huang, “P-P-N based 10T SRAM cell for lowleakage and resilient subthreshold operation,” IEEE J. Solid-State Circuits, vol. 46, no. 3, pp. 695–704, Mar. 2011.
[8] I. Carlson, S. Andersson, S. Natarajan, and A. Alvandpour, “A high density, low leakage, 5T SRAM for embedded caches,” in Proc. 30th Eur. Solid-State Circuits Conf., Sep. 2004, pp. 215–218.
[9] B. Zhai, S. Hanson, D. Blaauw, and D. Sylvester, “A variation-tolerant sub-200 mV 6-T subthreshold SRAM,” IEEE J. Solid-State Circuits, vol. 43, no. 10, pp. 2338–2348, Oct. 2008.
[10] S. A. Tawfik and V. Kursun, “Low power and robust 7T dual-Vt SRAM circuit,” in Proc. IEEE Int. Symp. Circuits Syst., May 2008, pp. 1452– 1455.