## Slide 1: Low-Power Variation-Tolerant Nonvolatile Lookup Table Design

## Slide 2: Abstract
Emerging nonvolatile memories (NVMs), such as MRAM, PRAM, and RRAM, have been widely investigated to replace SRAM as the configuration bits in field-programmable gate arrays (FPGAs) for high security and instant power ON. However, the variations inherent in NVMs and advanced logic process bring reliability issue to FPGAs. This brief introduces a low-power variation-tolerant nonvolatile lookup table (nvLUT) circuit to overcome the reliability issue. Because of large ROFF/RON , 1T1R RRAM cell provides sufficient sense margin as a configuration bit and a reference resistor. A single-stage sense amplifier with voltage clamp is employed to reduce the power and area without impairing the reliability. Matched reference path is proposed to reduce the parasitic RC mismatch for reliable sensing. Evaluation shows that 22% reduction in delay, 38% reduction in power, and the tolerance of variations of 2.5× typical RON or ROFF in reliability are achieved for proposed nvLUT with six inputs.

## Slide 3: Existing System
In existing system Magneto resistive random access memory(MRAM) is used as configuration bit.
Configuration bits are received in serially from external memory in the power down case, then data will be loss in this case.
In order to use this memory the inconsistency has been introduced in the implementation of look up table.
However, nvSRAM substantially larger than the cell size of the SRAM, and the writing half of the selected disturbance RRAM cells is also difficult to avoid.
However, MRAM's ROFF / RON small PRAM or RRAM, the serial / parallel magnetic junctions, seems low compared to the margin, or as a result of a large area.

## Slide 4: Disadvantage of Existing System
The problem can be solved by introducing nonvolatile memory (NVM) as the configuration bit.
A low-power variation-tolerant nvLUT circuit to overcome the issues in the previous work.
To resolve this issue, dummy RRAM cell, which is programmed to a mid-state resistance, is adopted as the reference resistor.
The resistance state of MRAM (Magneto resistive random access memory) is small compare with RRAM to store the data in the form of resistance state in storage cell of a MRAM ,thus resulting in larger area due to serial parallel magnetic junctions.

## Slide 5: PROPOSED SYSTEM :
Proposed system will be random access memory (resistive RAM structure of a storage cell.
RRAM cell is employed as a configuration bit to provide sufficient sense margin .
Based on the logic in memory concept that is look up table design, which is the core building block in FPGAs, has been proposed with non volatility.
However, the size of non volatile SRAM cell is remarkably larger than that of SRAM, and the write disturbance is also difficult to avoid for half-select RRAM cells, and also proposed eight input LUT.

## Slide 6: ADVANTAGE
SRAM-based field-programmable gate arrays (FPGAs) have been widely used during the last decades.
Because of its large ROFF/RON, 1T1R RRAM cell is used as a configuration bit and a reference resistor to provide sufficient sense margin against memory and logic variations.
RRAM(Resistive random access memory)has larger Roff/Ron(Resistance state) ratio to store the data in their storage cell .
RRAM cell has been used as the configuration bit in proposed and a reference resistor as been used to provide sufficient sense margin to read and write data.
The area cost is decreased because no serial and parallel memory cell combinations are needed.

## Slide 7
TITLE | AUTHOR | DESCRIPTION
Reproducible resistance switching in polycrystalline NiO films | S. Seo et al., | Negative resistance behavior and reproducible resistance switching were found in polycrystalline NiO films deposited by dc magnetron reactive sputtering methods.
Trends on the application of emerging nonvolatile memory to processors and programmable devices | L. Torres, R. M. Brum, L. V. Cargnini, and G. Sassatelli, | In this paper, we present an overview and current status of these logic circuits and discuss their potential applications in this field.

## Slide 8
TITLE | AUTHOR | DESCRIPTION
A novel CuxSiyO resistive memory in logic technology with excellent data retention and resistance distribution for embedded applications | M. Wang et al., | The activation energy of Cu vacancy migration in Cu x Si y O increases by 5 times than that in Cu x O, giving rise to the great performance improvement.
Nonvolatile SRAM cell based on CuxO | X. Xue et al., | A nonvolatile static random access memory (NVSRAM) cell with two back-up Cu x O memory devices is proposed in this paper.

## Slide 9: Block Diagram

## Slide 10: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 11: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 12: CONCLUSION
The design techniques of low-power variation-tolerant nvLUT are described in this brief. RRAM is adopted as the configuration bit and the reference resistor to provide large sense margin, thus alleviating the effects of memory and logic process variations. Because of the high ROFF/RON of RRAM, SSAVC helps to reduce the power and area without impairing the reliability. The MRP is also devised to reduce the parasitic RC mismatch between the selected path in the multiplexer and the reference path for reliable operation. By evaluation, remarkable improvements in power, delay, area, and reliability are achieved.

## Slide 13: REFERENCE
[1] S. D. Brown, R. J. Francis, J. Rose, and Z. G. Vranesic, FieldProgrammable Gate Arrays. Boston, MA, USA: Kluwer, 1992.
[2] S. Seo et al., “Reproducible resistance switching in polycrystalline NiO films,” Appl. Phys. Lett., vol. 85, no. 23, pp. 5655–5657, 2004.
[3] L. Torres, R. M. Brum, L. V. Cargnini, and G. Sassatelli, “Trends on the application of emerging nonvolatile memory to processors and programmable devices,” in Proc. IEEE Int. Symp. Circuits Syst. (ISCAS), May 2013, pp. 101–104.
[4] M. Wang et al., “A novel CuxSiyO resistive memory in logic technology with excellent data retention and resistance distribution for embedded applications,” in Proc. Symp. VLSI Technol. (VLSIT), Jun. 2010, pp. 89–90.
[5] X. Xue et al., “Nonvolatile SRAM cell based on CuxO,” in Proc. 9th Int. Conf. Solid-State Integr.-Circuit Technol. (ICSICT), Oct. 2008, pp. 869–871.

## Slide 14
[6] N. Bruchon, L. Torres, G. Sassatelli, and G. Cambon, “Technological hybridization for efficient runtime reconfigurable FPGAs,” in Proc. IEEE Comput. Soc. Annu. Symp. VLSI (ISVLSI), Mar. 2007, pp. 29–34.
[7] W. Zhao, E. Belhaire, B. Dieny, G. Prenat, and C. Chappert, “TAS-MRAM based non-volatile FPGA logic circuit,” in Proc. Int. Conf. Field-Program. Technol. (ICFPT), Dec. 2007, pp. 153–160.
[8] D. Suzuki et al., “Fabrication of a nonvolatile lookup-table circuit chip using magneto/semiconductor-hybrid structure for an immediatepower-up field programmable gate array,” in Proc. Symp. VLSI Circuits (VLSIC), Jun. 2009, pp. 80–81.
[9] D. Suzuki, M. Natsui, T. Endoh, H. Ohno, and T. Hanyu, “Six-input lookup table circuit with 62% fewer transistors using nonvolatile logicin-memory architecture with series/parallel-connected magnetic tunnel junctions,” J. Appl. Phys., vol. 111, no. 7, pp. 07E318-1–07E318-3, 2012.
[10] W. Zhao, E. Belhaire, C. Chappert, and P. Mazoyer, “Power and area optimization for run-time reconfiguration system on programmable chip based on magnetic random access memory,” IEEE Trans. Magn., vol. 45, no. 2, pp. 776–780, Feb. 2009.