## Slide 1: Probability Driven Multibit Flip-Flop Integration with Clock Gating

## Slide 2: Abstract
Data-driven clock gated (DDCG) and multibit flip-flops (MBFFs) are two low-power design techniques that are usually treated separately. Combining these techniques into a single grouping algorithm and design flow enables further power savings. We study MBFF multiplicity and its synergy with FF data-to-clock toggling probabilities. A probabilistic model is implemented to maximize the expected energy savings by grouping FFs in increasing order of their data-to-clock toggling probabilities. We present a front-end design flow, guided by physical layout considerations for a 65-nm 32-bit MIPS and a 28-nm industrial network processor. It is shown to achieve the power savings of 23% and 17%, respectively, compared with designs with ordinary FFs. About half of the savings was due to integrating the DDCG into the MBFFs.

## Slide 3: Existing System
In existing system power reduction is achieved by using clock gating.
With clock gating, the Clock signals are multiply with an AND gate logic to explicitly predefined enabling signal. But this clock gating still leaves large number of redundant clock pulses.
Although substantially increasing design productivity, such tools require the employment of a long chain of automatic synthesis algorithms, from register transfer level (RTL) down to gate level and net list.
Development of automatic and effective methods to reduce this inefficiency is desirable. In the sequel, we will use the terms toggling, switching, and activity interchangeably.

## Slide 4: Disadvantage of Existing System
The 2-MBFF merging is formulated as an optimization problem that aims at maximizing the number of merged FFs.
Using toggling correlations for MBFF grouping has the drawback of requiring early knowledge of the value change dump vectors of a typical workload.
That issue for Flip Flops combining yields maximum toggling0correlation, and consequently maximal power0savings, has been demonstrated as0NP-hard.
Its drawback is the requirement of early knowledge of Value Change Dump (VCD) vectors, derived from many power simulations representing the typical operation and applications of the design in hand.

## Slide 5: PROPOSED SYSTEM :
Our work proposes a systematic, toggling probability-driven MBFF grouping algorithm, provably maximizing the expected energy savings.
The proposed MBFF design flow has been used for a 32-bit pipelined MIPS processor, implemented in TSMC 65nm process technology.
In an attempt to reduce the overhead, it is proposed to group several FFs to be driven by the same clock signal, generated by bring the enabling signals of the individual FFs.
Multi-bit Flip-Flop method is to eliminate the total inverter number by sharing the inverters in the flip-flops. Data driven clock gating reduce redundant clock pulses.

## Slide 6: ADVANTAGE
MBPL clock power was minimized by taking advantage of pulsed-latch timing behavior that is similar to a FF, and its time-borrowing capabilities similar to a latch.
More common information is the average toggling bulk probability of each FF in the design, which the following discussion takes advantage of in deriving an optimal toggling probability-driven FFs grouping.
A power savings model utilizing MBFF multiplicities and FF toggling probabilities is developed, which was then used by the algorithm in a practical design flow.
The FF clustering approach presented in has later been used in for replacement of 1-bit FF with Multi-Bit Pulsed-Latch (MBPL) in the physical layout.

## Slide 7
TITLE | AUTHOR | DESCRIPTION
Digital systems power management for high performance mixed signal platforms | A. Kapoor et al., | In this paper we present an overview of low power design techniques, challenges and opportunities faced in an industrial research environment.
The optimal fan-out of clock network for power minimization by adaptive gating | S. Wimer and I. Koren, | In this paper we develop a probabilistic model of the clock gating network that allows us to quantify the expected power savings and the implied overhead.

## Slide 8
TITLE | AUTHOR | DESCRIPTION
Multi-bit flipflop usage impact on physical synthesis | C. Santos, R. Reis, G. Godoi, M. Barros, and F. Duarte, | Reducing clock network power is an efficient way to reduce power consumption of the high-frequency ASICs since it accounts for a considerable amount of the dynamic chip power.
Pulsed-latch replacement using concurrent time borrowing and clock gating | C. L. Chang and I. H. R. Jiang, | Flip-flops are the most common form of sequencing elements; however, they have a significantly higher sequencing overhead than latches in terms of delay, power, and area.

## Slide 9: Block Diagram

## Slide 10: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 11: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 12: CONCLUSION
This brief suggests combining MBFFs and probability-driven CG to increase their power savings. A model utilizing the relationship between the optimal MBFF multiplicities to FF data-to-clock toggling probabilities is used in a practical design flow, achieving 17% and 23% power savings, compared with designs with ordinary FFs. About half of these savings can be attributed to the integration of DDCG into MBFFs.

## Slide 13: REFERENCE
[1] A. Kapoor et al., “Digital systems power management for high performance mixed signal platforms,” IEEE Trans. Circuits Syst. I, Reg. Papers, vol. 61, no. 4, pp. 961–975, Apr. 2014.
[2] S. Wimer and I. Koren, “The optimal fan-out of clock network for power minimization by adaptive gating,” IEEE Trans. VLSI Syst., vol. 20, no. 10, pp. 1772–1780, Oct. 2012.
[3] C. Santos, R. Reis, G. Godoi, M. Barros, and F. Duarte, “Multi-bit flipflop usage impact on physical synthesis,” in Proc. 25th IEEE Symp. Integr. Circuits Syst. Design (SBCCI), Sep. 2012, pp. 1–6.
[4] J.-T. Yan and Z.-W. Chen, “Construction of constrained multi-bit flipflops for clock power reduction,” in Proc. IEEE Int. Conf. Green Circuits Syst. (ICGCS), 2010, pp. 675–678.
[5] IH-R. Jiang, C-L. Chang, and Y-M. Yang, “INTEGRA: Fast multibit flip-flop clustering for clock power saving,” IEEE Trans. CAD Integr. Circuits Syst., vol. 31, no. 2, pp. 192–204, Feb. 2012.

## Slide 14
[6] C. L. Chang and I. H. R. Jiang, “Pulsed-latch replacement using concurrent time borrowing and clock gating,” IEEE Trans. Comput.- Aided Design Integr., vol. 32, no. 2, pp. 242–246, Feb. 2013.
[7] M. P.-H. Lin, C-C. Hsu, and Y-T. Chang, “Post-placement power optimization with multi-bit flip-flops,” IEEE Trans. CAD Integr. Circuits Syst., vol. 30, no. 12, pp. 1870–1882, Dec. 2011.
[8] Y.-T. Shyu, J.-M. Lin, C.-P. Huang, C.-W. Lin, Y.-Z. Lin, and S.-J. Chang, “Effective and efficient approach for power reduction by using multi-bit flip-flops,” IEEE Trans. VLSI Syst., vol. 21, no. 4, pp. 624–635, Apr. 2013.
[9] S. Liu, W.-T. Lo, C.-J. Lee, and H.-M. Chen, “Agglomerative-based flip-flop merging and relocation for signal wirelength and clock tree optimization,” ACM Trans. Design Autom. Electron. Syst., vol. 18, no. 3, article no. 40, Jul. 2013.
[10] M. P. H. Lin, C. C. Hsu, and Y. C. Chen, “Clock-tree aware multibit flip-flop generation during placement for power optimization,” IEEE Trans. Comput.-Aided Design Integr., vol. 34, no. 2, pp. 280–292, Feb. 2015.