## Slide 1: A Process-Tolerant, Low-Voltage, Inverter-Based OTA for Continuous-Time, ADC

## Slide 2: Abstract
Inverter-based implementation of operational transconductance amplifiers is an attractive approach for lowvoltage realization of analog subsystems. However, the high sensitivity of inverter like amplifiers’ performance to process and temperature variations limit the achievable performance of the whole system across process and temperature corners. In this paper, a tuning technique is proposed to maintain the inverter based amplifier performance across the process and temperature corners without requiring additional voltage headroom than that required by the inverter circuit. The introduced technique is used to implement a third-order continuous-time sigma–delta (–) analog-to-digital converter (ADC). The main building block of the implemented ADC is an inverter-based amplifier. This makes the resulting – ADC easier to scale to different technology nodes. A 74-dB signal-to-noise and distortion ratio is achieved, for a signal bandwidth of 64 kHz at a sampling frequency of 6.4 MHz, while consuming 400 μA from a 0.8 V supply in 65-nm CMOS technology.

## Slide 3: Existing System
Existing strategies to compensate PVT variations increase the OTAs design complexity, and the development of new compensation strategies is an open research field.
Existing techniques for the design of inverter-based amplifiers are analyzed and used as a starting point to develop novel amplifier topologies.
One must determine the NTF of the modulator and map the NTF to one of the existing SDM architectures.
The CT-SDMs intrinsic anti-alias filter ceases to exist because the input signal is applied directly to the input of the quantizer and is not filtered by the low-pass filter of the modulator.

## Slide 4: Disadvantage of Existing System
A main disadvantage of operating the inverter as an amplifier is the high variation of the inverter dc gain and gain bandwidth (GBW), with temperature and process corners.
A reduction in the dc gain of an amplifier directly impacts the performance of continuous time (CT) sigma–delta (–) analog-to-digital converter (ADC) by raising the noise floor, which consequently degrades the signal-to-noise ratio.
However, high-order modulators are conditionally stable and instability problems can arise in modulators with no proper coefficient scaling.
The loop filter integrators should present reduced output swing to minimize linearity issues.

## Slide 5: PROPOSED SYSTEM :
The proposed architecture has been validated by designing OTAs in 180 nm standard CMOS process for operation on 1.8 V supply.
A 1-bit third order DTDSM has been designed using the second OTA to prove that the proposed design fits well for SC applications.
This research proposes an architecture for inverter-based OTA to realize high DC gain while keeping the quiescent current to a low value.
The proposed IGB-OTA can easily achieve a DC gain in excess of 90 dB with careful sizing and biasing of transistors.
The performance of the proposed OTA is also compared with OTA’s operating on lower supply voltage and it is presented.

## Slide 6: ADVANTAGE
The proposed circuit is used to build a CT – ADC, and the worst case performance across the process and temperature variations is reported.
This input level, the performance of the modulator degrades, as the second and third harmonics contribution becomes relatively high, and effectively raises the modulator overall noise floor.
The achieved performance is compared with prior art measurements, only to show how this paper may fit within the state of the art.
The mapped coefficients are selected to maintain a stable operation of the ADC for specific input ranges.
All loop filters coefficients are scaled to obtain a reasonable signal swing at the integrators outputs and the comparator input.

## Slide 7
TITLE | AUTHOR | DESCRIPTION
A 0.6-to-1 V inverter-based 5-bit flash ADC in 90 nm digital CMOS | J. E. Proesel and L. T. Pileggi, | The comparators are designed for compatibility with nanoscale CMOS lithography.
A low voltage inverter-based continuous-time sigma delta analog-to-digital converter in 65 nm CMOS technology | A. Essawy and A. Ismail, | In this work an inverted-based low-voltage implementation for continuous-time sigma delta analog-to-digital converters is proposed.

## Slide 8
TITLE | AUTHOR | DESCRIPTION
A 0.9 V 1.5 mW continuous-time modulator for WCDMA | T. Ueno and T. Itakura, | Inverter-based balanced OTAs without using differential pair are proposed for a low-voltage operation.
A CMOS transconductance-C filter technique for very high frequencies | B. Nauta, | This integrator has good linearity properties and nondominant poles in the gigahertz range owing to the absence of internal nodes.

## Slide 9: Block Diagram

## Slide 10: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 11: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 12: CONCLUSION
In this paper, a low-voltage inverter-based OTA with robust operation across the process corners is proposed. The proposed OTA employs a tuning circuit that controls the inverter structure output CM voltage and maintains the OTA dc gain across the process and temperature corners. The tuning circuit is built, such that it does not stack any devices to the simple inverter structure, and therefore, the OTA achieves a low-voltage operation. A third-order CT – modulator is implemented using the proposed tunable OTA. The main building block of the implemented modulator is an inverter-based amplifier, and therefore, the modulator is scaling friendly. The modulator achieves an SNDR of 74 dB and a worst corner SNDR of 70 dB. The modulator circuitry runs from a low supply voltage of 0.8 V and consumes 320 μW in 65-nm CMOS technology.

## Slide 13: REFERENCE
[1] J. E. Proesel and L. T. Pileggi, “A 0.6-to-1 V inverter-based 5-bit flash ADC in 90 nm digital CMOS,” in Proc. IEEE Custom Integr. Circuits Conf. (CICC), Sep. 2008, pp. 153–156.
[2] S. Zeller, C. Muenker, R. Weigel, and U. Ussmueller, “A 0.039 mm2 inverter-based 1.82 mW 68.6 dB-SNDR 10 MHz-BW CT--ADC in 65 nm CMOS using power- and area-efficient design techniques,” IEEE J. Solid-State Circuits, vol. 49, no. 7, pp. 1548–1560, Jul. 2014.
[3] A. Essawy and A. Ismail, “A low voltage inverter-based continuous-time sigma delta analog-to-digital converter in 65 nm CMOS technology,” in Proc. IEEE Faible Tension Faible Consommation (FTFC), May 2014, pp. 1–4.
[4] T. Ueno and T. Itakura, “A 0.9 V 1.5 mW continuous-time modulator for WCDMA,” in IEEE Int. Solid-State Circuits Conf. Dig. Tech. Papers (ISSCC), Feb. 2004, pp. 78–79.
[5] K.-P. Pun, S. Chatterjee, and P. R. Kinget, “A 0.5-V 74-dB SNDR 25-kHz continuous-time delta-sigma modulator with a return-to-open DAC,” IEEE J. Solid-State Circuits, vol. 42, no. 3, pp. 496–507, Mar. 2007.

## Slide 14
[6] J. Zhang, Y. Lian, L. Yao, and B. Shi, “A 0.6-V 82-dB 28.6-μW continuous-time audio delta-sigma modulator,” IEEE J. Solid-State Circuits, vol. 46, no. 10, pp. 2326–2335, Oct. 2011.
[7] B. Nauta, “A CMOS transconductance-C filter technique for very high frequencies,” IEEE J. Solid-State Circuits, vol. 27, no. 2, pp. 142–153, Feb. 1992.
[8] R. Schreier and G. C. Temes, Understanding Delta-Sigma Data Converters. New York, NY, USA: Wiley, 2005.
[9] M. Ortmanns and F. Gerfers, Continuous-Time Sigma-Delta A/D Conversion: Fundamentals, Performance Limits and Robust Implementations. Heidelberg, Germany: Springer-Verlag, 2005.
[10] J. A. Cherry and W. M. Snelgrove, “Excess loop delay in continuoustime delta-sigma modulators,” IEEE Trans. Circuits Syst. II, Analog Digit. Signal Process., vol. 46, no. 4, pp. 376–389, Apr. 1999.