## Slide 1: A Single-Stage Low-Dropout Regulator With a Wide Dynamic Range for Generic Applications

## Slide 2: Abstract
Single-stage regulator topologies are often preferred in embedded applications due to their low power consumption with a single-pole behavior, resulting in easy frequency compensation. Since the achievable differential gain from a single stage is low, the dc load regulation is poor over a wide dynamic range. This paper presents a single-stage, adaptively biased, low-dropout regulator to achieve a comparable dc load regulation similar to multistage topologies. This is achieved mainly by modifying the adaptive bias loop which amplifies both the common-mode and differential-mode signals. In addition, as the proposed regulator is stable for a wide range of output capacitors, including the capacitor-less (on-chip) and with-capacitor (off-chip) conditions, it is suitable for more generic applications. The proposed regulator is implemented in a standard 0.18-µm CMOS technology. The experimental results show that the regulator is capable of delivering up to 100 mA with a dc load regulation of 0.140 mV/mA and is stable with Co ≤ 3.3 nF (capacitor-less) and Co ≥ 1 µF (with-capacitor).

## Slide 3: Existing System
Several techniques for generating accurate output currents exist. The simplest uses a single resistor in the ground return lead.
Several options exist for the desktop computer system designer.
Another is to use the existing high current 5V supply and employ a low dropout (LDO) linear regulator to provide 3.3V.
The heat sink should be mounted so that at least 0.25 inches (about 6mm) of separation exists between the sides and top of the sink and other components or the system case.
Existence of a shorted output is continually monitored; the system will protect the pass device for an indefinite time.

## Slide 4: Disadvantage of Existing System
The key issue of developing a generic LDO topology is the tradeoff between the dc accuracy and the loop stability.
The only way to mitigate this issue is to increase the size of the pMOS power transistor.
The simplest, lowest cost solution for this problem is the modern, very low dropout version of the venerable linear regulator.
This circuit has a number of problems, including poor stability (a large output capacitor is required to squelch oscillations), poor current limiting characteristics, poor load transient response, no over temperature shutdown protection, and requires numerous external components.

## Slide 5: PROPOSED SYSTEM :
A low-dropout regulator (LDO) with 800 mA load current with wide range input voltage is designed and proposed in this paper.
The proposed regulator is stable for a wide range of logics with variable capacitors and also for the capacitor-less conditions.
The stability of the proposed LDO regulator is achieved by three diferent compensation techniques including Miller, cascode, and Q-reduction.
The load and line transient responses of the proposed LDO regulator are simulated to verify the stability and evaluate the transient performance.
It is worth mentioning that the proposed regulator consumes only a quiescent current of 1.83 µA at small load current.

## Slide 6: ADVANTAGE
Based on the critical dynamic performance requirement of different blocks, one may need multiple instances of both the categories in a single chip.
The different performance metrics vary widely in various applications based on their input–output voltage/current ranges, compensation strategy, adopted technology for implementation, and so on.
Therefore, a figure of merit (FOM) may reasonably reflect the tradeoff performance but does not universally hold good.
Due to the unavailability of the other performance parameters, we are not in a position to compare them.
Moreover, the proposed regulator consumes a lowquiescent current at no-load condition without significantly degrading the current efficiency ηc at maximum load current.

## Slide 7
TITLE | AUTHOR | DESCRIPTION
Area-efficient linear regulator with ultra-fast load regulation | P. Hazucha, T. Karnik, B. A. Bloechel, C. Parsons, D. Finan, and S. Borkar, | We demonstrate a fully integrated linear regulator for multisupply voltage microprocessors implemented in a 90 nm CMOS technology.
A 6-μW chip-area-efficient output capacitorless LDO in 90-nm CMOS technology | J. Guo and K. N. Leung, | An output-capacitorless low-dropout regulator (LDO) compensated by a single Miller capacitor is implemented in a commercial 90-nm CMOS technology.

## Slide 8
TITLE | AUTHOR | DESCRIPTION
A 0.9 V 0.35 μm adaptively biased CMOS LDO regulator with fast transient response | Y.-H. Lam and W.-H. Ki, | The LDO regulator has to be stable for all load conditions and frequency compensation is usually needed to stabilize the regulation loop.
Design of a low-voltage low dropout regulator | C.-H. Huang, Y.-T. Ma, and W.-C. Liao, | A simple symmetric operational transconductance amplifier is used as the error amplifier (EA), with a current splitting technique adopted to boost the gain.

## Slide 9: Block Diagram

## Slide 10: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 11: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 12: CONCLUSION
In this paper, a generic, single-stage voltage regulator circuit is proposed to cover a wide dynamic range with a good dc load regulation, similar to the multistage regulator architectures. The main advantage of the proposed single-stage topology over multistage topologies is that both the MFL and the ABL have single-pole behavior, and hence it is easy to stabilize for the with-capacitor (Co ≥ 1 μF) and capacitor-less (Co ≤ 3.3 nF) conditions. This makes it more suitable for generic application. The combination of the cross-coupled transistor pair and the adaptive biasing uniquely helps to achieve a well-controlled ABL for an improved load regulation over a wide range. At the same time, in the slewing mode of operation, it acts as a pull-up path which was missing in the conventional single-stage topologies. The experimental result shows that the proposed regulator is capable of delivering 100 mA of load current with a dc variation of 1.17% of the output voltage. The line regulation is 12.3 mV/V. The quiescent current consumption at the low load condition is as low as 400 nA while keeping a maximum current efficiency of 99.75% at high load condition. A resonably low FOM of the proposed topology at no-load condition is very attractive to use in battery-operated portable applications.

## Slide 13: REFERENCE
[1] P. Hazucha, T. Karnik, B. A. Bloechel, C. Parsons, D. Finan, and S. Borkar, “Area-efficient linear regulator with ultra-fast load regulation,” IEEE J. Solid-State Circuits, vol. 40, no. 4, pp. 933–940, Apr. 2005.
[2] J. Guo and K. N. Leung, “A 6-μW chip-area-efficient outputcapacitorless LDO in 90-nm CMOS technology,” IEEE J. Solid-State Circuits, vol. 45, no. 9, pp. 1896–1905, Sep. 2010.
[3] Y.-H. Lam and W.-H. Ki, “A 0.9 V 0.35 μm adaptively biased CMOS LDO regulator with fast transient response,” in IEEE Int. Solid-State Circuits Conf. Dig. Tech. Papers (ISSCC), Feb. 2008, pp. 442–626.
[4] C.-H. Huang, Y.-T. Ma, and W.-C. Liao, “Design of a low-voltage lowdropout regulator,” IEEE Trans. Very Large Scale Integr. (VLSI) Syst., vol. 22, no. 6, pp. 1308–1313, Jun. 2014.
[5] Y.-S. Yuk, S. Jung, C. Kim, H.-D. Gwon, S. Choi, and G.-H. Cho, “PSR enhancement through super gain boosting and differential feed-forward noise cancellation in a 65-nm CMOS LDO regulator,” IEEE Trans. Very Large Scale Integr. (VLSI) Syst., vol. 22, no. 10, pp. 2181–2191, Oct. 2014.

## Slide 14
[6] S. K. Lau, P. K. T. Mok, and K. N. Leung, “A low-dropout regulator for SoC with Q-reduction,” IEEE J. Solid-State Circuits, vol. 42, no. 3, pp. 658–664, Mar. 2007.
[7] C. Zhan and W.-H. Ki, “Output-capacitor-free adaptively biased lowdropout regulator for system-on-chips,” IEEE Trans. Circuits Syst. I, Reg. Papers, vol. 57, no. 5, pp. 1017–1028, May 2010.
[8] K. N. Leung, Y. Y. Mai, and P. K. T. Mok, “A chip-area efficient voltage regulator for VLSI systems,” IEEE Trans. Very Large Scale Integr. (VLSI) Syst., vol. 18, no. 12, pp. 1757–1762, Dec. 2010.
[9] C.-J. Park, M. Onabajo, and J. Silva-Martinez, “External capacitor-less low drop-out regulator with 25 dB superior power supply rejection in the 0.4–4 MHz range,” IEEE J. Solid-State Circuits, vol. 49, no. 2, pp. 486–501, Feb. 2014.
[10] S. S. Chong and P. K. Chan, “A sub-1 V transient-enhanced outputcapacitorless LDO regulator with push–pull composite power transistor,” IEEE Trans. Very Large Scale Integr. (VLSI) Syst., vol. 22, no. 11, pp. 2297–2306, Nov. 2014.