## Slide 1: Flexible DSP Accelerator Architecture Exploiting Carry-Save Arithmetic

## Slide 2: Abstract
Hardware acceleration has been proved an extremely promising implementation strategy for the digital signal processing (DSP) domain. Rather than adopting a monolithic application-specific integrated circuit design approach, in this brief, we present a novel accelerator architecture comprising flexible computational units that support the execution of a large set of operation templates found in DSP kernels. We differentiate from previous works on flexible accelerators by enabling computations to be aggressively performed with carry-save (CS) formatted data. Advanced arithmetic design concepts, i.e., recoding techniques, are utilized enabling CS optimizations to be performed in a larger scope than in previous approaches. Extensive experimental evaluations show that the proposed accelerator architecture delivers average gains of up to 61.91% in area-delay product and 54.43% in energy consumption compared with the state-of-art flexible datapaths.

## Slide 3: Existing System
Existing works on coarse-grained reconfigurable data paths mainly exploit architecture-level optimizations, e.g., increased instruction-level parallelism (ILP) .
The existing accelerator architecture comprises flexible computational units (FCUs), which enable the execution of a large set of operation templates found in DSP kernels.
The main constraint of existing DSP systems is its inflexibility. The main focus of my work is to implement reconfigurable DSP functions.
An astounding use methodology has been shown up by the hardware animating operator for the DSP space.

## Slide 4: Disadvantage of Existing System
Design decisions on the accelerator’s datapath highly impact its efficiency.
However, research activities have shown that the arithmetic optimizations at higher abstraction levels than the structural circuit one significantly impact on the datapath performance.
The aforementioned CS optimization approaches have limited impact on DFGs dominated by multiplications, e.g., filtering DSP applications.
This experimentation targets to show that the scaling impact on the performance does not eliminate the benefits of using CS arithmetic.

## Slide 5: PROPOSED SYSTEM :
The proposed accelerator architecture delivers average gains in area-delay product and in energy consumption compared to state-of-art flexible datapaths , sustaining efficiency toward scaled technologies.
There are many different types of fast adder like carry skip adder( CSK ), carry-select adder( CSL) and carry-look-ahead adder( CLA) has been developed and also there are many low-power adder design techniques that have been proposed.
The multiplier comprises a CS-to-MB module, which adopts a recently proposed technique to recode the 17-bit P ̽in its respective MB digits with minimal carry propagation.
The proposed multirate processor exploits the features of this flexible ALU.

## Slide 6: ADVANTAGE
Many researchers have proposed the use of domain-specific coarse-grained reconfigurable accelerators in order to increase ASICs’ flexibility without significantly compromising their performance.
However, research activities have shown that the arithmetic optimizations at higher abstraction levels than the structural circuit one significantly impact on the datapath performance.
A CS to binary conversion is inserted before each operation that differs from addition/subtraction, e.g., multiplication, thus, allocating multiple CS to binary conversions that heavily degrades performance due to time-consuming carry propagations.
Modern embedded systems target high-end application domains requiring efficient implementations of computationally intensive digital signal processing (DSP) functions.

## Slide 7
TITLE | AUTHOR | DESCRIPTION
A flexible and energy-efficient coarse-grained reconfigurable architecture for mobile systems | P. M. Heysters, G. J. M. Smit, and E. Molenkamp, | The focal point is the coarse-grained reconfigurable architecture of the Montium processing tile, which is designed to execute digital signal processing algorithms energy-efficiently.
ADRES: An architecture with tightly coupled VLIW processor and coarse-grained reconfigurable matrix | B. Mei, S. Vernalde, D. Verkest, H. D. Man, and R. Lauwereins, | To address this problem, we propose a novel architecture with tightly coupled very long instruction word (VLIW) processor and coarse-grained reconfigurable matrix.

## Slide 8
TITLE | AUTHOR | DESCRIPTION
A high-performance data path for synthesizing DSP kernels | M. D. Galanis, G. Theodoridis, S. Tragoudas, and C. E. Goutis, | Due to the universality and flexibility of the FCC, simple and efficient algorithms perform scheduling and binding of the data flow graph (DFG).
Automatic design of reconfigurable domain specific flexible cores | K. Compton and S. Hauck, | Reconfigurable hardware is ideal for use in systems-on-a-chip (SoC), as it provides both hardware-level performance and post-fabrication flexibility.

## Slide 9: Block Diagram

## Slide 10: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 11: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 12: CONCLUSION
In this brief, we introduced a flexible accelerator architecture that exploits the incorporation of CS arithmetic optimizations to enable fast chaining of additive and multiplicative operations. The proposed flexible accelerator architecture is able to operate on both conventional two’s complement and CS-formatted data operands, thus enabling high degrees of computational density to be achieved. Theoretical and experimental analyses have shown that the proposed solution forms an efficient design tradeoff point delivering optimized latency/area and energy implementations.

## Slide 13: REFERENCE
[1] P. Ienne and R. Leupers, Customizable Embedded Processors: Design Technologies and Applications. San Francisco, CA, USA: Morgan Kaufmann, 2007.
[2] P. M. Heysters, G. J. M. Smit, and E. Molenkamp, “A flexible and energy-efficient coarse-grained reconfigurable architecture for mobile systems,” J. Supercomput., vol. 26, no. 3, pp. 283–308, 2003.
[3] B. Mei, S. Vernalde, D. Verkest, H. D. Man, and R. Lauwereins, “ADRES: An architecture with tightly coupled VLIW processor and coarse-grained reconfigurable matrix,” in Proc. 13th Int. Conf. Field Program. Logic Appl., vol. 2778. 2003, pp. 61–70.
[4] M. D. Galanis, G. Theodoridis, S. Tragoudas, and C. E. Goutis, “A high-performance data path for synthesizing DSP kernels,” IEEE Trans. Comput.-Aided Design Integr. Circuits Syst., vol. 25, no. 6, pp. 1154–1162, Jun. 2006.
[5] K. Compton and S. Hauck, “Automatic design of reconfigurable domainspecific flexible cores,” IEEE Trans. Very Large Scale Integr. (VLSI) Syst., vol. 16, no. 5, pp. 493–503, May 2008.

## Slide 14
[6] S. Xydis, G. Economakos, and K. Pekmestzi, “Designing coarse-grain reconfigurable architectures by inlining flexibility into custom arithmetic data-paths,” Integr., VLSI J., vol. 42, no. 4, pp. 486–503, Sep. 2009.
[7] S. Xydis, G. Economakos, D. Soudris, and K. Pekmestzi, “High performance and area efficient flexible DSP datapath synthesis,” IEEE Trans. Very Large Scale Integr. (VLSI) Syst., vol. 19, no. 3, pp. 429–442, Mar. 2011.
[8] G. Ansaloni, P. Bonzini, and L. Pozzi, “EGRA: A coarse grained reconfigurable architectural template,” IEEE Trans. Very Large Scale Integr. (VLSI) Syst., vol. 19, no. 6, pp. 1062–1074, Jun. 2011.
[9] M. Stojilovic, D. Novo, L. Saranovac, P. Brisk, and P. Ienne, “Selective flexibility: Creating domain-specific reconfigurable arrays,” IEEE Trans. Comput.-Aided Design Integr. Circuits Syst., vol. 32, no. 5, pp. 681–694, May 2013.
[10] R. Kastner, A. Kaplan, S. O. Memik, and E. Bozorgzadeh, “Instruction generation for hybrid reconfigurable systems,” ACM Trans. Design Autom. Electron. Syst., vol. 7, no. 4, pp. 605–627, Oct. 2002.