## Slide 1: A 65-nm CMOS Constant Current Source With Reduced PVT Variation

## Slide 2: Abstract
This paper presents a new nanometer-based low-power constant current reference that attains a small value in the total process–voltage–temperature variation. The circuit architecture is based on the embodiment of a process-tolerant bias current circuit and a scaled process-tracking bias voltage source for the dedicated temperature-compensated voltageto-current conversion in a preregulator loop. Fabricated in a UMC 65-nm CMOS process, it consumes 7.18 µW with a 1.4 V supply. The measured results indicate that the current reference achieves an average temperature coefficient of 119 ppm/°C over 12 samples in a temperature range from −30 °C to 90 °C without any calibration. Besides, a low line sensitivity of 180 ppm/V is obtained. This paper offers a better sensitivity figure of merit with respect to the reported representative counterparts.

## Slide 3: Existing System
There exists another challenge from the non-ideal CMOS stress effect that causes the performance degradation in the PVT-aware circuits.
The coexistence of the DC/DC and LDO regulators helps to achieve low-noise power supply whilst maintaining high power efficiency.
Although a good solution for the threshold voltage reference is reported using the weak inversion transistors and linear resistors other than the bipolar transistors, the T.C. is limited by the nonlinear temperature effect existing in VGS(T).
The increasing demand on the LDO regulators for the portable devices gives rise to one of the motivations on the design of performance-aware LDO regulators.

## Slide 4: Disadvantage of Existing System
These problems have increased the motivation for the design of a low-power constant current reference with reduced PVT variation in the context of aggressively scaled nanometer technology.
The VTH mismatch issue between the tracking device pair will degrade the current accuracy.
This is in contrast with the designs from, which suffer from the offset issues induced by the op-amp. In view of D2D variation, the obtained process sensitivity is 5% because it comes from the combined accuracy of the compensation voltage and the sense resistor.
Turning to the power consumption issue, it is often regarded as the performance tradeoff parameter.

## Slide 5: PROPOSED SYSTEM :
The proposed reference voltage by the BGR circuit can also be minimized to the diode voltage level if the supply voltage is reduced to the same level.
The proposed design achieves a low chip area, a higher temperature range and reasonable TC and PSRR.
The proposed circuit with pre-regulator will increase the immunity against the supply variation from dc to high frequencies.
A low T.C. current reference with PVT insensitivity and wide temperature range in 65-nm CMOS technology is proposed.
Those designs, that deal with the first-order temperature effect from the on-chip resistors, the proposed circuit takes into account the second-order temperature effect.

## Slide 6: ADVANTAGE
The thermal drift over the temperature range is quite small and within 5 nA, demonstrating that the proposed temperature compensation method permits a low T.C. performance metric.
This paper achieves the best performance in terms of line sensitivity in comparison with the other works except for, in which it benefits from a high supply voltage architecture.
In particular, it has a lower power consumption except for, which focus on a very low-power circuit design at the expense of a higher T.C. performance metric.
This paper can offer good FOM values while providing a good balance in the performance metrics like low power consumption and reduced PVT variation.

## Slide 7
TITLE | AUTHOR | DESCRIPTION
A CMOS temperature compensated current reference | W. M. Sansen, F. Op’t Eynde, and M. Steyaert, | A temperature-compensated current reference for CMOS integrated circuits based on a MOSFET as current-defining element, is described.
CMOS current reference without resistance | H. J. Oguey and D. Aebischer, | A micropower current reference in the range of 1 to 100 nA is built with CMOS transistors only, featuring low sensitivity with respect to technology and temperature.

## Slide 8
TITLE | AUTHOR | DESCRIPTION
A 2-nW 1.1-V self-biased current reference in CMOS technology | E. M. Camacho-Galeano, C. Galup-Montoro, and M. C. Schneider, | We propose the use of a very simple topology along with a design methodology based on the concept of inversion level.
A new compact temperature-compensated CMOS current reference | F. Fiori and P. S. Crovetti, | The operation principle of the new circuits is described and the relationships between design and technology process parameters are derived.

## Slide 9: Block Diagram

## Slide 10: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 11: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 12: CONCLUSION
A low-power constant current reference in the 65-nm CMOS is proposed. By matching the temperature characteristic of the dedicated reference compensation voltage with that of the output sense resistor in the op-amp-less VI converter, a constant current reference with lower T.C. over the operating temperature range and relatively lower sensitivity to the total PVT are achieved. With the embedded preregulator, the current reference gives good line sensitivity. The current reference offers one of the lowest values of the sensitivity FOM with respect to reported counterparts.

## Slide 13: REFERENCE
[1] C.-H. Lee and H.-J. Park, “All-CMOS temperature independent current reference,” Electron. Lett., vol. 32, no. 14, pp. 1280–1281, Jul. 1996.
[2] W. M. Sansen, F. Op’t Eynde, and M. Steyaert, “A CMOS temperature compensated current reference,” IEEE J. Solid-State Circuits, vol. 23, no. 3, pp. 821–824, Jun. 1988.
[3] H. J. Oguey and D. Aebischer, “CMOS current reference without resistance,” IEEE J. Solid-State Circuits, vol. 32, no. 7, pp. 1132–1135, Jul. 1997.
[4] E. M. Camacho-Galeano, C. Galup-Montoro, and M. C. Schneider, “A 2-nW 1.1-V self-biased current reference in CMOS technology,” IEEE Trans. Circuits Syst. II, Express Briefs, vol. 52, no. 2, pp. 61–65, Feb. 2005.
[5] F. Fiori and P. S. Crovetti, “A new compact temperature-compensated CMOS current reference,” IEEE Trans. Circuits Syst. II, Express Briefs, vol. 52, no. 11, pp. 724–728, Nov. 2005.

## Slide 14
[6] A. Bendali and Y. Audet, “A 1-V CMOS current reference with temperature and process compensation,” IEEE Trans. Circuits Syst. I, Reg. Papers, vol. 54, no. 7, pp. 1424–1429, Jul. 2007.
[7] K. Ueno et al., “A 46-ppm/°C temperature and process compensated current reference with on-chip threshold voltage monitoring circuit,” in Proc. IEEE Asian Solid-S tate Circuits Conf., Nov. 2008, pp. 161–164.
[8] K. Ueno, T. Hirose, T. Asai, and Y. Amemiya, “A 1-μW 600-ppm/°C current reference circuit consisting of subthreshold CMOS circuits,” IEEE Trans. Circuits Syst. II Express Briefs, vol. 57, no. 9, pp. 681–685, Sep. 2010.
[9] H. Kayahan, O. Ceylan, M. Yazici, S. Zihir, and Y. Gurbuz, “Wide range, process and temperature compensated voltage controlled current source,” IEEE Trans. Circuits Syst. I, Reg. Papers, vol. 60, no. 5, pp. 1345–1353, May 2013.
[10] C. Yoo and J. Park, “CMOS current reference with supply and temperature compensation,” Electron. Lett., vol. 43, no. 25, pp. 1422–1424, Dec. 2007.