## Slide 1: Implementation of Sub-threshold Adiabatic Logic for Ultralow-Power Application

## Slide 2: Abstract
Behavior of adiabatic logic circuits in weak inversion or subthreshold regime is analyzed in depth for the first time in the literature to make great improvement in ultralowpower circuit design. This novel approach is efficacious in low-speed operations where power consumption and longevity are the pivotal concerns instead of performance. The schematic and layout of a 4-bit carry look ahead adder (CLA) has been implemented to show the workability of the proposed logic. The effect of temperature and process parameter variations on subthreshold adiabatic logic-based 4-bit CLA has also been addressed separately. Postlayout simulations show that subthreshold adiabatic units can save significant energy compared with a logically equivalent static CMOS implementation. Results are validated through extensive simulations in 22-nm CMOS technology using CADENCE SPICE Spectra.

## Slide 3: Existing System
A CMOS transistor (or device) has four terminals: gate, source, drain, and a fourth terminal that we shall ignore until the next section. A CMOS transistor is a switch.
The switch must be conducting or on to allow current to flow between the source and drain terminals (using open and closed for switches is confusing-for the same reason we say a tap is on and not that it is closed).
The transistor source and drain terminals are equivalent as far as digital signals are concernedwe do not worry about labeling an electrical switch with two terminals.
Multiplier is an important building block in applications such as digital signal processing, communication systems and arithmetic logic units.

## Slide 4: Disadvantage of Existing System
The design of SAL requires a deep knowledge of the main features of the adopted logic style, such as power dissipation, leakage current, impact of temperature variation, operating frequency, and noise immunity.
In particular, the impact of temperature variation on leakage dissipation, output swing, etc., has been discussed thoroughly in this paper.
Complex architecture and clock synchronization are the major drawbacks of full adiabatic logic circuits. Threshold voltage of the transistors in sub-threshold based digital circuits is higher than the supply voltage.

## Slide 5: PROPOSED SYSTEM :
In adiabatic logic circuits, ramp type supply voltage is used to slow down the charge transport mechanism. Hence, the supply clock plays the pivotal role.
A ramp type supply voltage φ(t) is considered, which gradually swings in between logic 0 (Gnd potential) and logic 1 (VDD) in time duration 2T, where f (=1/2T ) is the supply clock’s frequency.
The power supply waveform φ(t) can be divided into charging phase, when φ(t) ramps up from 0 to VDD in 0 to T unit time and discharging phase when φ(t) ramps down from VDD to 0 in T to 2T unit time.
The proposed adiabatic logic circuit is advantageous for the design of ultralow-power digital circuits.

## Slide 6: ADVANTAGE
These emerging applications have low energy as the primary concern instead of performance, with the eventual goal of harvesting energy from the environment.
The performance requirements are quite relaxed in many of these energy efficient subthreshold applications, we believe that the adiabatic style can be used efficaciously in a subthreshold regime to make the circuit more energy efficient.
As SAL is efficacious where instead of performance, power dissipation is major concern. For example, in implanted biomedical systems, the circuits remain active for a very small span of time and remain idle for most of the time.
Therefore, the SAL-based CLA is also area efficient in comparison with the conventional structure.

## Slide 7
TITLE | AUTHOR | DESCRIPTION
A 65 nm sub-Vt microcontroller with integrated SRAM and switched capacitor DC-DC converter | J. Kwong, Y. K. Ramadass, N. Verma, and A. P. Chandrakasan, | Aggressive supply voltage scaling to below the device threshold voltage provides significant energy and leakage power reduction in logic and SRAM circuits.
A 0.25 V 460 nW asynchronous neural signal processor with inherent leakage suppression | T.-T. Liu and J. M. Rabaey, | In this paper, we present a robust and energy-efficient computation architecture exploiting an asynchronous timing strategy to dynamically minimize leakage and to self-adapt to process variations and different operating conditions.

## Slide 8
TITLE | AUTHOR | DESCRIPTION
Design techniques and architectures for low-leakage SRAMs | A. Calimera, A. Macii, E. Macii, and M. Poncino, | In high performance Systems-on-Chip, leakage power consumption has become comparable to the dynamic component, and its relevance increases as technology scales.
Robust subthreshold logic for ultra-low power operation | H. Soeleman, K. Roy, and B. C. Paul, | Digital subthreshold logic circuits can be used for applications in the ultra-low power end of the design spectrum, where performance is of secondary importance.

## Slide 9: Block Diagram

## Slide 10: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 11: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 12: CONCLUSION
SAL has been presented in this paper for the first time in the literature to advance the ultralow power research. A closedform expression of the energy dissipation has been derived, from which insight is gained into the dependence of energy dissipation on design and process parameters. SAL saves considerable energy compared with the static conventional logic counterpart over a wide range of frequency. In particular, the impact of temperature variation on leakage dissipation, output swing, etc., has been discussed thoroughly in this paper. Hence, the predicted values of optimum frequency and optimum supply voltage almost match the simulated ones. Postlayout simulations using CADENCE SPICE Spectra and the comparison with the static counterpart explain the workability of SAL. This proposed logic scheme can be used in future energy-saving embedded circuits and mainly for energyefficient devices where ultralow power and longevity are the pivotal issues.

## Slide 13: REFERENCE
[1] J. Kwong, Y. K. Ramadass, N. Verma, and A. P. Chandrakasan, “A 65 nm sub-Vt microcontroller with integrated SRAM and switched capacitor DC-DC converter,” IEEE J. Solid-State Circuits, vol. 44, no. 1, pp. 115–126, Jan. 2009.
[2] T.-T. Liu and J. M. Rabaey, “A 0.25 V 460 nW asynchronous neural signal processor with inherent leakage suppression,” IEEE J. Solid-State Circuits, vol. 48, no. 4, pp. 897–906, Apr. 2013.
[3] A. Calimera, A. Macii, E. Macii, and M. Poncino, “Design techniques and architectures for low-leakage SRAMs,” IEEE Trans. Circuits Syst. I, Reg. Papers, vol. 59, no. 9, pp. 1992–2007, Sep. 2012.
[4] H. Soeleman, K. Roy, and B. C. Paul, “Robust subthreshold logic for ultra-low power operation,” IEEE Trans. Very Large Scale Integr. (VLSI) Syst., vol. 9, no. 1, pp. 90–99, Feb. 2001.
[5] C.-S. A. Gong, M.-T. Shiue, C.-T. Hong, and K.-W. Yao, “Analysis and design of an efficient irreversible energy recovery logic in 0.18-μm CMOS,” IEEE Trans. Circuits Syst. I, Reg. Papers, vol. 55, no. 9, pp. 2595–2607, Oct. 2008.

## Slide 14
[6] D. Maksimovic, V. G. Oklobdzija, B. Nikolic, and K. W. Current, “Clocked CMOS adiabatic logic with integrated single-phase powerclock supply,” IEEE Trans. Very Large Scale Integr. (VLSI) Syst., vol. 8, no. 4, pp. 460–463, Aug. 2000.
[7] V. S. Sathe, J.-Y. Chueh, and M. C. Papaefthymiou, “Energy-efficient GHz-class charge-recovery logic,” IEEE J. Solid-State Circuits, vol. 42, no. 1, pp. 38–47, Jan. 2007.
[8] N. S. S. Reddy, M. Satyam, and K. L. Kishore, “Cascadable adiabatic logic circuits for low-power applications,” IET Circuits, Devices Syst., vol. 2, no. 6, pp. 518–526, Dec. 2008.
[9] Y. Tsividis, Operation and Modeling of the Transistor MOS, 2nd ed. Oxford, U.K.: Oxford Univ. Press, 2003.
[10] X. Xi et al., “BSIM4.3.0 MOSFET Model,” Dept. Elect. Eng. Comput. Sci., Univ. California, Berkeley, CA, Tech. Rep. 94720, 2003.