## Slide 1: CMOS TRANS-CONDUCTANCE LNA INTEGRATION OF VITAL SIGN PROCESSING RECIEVER WITH CLUTTER ELIMINATION USING SC CHEBYSHEV LPF

## Slide 2: Abstract
This brief describes a critical signal processing circuit without any automatic signal processing or ultra-wideband (UWB) pulse-based radar algorithm for simultaneous dc/near-dc exclusion and out-of-band interference removal. As a secure and balanced pseudo resistor applied under a servo feedback mechanism in a critical signal receiver of the sensing radar, it was proposed that an inherent self-balancing MOS diode (SBMD) operate as a High-Pass Filter (HPF) with an ultra-low corner frequency below 0.5 Hz to suppress undesired clutters of reflected signals and input dc-offset voltages from underlying circuit offsets. A third-order switched-capacitor (SC) Chebyshev low-pass Filter (LPF) with trans-conductance low-noise amplifier (LNA) and leap-frog topology was embraced as the next step to remove out-band noise, create an integrated band-pass response vital-sign transmission circuit and incorporate it into a radar module to verify its viability. This study was finally established at 130 nm and 45 nm CMOS Technology in Tanner EDA.

## Slide 3: Existing System
The CW radars suffer from the null detection problem that exists at every multiple of a quarter free-space wavelength distance.
In this paper, we propose a single channel receiver topology to eliminate the null points using the path-diversity transmission.
The conventional FFT method and the proposed feature extraction method for two separation distances between two targets to evaluate the performance of the proposed algorithm for the vital sign detection of multiple targets: one closer than the theoretical range resolution and the other greater.
It is a very simpler scheme devised for data loss and has been employed in numerous application.

## Slide 4: PROPOSED SYSTEM :
Phase noise analysis shows that the proposed radar has the advantages of both phase-locked oscillators and self-injection-locked oscillators to achieve high power spectral signal-to-noise ratio.
A Doppler radar using a self-injection-locked (SIL) oscillator has been proposed to achieve a high SNR gain in the vital-signal bandwidth.
Single channel receivers using the dynamic phase variation technique have been proposed to find the optimal detection point with complicated algorithm.
The present study proposes a novel vital-sign sensing algorithm for clear target identification and accurate vital sign estimation using a single 24 GHz FMCW Doppler radar based on FCC regulation.

## Slide 5: Block Diagram

## Slide 6: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 7: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 8: CONCLUSION
This brief proposed an alternative way to reject the clutter signals of the vital-sign radar. A vital-sign processing receiver with a servo feedback loop was developed to perform a high-pass response. An intrinsic SBMD structure was further applied at the servo feedback path to realize a high-pass corner close to dc for suppressing the in-band dc offset. Meanwhile, the third-order SC Chebyshev LPF with variable bandwidth was also used to remove the outband interferences. Consequently, instead of using extra digital signal processing, the radar featured the dc/near-dc rejection in the analog vital-sign receiver, which automatically performed clutter signals’ reduction. To demonstrate the concept and its feasibility, a pulsebased radar with a clutter elimination circuit for short-range detection was designed, measured, and analyzed.

## Slide 9: REFERENCE
[1] B.-K. Park, O. Boric-Lubecke, and V. M. Lubecke, “Arctangent demodulation with DC offset compensation in quadrature Doppler radar receiver systems,” IEEE Trans. Microw. Theory Techn., vol. 55, no. 5, pp. 1073–1079, May 2007.
[2] H.-C. Kuo et al., “A fully integrated 60-GHz CMOS direct-conversion Doppler radar RF sensor with clutter canceller for single-antenna noncontact human vital-signs detection,” IEEE Trans. Microw. Theory Techn., vol. 64, no. 4, pp. 1018–1028, Apr. 2016.
[3] P.-H. Wu et al., “Phase–and self-injection-locked radar for detecting vital signs with efficient elimination of DC offsets and null points,” IEEE Trans. Microw. Theory Techn., vol. 61, no. 1, pp. 685–695, Jan. 2013.
[4] Z.-P. Yang and Y.-C. Chiang, “Vital signal radar with adaptive compensation circuits to effectively eliminate DC offsets,” IEEE Microw. Wireless Compon. Lett., vol. 28, no. 1, pp. 88–90, Jan. 2018.
[5] P.-I. Mak, S.-P.U, and R.P. Martins, “On the design of a programmable gain amplifier with built-In compact DC-Offset cancellers for very low voltage WLAN systems,” IEEE Trans. Circuits Syst. I, Reg. Papers, vol. 55, no. 2, pp. 496–509, Mar. 2008.

## Slide 10
[6] A. M. Sodagar, G. E. Perlin, Y. Yao, K. Najafi, and K. D. Wise, “An implantable 64-channel wireless microsystem for single-unit neural recording,” IEEE J. Solid-State Circuits, vol. 44, no. 9, pp. 2591–2604, Sep. 2009.
[7] R. R. Harrison and C. Charles, “A low-power low-noise CMOS amplifier for neural recording applications,” IEEE J. Solid-State Circuits, vol. 38, no. 6, pp. 958–965, Jun. 2003.
[8] R. Puddu et al., “A precision Pseudo Resistor bias scheme for the design of very large time constant filters,” IEEE Trans. Circuits Syst. II, Exp. Briefs, vol. 64, no. 7, pp. 762–766, Jul. 2017.
[9] W.-P. Hung, C.-H. Chang, and T.-H. Lee, “Real-time and noncontact impulse radio radar system for μm movement accuracy and vital-sign monitoring applications,” IEEE Sensors J., vol. 17, no. 8, pp. 2349–2358, Apr. 2017.
[10] D. Zito et al., “SoC CMOS UWB pulse radar sensor for contactless respiratory rate monitoring,” IEEE Trans. Biomed. Circuits Syst., vol. 5, no. 6, pp. 503–511, Dec. 2010.