## Slide 1: Design and application of a self-powered dual-stage circuit for piezoelectric energy harvesting system

## Slide 2: Abstract
This paper describes the design and practical application of a dual-stage H-Bridge (DSHBR) circuit to reduce the rectification losses and mitigate ripples in piezoelectric energy harvesting.
The proposed DSHBR circuit integrates both AC-DC and DC-DC conversion processes using bidirectional switches and a step-up DC-DC converter, which applies to both positive and negative half cycles.
One additional feature is that it does not require external power to turn on the bidirectional switches (Vth < 0.3 V). Such feature facilitates active rectification at very low AC voltages (Vac < 0.5) generated by the piezoelectric device (PD).

## Slide 3
To validate the performance of the proposed circuit, a series of experimental tests were conducted. Firstly, the performance of circuit on rectifying the PD output was investigated using a shaker to generate high and low frequency excitations.
Next, real-life testing was conducted with human arm motion as the source of excitation. Then, the ability of the entire system to charge solar batteries was investigated.
The outcome shows that the DSHBR circuit prominently increased the rectified voltage and the output power while stabilising the DC voltage when compared with the conventional H-Bridge circuit.

## Slide 4: Existing System
One of the most widely used power harvesting techniques for micro-power applications uses piezoelectric materials to convert any type of energy to electrical energy.
The process of extracting unused energy from the ambient environment and converting it into a usable form of electrical energy is known as Energy Harvesting.
Piezoelectric materials can be used as a means of transforming ambient vibrations into electrical energy that can be stored and used to power other devices.

## Slide 5: Disadvantage of Existing System
The technique uses a mechanical stopper to broaden the operating frequency range by changing the damping and the stiffness of the system at impact.
The design is simple, but it has energy losses due to mechanical impact and risks of mechanical impact fatigue.
Some of the disadvantages associated with piezoelectric ceramics are: rigidity, brittleness, high density, lower voltage coefficient, physical limitation in producing small-sized piezoelectric ceramics, and lack of design flexibility.

## Slide 6: PROPOSED SYSTEM :
In this paper, a modified circuit and an improved analysis for the self powered SSHI (SP-SSHI) are proposed.
The essence of the SP-SSHI technique proposed is the electronic breaker.
Different energy harvesting techniques have been investigated for the purpose to broaden the energy sources, alleviate the dependence on batteries, and hopefully someday make all WSN devices self-powered.

## Slide 7: ADVANTAGE
In their study, the performance of PD and single stage conditioning circuit has been analysed.
The magnitude of extracted output power is a useful indicator of the performance of the proposed DSHBR circuit.
An improvement in output power and efficiency was augmented in comparison with the FBR circuit.
It includes a synchronous rectification process, which eliminates the need of diodes, minimises the size of the circuit and improves the overall efficiency.

## Slide 8
TITLE | AUTHOR | DESCRIPTION
High-temperature, point-focus, pressurised gas-phase solar receivers: A comprehensive | M. Sedighi, R. V. Padilla, R. A. Taylor, M. Lake, I. Izadgoshasb, and A. Rose, | The ideal gas-phase receiver would provide high thermal efficiency and high HTF outlet temperature with low pressure drop and low capital cost.
A study of low level vibrations as a power source for wireless sensor nodes | S. Roundy, P. K. Wright, and J. Rabaey, | Low-level vibrations occurring in common household and office environments as a potential power source are studied in depth.

## Slide 9
TITLE | AUTHOR | DESCRIPTION
A review on piezoelectric energy harvester and its power conditioning circuit | N. A. A. Nawir, A. A. Basari, M. S. M. Saat, N. X. Yan, and S. Hashimoto, | This paper presents the recent concern on the power requirements of Wireless Sensor Nodes and the studies on the development of energy harvesting system using piezoelectric devices.
A novel self-power SSHI circuit for piezoelectric energy harvester | A. M. Eltamaly and K. E. Addoweesh, | A parallel SSHI technique has been used to flip the terminal voltage of the PEH through external inductor.

## Slide 10: Block Diagram

## Slide 11: SOFTWARE REQUIREMENTS:
Language: Java J2SE and JDK DE, Eclipse MARS.1
Operating System: Windows 10
Database required: MySQL
Apache Tomcat Server
Arduino 16.9

## Slide 12: HARDWARE REQUIREMENTS:
Node MCU
4 GB RAM
500 GB Hard disk
GPS receiver
Jumper Wires
GPS antenna
Accelerometer

## Slide 13: CONCLUSION
In this study, a DSHBR circuit for rectifying voltage and power from PEH system under high and low frequencies of vibrations and human motion-induced excitation was designed and investigated.
By assimilating the advantage of MOSFETs, which has low threshold voltage in Stage – 1, and DC-DC converter, which stabilises the rectified voltage in Stage – 2, the DSHBR circuit successfully produced higher rectified voltage with fewer ripples and higher output power when compared with the regular H-Bridge circuit.

## Slide 14
In addition, the voltage rectified through the proposed circuit as a result of low frequency PEH was found to be able to charge a solar battery, demonstrating the practical application of the circuit.
In the HMIV test involving arm movement, the proposed circuit delivered 3.4 Vdc of rectified voltage and 115.6 µW of output power from PVDF, while in the SIV tests, 8.8 Vdc and 84.2 µW of rectified voltage and output power was achieved.
For future work, modification of the DSHBR circuit to incorporate the non-linear process is recommended.

## Slide 15: REFERENCE
[1] M. Sedighi, R. V. Padilla, R. A. Taylor, M. Lake, I. Izadgoshasb, and A. Rose, ‘‘High-temperature, point-focus, pressurised gas-phase solar receivers: A comprehensive,’’ Energy Convers. Managemen, vol. 185, pp. 678–717, Apr. 2019.
[2] S. Roundy, P. K. Wright, and J. Rabaey, ‘‘A study of low level vibrations as a power source for wireless sensor nodes,’’ Comput. Commun., vol. 26, no. 11, pp. 1131–1144, Jul. 2003.
[3] N. A. A. Nawir, A. A. Basari, M. S. M. Saat, N. X. Yan, and S. Hashimoto, ‘‘A review on piezoelectric energy harvester and its power conditioning circuit,’’ ARPN J., 2018.

## Slide 16
[4] I. Izadgoshasb, Y. Y. Lim, L. Tang, R. V. Padilla, Z. S. Tang, and M. Sedighi, ‘‘Improving efficiency of piezoelectric based energy harvesting from human motions using double pendulum system,’’ Energy Convers. Manage., vol. 184, pp. 559–570, Mar. 2019.
[5] Y. Y. Lim, S. T. Smith, R. V. Padilla, and C. K. Soh, ‘‘Monitoring of concrete curing using the electromechanical impedance technique: Review and path forward,’’ Struct. Health Monitor., vol. 20, no. 2, pp. 604–636, Mar. 2021.
[6] Y. Y. Lim, S. T. Smith, and C. K. Soh, ‘‘Wave propagation based monitoring of concrete curing using piezoelectric materials: Review and path forward,’’ NDT E Int., vol. 99, pp. 50–63, Oct. 2018.

## Slide 17
[7] A. M. Eltamaly and K. E. Addoweesh, ‘‘A novel self-power SSHI circuit for piezoelectric energy harvester,’’ IEEE Trans. Power Electron., vol. 32, no. 10, pp. 7663–7673, Oct. 2017.
[8] A. Rahman, O. Farrok, M. R. Islam, and W. Xu, ‘‘Recent progress in electrical generators for oceanic wave energy conversion,’’ IEEE Access, vol. 8, pp. 138595–138615, 2020.
[9] A. S. Sadangi, S. K. Sahu, and K. Patra, ‘‘Comparison of circuits for dielectric elastomer based energy harvesting,’’ in Proc. 2nd Int. Conf. Inventive Syst. Control (ICISC), Jan. 2018, pp. 413–417.

## Slide 18
[10] M. Sedighi, R. V. Padilla, P. Alamdari, M. Lake, A. Rose, I. Izadgoshasb, and R. A. Taylor, ‘‘A novel high-temperature (>700 ◦C), volumetric receiver with a packed bed of transparent and absorbing spheres,’’ Appl. Energy, vol. 264, Apr. 2020, Art. no. 114705.