## Slide 1: Performance Analysis and Optimal Cooperative Cluster Size for Randomly Distributed Small Cells Under Cloud RAN

## Slide 2: Abstract
One major advantage of cloud/centralized radio access network is the ease of implementation of multi-cell coordination mechanisms to improve the system spectrum efficiency (SE).
Theoretically, large number of cooperative cells lead to a higher SE; however, it may also cause significant delay due to extra channel state information feedback and joint processing computational needs at the cloud data center, which is likely to result in performance degradation.

## Slide 3
In order to investigate the delay impact on the throughput gains, we divide the network into multiple clusters of cooperative small cells and formulate a throughput optimization problem.
We model various delay factors and the sum-rate of the network as a function of cluster size, treating it as the main optimization variable.
For our analysis, we consider both base stations’ as well as users’ geometric locations as random variables for both linear and planar network deployments.

## Slide 4
The output signal-to-interference-plus-noise ratio and ergodic sum-rate are derived based on the homogenous Poisson point processing model.
The sum-rate optimization problem in terms of the cluster size is formulated and solved. Simulation results show that the proposed analytical framework can be utilized to accurately evaluate the performance of practical cloud-based small cell networks employing clustered cooperation.

## Slide 5: Existing System
These challenges, new and existing technologies need to coexist and cooperate in order for the emerging networks to fulfill the users’ needs for high Quality of Experience (QoE).
Moreover, another factor that contributed to this throughput reduction is the intrabeam interference which increases for the previously existing UEs in the NOMA clusters when new edge users are added to them.
The existence of singleton coalitions in the game JT-CoMP case, when the conditions of the proposed coalition formation algorithm are not satisfied, resulted in a small percentage of users having the same average throughput as in the case of no JT-CoMP.

## Slide 6: Disadvantage of Existing System
All of the parameters are converted into a function of cluster size to formulate the optimization problem.
The geographic area of a network is considered to be divided into separate clusters and an optimization problem is formulated by expressing ergodic sum-rate in terms of the cooperative cluster size.
To investigate the proposed clustering optimization problem with ZF and MRT precoding algorithms for linear and planar dense small cell deployments.

## Slide 7: PROPOSED SYSTEM :
One of the relatively recently proposed concepts, aiming to fulfill the needs of mobile users in 5G networks, is the Non Orthogonal Multiple Access (NOMA) technique.
In, base station coordination with dirty paper coding was initially proposed with single-antenna transmitters and receivers in each cell.
The schemes proposed therein include a dirty paper coding approach with perfect data and power cooperation among base stations with a pooled power constraint and several sub-optimal joint transmission schemes with per-base power constraints.

## Slide 8: ADVANTAGE
We conjecture that there must be an optimal cluster size, large enough to mitigate interference into a reasonable level yet small enough to save the performance loss due to the delay-caused channel mismatch.
There must be an optimal cluster size to trade off delay and interference for maximizing system performance.
The SINR expression in is very difficult to analyze theoretically since it is a compound function of multiple variables including large-scale and fast fading of the channels, delay and precoding coefficients as well as multiple random deployed RRHs and users.

## Slide 9
TITLE | AUTHOR | DESCRIPTION
Quantitative analysis of split base station processing and determination of advantageous architectures for LTE | U. Dötsch, M. Doll, H.-P. Mayer, F. Schaich, J. Segel, and P. Sehier, | To mitigate that deficiency without sacrificing the benefits of centralized processing, we identified alternative interfacing options between central and remote units.
Benefits and impact of cloud computing on 5G signal processing: Flexible centralization through cloud-RAN | D. Wubben et al., | In this article, we will explore the benefits that cloud computing offers for fifth-generation (5G) mobile networks and investigate the implications on the signal processing algorithms.

## Slide 10
TITLE | AUTHOR | DESCRIPTION
Cloud technologies for flexible 5G radio access networks | P. Rost et al., | The evolution toward 5G mobile networks will be characterized by an increasing number of wireless devices, increasing device and service complexity, and the requirement to access mobile services ubiquitously.
Performance evaluation of cloudran system with carrier frequency offset | J. Li, D. Chen, Y. Wang, and J. Wu, | When inter-TP CFO does not exceed ±3~5ppb, CRAN can still achieve remarkable performance gain on both capacity and coverage even in nonideal channel.

## Slide 11: Block Diagram

## Slide 12: SOFTWARE REQUIREMENTS:
Operating System : Windows 10
Platform : DOT NET TECHNOLOGY
Front End : ASP.Net 4.0
Back End : SQL SERVER 2014

## Slide 13: HARDWARE REQUIREMENTS:
Keyboard
Mouse
Hard disk 500GB
Ram 4 Gb

## Slide 14: CONCLUSION
Based on commonly used linear precoding algorithms (ZF and MRT) and linear and planar small cell deployment configurations, the paper proposed an approach for cluster size optimization in cloud-based distributed cooperative small cell networks in the presence of CSI latency, which is mainly caused by cloud processing delay and CSI feedback delay.
An optimization problem is formulated in the aforementioned framework and desired signal and interference signal are calculated, which is followed by derivation of the output SINR by taking into consideration the channel mismatch caused by latency due to small cells cooperation.

## Slide 15
Both delay and output SINR have been derived as a function of cooperation cluster size and an optimization problem to trade off the interference and channel mismatch has been formulated for maximizing network sum-rate.
Simulations reveal a small gap with the analytical results in terms of SINR and sum-rate evaluations, and the proposed concise analytical framework can be safely used in order identify the optimal cluster size for any specific deployment

## Slide 16: REFERENCE
[1] U. Dötsch, M. Doll, H.-P. Mayer, F. Schaich, J. Segel, and P. Sehier, ‘‘Quantitative analysis of split base station processing and determination of advantageous architectures for LTE,’’ Bell Labs Tech. J., vol. 18, no. 1, pp. 105–128, Jun. 2013.
[2] D. Wubben et al., ‘‘Benefits and impact of cloud computing on 5G signal processing: Flexible centralization through cloud-RAN,’’ IEEE Signal Process. Mag., vol. 31, no. 6, pp. 35–44, Nov. 2014.
[3] P. Rost et al., ‘‘Cloud technologies for flexible 5G radio access networks,’’ IEEE Commun. Mag., vol. 52, no. 5, pp. 68–76, May 2014.

## Slide 17
[4] R. Irmer et al., ‘‘Coordinated multipoint: Concepts, performance, and field trial results,’’ IEEE Commun. Mag., vol. 49, no. 2, pp. 102–111, Feb. 2011.
[5] L. Li, J. Liu, K. Xiong, and P. Butovitsch, ‘‘Field test of uplink CoMP joint processing with C-RAN testbed,’’ in Proc. IEEE Commun. Netw. China (CHINACOM), Aug. 2012, pp. 753–757.
[6] J. Li, D. Chen, Y. Wang, and J. Wu, ‘‘Performance evaluation of cloudran system with carrier frequency offset,’’ in Proc. IEEE Globecom Workshops (GC Wkshps), Dec. 2012, pp. 222–226.

## Slide 18
[7] Small Cell Enhancements for E-UTRA and E-UTRAN—Physical Layer Aspects, document TR 36.872, 3GPP, Sep. 2013.
[8] Small Cell Enhancements for E-UTRA and E-UTRAN—Higher Layer Aspects, document TR 36.842, 3GPP, May 2013.
[9] J.-J. van de Beek, O. Edfors, M. Sandell, S. K. Wilson, and P. O. Borjesson, ‘‘On channel estimation in OFDM systems,’’ in Proc. IEEE 45th Veh. Technol. Conf., vol. 2. Jul. 1995, pp. 815–819.
[10] S. Colieri, M. Ergen, A. Puri, and A. Bahai, ‘‘A study of channel estimation in OFDM systems,’’ in Proc. IEEE 56th Veh. Technol. Conf. Fall, Sep. 2002, pp. 894–898.